## Slide 2: Why Choose a Desktop NAS over a Rackmount One
Internal use in a department
No server room in the company
NAS has outdoor needs

## Slide 3: Smart Investment: Expand when Necessary
When purchasing a business entry level NAS, you should not only consider current requirements, but also reserve the expandability to future-proof your investment
Storage Expansion
Network Expansion
Performance Expansion
10GbE

## Slide 4
QuTS hero with ZFS
Enterprise OS

## Slide 5: Why we choose ZFS file system for our enterprise NAS
Enterprises implement a lot of All Flash solutions, and SSD wear out has become the key to IT cost structure
The 3rd QuTS hero dedicated machine launched by QNAP
Because we know that enterprises all value these ...
Corporate data cannot tolerate unintentional error; it is essential to ensure data integrity.
Digital transformation relies on massive data analysis and requires PB-level storage space
Instant disaster recovery capability & complete data protection are the competitiveness indexes of an enterprise

## Slide 6: Powerful data reduction: Extend the SSD endurance
ZFS file system with inline deduplication & inline compression features.
The ZFS file system can be the best choice to pair with the all-flash and SSD storage because it reduces the data size and pattern that need to be written to the SSD directly.
Write to SSDs as sequential as much as possible.
A
C
B
D
Deduplicated Data
A
C
B
D
A
C
B
D
Original Data
SSD Pool
Write
Compression
Deduplication
Compressed Data
A
C
B
D
A
C
B
D
Write to SSDs as sequential as much as possible.
only available when inline dedup/compress enabled

## Slide 7: Amazing massive storage
Data
Model building
Parameter adjustment
Model validation
Deep Learning
200TB is not enough
Only PB-level shared folder is enough to store the huge data matrix .
The best data carrier of big data analysis/edge computing/AI inference

## Slide 8: Silent data corruption & self-healing
ZFS RAID
Application
ZFS RAID
Application
ZFS RAID
Application
Avoid data loss that occurred on the running system.

## Slide 9: Three-layer backup solution : Provide you the most complete data backup protection
Real-time
SnapSync
Real-time
SnapSync
Snapshot & Replica:
SnapSync:
HBS 3 :
Block level, multi-version management; ZFS provides the most lightweight snapshot without affecting storage performance at all.
Block level, Mirror the data copy and always kept up to date.
File level, multi-version management
RPO : daily / schedule
RPO : hourly / 24 hr / 365 day
RPO : Real-time

## Slide 10: WORM (Write Once Read Many times)
WORM is used to avoid modification of saved data. Once this feature is enabled, data in shared folders can only be read and cannot be deleted or modified to ensure data integrity.
  Enterprise Mode: Remove the shared folder through QTS hero UI or SSH commands (QCLI).
  Compliance Mode: Have to take the Storage Pool offline and remove the Pool if want to destroy data.

## Slide 11: TS-h686/TS-h886 – Affordable Xeon D NAS
4 x 2.5GbE!
x 4
4 x 2.5GbE!
TS-h686-D1602-8G
Intel Xeon D-1602 2C4T processor
8GB DDR4 ECC RAM (2x 4GB)
2 x NVMe M.2 SSD port (Gen3 x4)
4 x 2.5GbE LAN port
2 x PCIe Gen3 x8 slot
Built-in QuTS hero OS
TS-h886-D1622-16G
Intel Xeon D-1622 4C8T processor
16GB DDR4 ECC RAM (2x 8GB)
2 x NVMe M.2 SSD port (Gen3 x4)
4 x 2.5GbE LAN port
2 x PCIe Gen3 x8 slot
Built-in QuTS hero OS
x 4

## Slide 12: Intel Xeon D Enterprise Processor
Intel® Xeon® D-1622
  4-core / 8-thread processor
  2.6 GHz, max. boost to 3.2 GHz
Intel® Xeon® D-1602
  2-core / 4-thread processor
  2.5 GHz , max. boost to 3.2 GHz

## Slide 13: Support ECC Memory (Error Correcting Code)
Intel Xeon processors support ECC which automatically detects and repairs single-bit error on-the-fly. ​
Supports up to 128GB
Running reliably without data corruption

## Slide 14: ECC Memory is Important for ZFS
ZFS "Trusts" the contents of memory
  Data checksum is done after reading from memory.
  Corrupt in-memory-data will cause ZFS to use the wrong data to checksum and store in the hard drive
Data source: https://research.cs.wisc.edu/wind/Publications/zfs-corruption-fast10.pdf

## Slide 15: TS-h686/ TS-h886 Front View
TS-h686
3.5"/ 2.5”SATA
6Gb/s HDD/SSD tray
HDD and M.2 port LEDs
LCD Panel
Power button
USB 3.2 Gen 1 & OTC button
2.5”SATA
6Gb/s SSD tray
Lockable tray with 2 keys provided
TS-h886

## Slide 16: Rear View
TS-h886
250W Power supply
Smart system cooling fan(s)
4 x 2.5GbE LAN port
2 x USB 3.2 Gen 1 port
2 x PCIe slot
Slot 2: PCIe Gen3 x8
Slot 1: PCIe Gen3 x8
TS-h686

## Slide 17: Internal Design
Intel Xeon D processor
1 x 6cm CPU cooling fan
2 x NVMe Gen3 x4 M.2 port (2280/22110)
4 x DDR4 long-DIMM slot
1 x PCIe Gen3 x8 slot (CPU side)
1 x PCIe Gen3 x8 slot (HDD side)
Notes: 修改筆記: 中英文數字間加空格

## Slide 18: Multi-zone Heat Dissipation for Low-noise Operation
Sound pressure test：sound pressure is measure at the front bystander position with low fan speed.
The multi-zone heat dissipation utilized in the TS-hx86 enables the dynamic adjustment of the system fan and CPU fan speeds in different zones of the system. It works smoothly and quietly on your desk.
CPU Zone
HDD Zone
Sound Pressure (dB A)
20
50
60
Studio
Office
40
30
70
Library
Suburbs
On the road
TS-h886
21.8
Talk loudly

## Slide 19: Built-in Four 2.5 GbE LAN Ports
(MB/s)
1 x 2.5GbE Windows file transfer
291
265
0
50
100
150
200
250
300
(MB/s)
2.5GbE Benefits:
Up to 2.5x performance
Use the existing wiring infrastructure to support 2.5GbE
New motherboards & Wi-Fi routers are equipped with 2.5GbE.
4 x 2.5GbE
(compatible with 1 GbE)
Read
Write

## Slide 20: QNAP 2.5GbE 5-Port Network Switch
QSW-1105-5T
Set up a multi-user collaboration workflow
Can use current RJ45 Cat5e cable, saving money for replacing cable
TS-h686
2.5GbE
2.5GbE
2.5GbE
2.5GbE
WiFi 6 AP

## Slide 21: Upgrade Network Bandwidth with 5GbE Adapter
Single port：QXG-5G1T-111C
Versatile options
  Support single-port, dual-port, and qual-port adapters
Dual port：QXG-5G2T-111C
Quad port：QXG-5G4T-111C

## Slide 22: Built-in Two PCIe Gen3 x4 M.2 SSD slots
Random
Read
Random
Writer
(IOPS)
Samsung 970 EVO Plus
(Gen3 x4)
620,000
560,000
0
100,000
200,000
300,000
400,000
500,000
600,000
Random
Read
Random
Writer
Samsung 860 Pro
(SATA 6Gb/s)
100,000
90,000
Support PCIe Gen3 x4 M.2 SSD, providing up to 3.2 GB/s bandwidth per slot
Boost random IOPS for multiple concurrent connections
* Performance information is from Samsung official website
NVMe SSD v.s. SATA SSD
Notes: 22

## Slide 23: Tiered storage configuration for a QuTS hero NAS
Step1: system drive
  Creating an SSD RAID with at least two SSDs for the system drive is recommended.
Step2: read/wrie cache
  Use NVMe M.2 SSD for a read/write cache.
Step3: data storage
  Allocate HDDs/SSDs to create a RAID for storing files and application data.
System Drive
Read/Write Cache
Data Storage
SATA HDD
SSD

## Slide 24: Two PCIe Gen3 x8 Slots Provide the Horsepower for Expansion
Each PCIe Gen3 x8 slot provides up to 64 Gb/s bandwidth
Two expansion slots offer the flexibility for expansion
PCIe slot 2：
    Support half high, half length (HHHL) PCIe card
PCIe slot 1：
    Support full high, full length (FHFL) PCIe card

## Slide 25
Complete Expansion Solutions

## Slide 26: Storage Expansion: TL SATA JBOD - economical and flexible expansion enclosures
TL-D400S
By installing QNAP QXP expansion card, NAS can access the TL SATA JBOD with high performance
A single SFF-8088 cable for up to 4 x SATA 6Gb/s = 24 Gb/s transfer speed. Using multiple cables can achieve up to 64 Gb/s between the host and JBOD.
TL-D800S
TL-D1600S
TL SATA JBOD

## Slide 27: Ready to use by including a QXP PCIe SATA expansion card and SFF cable(s)
TL-D400S
1 x QXP-400eS-A1164
PCIe 4-port SATA card
1 x 1M SFF-8088 cable
TL-D800S
QXP-800eS-A1164
PCIe 4-port SATA card
2 x 1M SFF-8088 cable
TL-D1600S
1 x QXP-1600eS
PCIe 16-port SATA card
4 x 1M SFF-8088 to SFF-8644 cable
+
+
+
+
+
+

## Slide 28: Network Expansion： Versatile Network Expansion Accessories
QXG-10G2T-107
LAN-10G2T-X550
QXG-10G2SF-CX4
QXG-5G1T
QXG-5G2T
QXG-5G4T
1 x RJ45
2 x RJ45
4 x RJ45
QXG-10G2T-107
2 x RJ45
1x RJ45
2 x SFP+
LAN-40G2SF-MLX
QXG-25G2SF-CX4
40Gb/s
25Gb/s
2 x RJ45
QXG-32G2FC/QXG-16G2FC
10GbE Network Card
Fibre Channel
5GbE Network Card
40/25GbE Network Card

## Slide 29: Performance Expansion： Expand more NVMe SSD with QM2 Card
4 x M.2 2280 PCIe Gen 3 x4 NVMe SSD slot
QM2-4P-384
(Gen 3 x8)
2 x M.2 22110/2280 PCIe Gen 3 x4 NVMe SSD slot
QM2-2P-384
(Gen 3 x8)
Need more NVMe M.2 SSD for acceleration？Sure！Achieve that with QNAP QM2 cards
Note: QM2-4P-384 can only be installed in PCIe slot 1
Without changing existing configurations

## Slide 30
Applications
QuTS Hero

## Slide 31: Complete Backup 3-2-1 with HBS 3.0
From remote NAS ( via File Station )
Carry and Use (QuDedup Extract Tool)
Access from Cloud
File station with QuDedup (soon)
File station with QuDedup (soon)
HBS 3 (Hybrid Backup Sync 3)
From local NAS
(via HBS 3)
Backup/Restore
.qdff
.qdff
Tokyo
.qdff
.qdff
TCP BBR
CIFS / NFS / FTP
New York
Beijing
.qdff
Taipei
Taipei

## Slide 32: HybridMount provides two modes for file-based cloud storage gateway
 | File Station Mount | File Cloud Gateway
Setup Method | Mount cloud drives | Select “File Cloud Gateway” mode and create a dedicated cache space
Connections | No limit | 2 free and perpetual connections. Purchase license for more connections
Access Performance | Depends on network speed | High performance thanks to caching
Access in File Station | Supported | Supported
Access through SMB / NFS / AFP | Not supported | Supported
Sync with the cloud | Sync only when browsing | Sync constantly for quick access
Integration with QTS Apps | Not supported | Supported ...
NAS
cache
Meta
data
Internet
Slower
LAN
Faster
1
2
3
Online collaboration
File data analysis

## Slide 33: Enterprise LUN backup: VJBOD Cloud block-based gateway
VJBOD Cloud Gateway
Snapshot
Cloud Volume
/Shared folder
Cloud LUN
Target
Cloud object storage space
snapshot
Application
Server
Initiator
SMB/NFS/AFP/
FTP/WebDAV
iSCSI
Client
Initiator
iSCSI
Local user
Local user

## Slide 34: Boxafe: Comprehensive Backup Solution for Google™ G Suite and Microsoft 365®
Keep important data in your hands.
Move older data out of the cloud to reduce cost
Gmail
Backup all your emails and attachments in Gmail
Google Drive
Backup all your file versions in Google Drive and supports My Drive and Shared Drive (coming soon)
Contacts
Backup all your contacts in Google Contacts
Calendar
Backup all your events and attachments in Google Calendar
Outlook
Backup all your emails and attachments in Outlook
Contacts (People)
Backup all your contacts in Outlook People
Calendar
Backup all your events and attachments in Outlook Calendar
OneDrive
Backup all your files in OneDrive and support SharePoint (coming soon)
Google™ G Suite
Microsoft 365®

## Slide 35: Install a Graphics Card for HDMI Output and GPU-accelerated Computing
The TS-hx86 series offers a PCIe Gen3 slot to support low-profile graphics cards that do not need additional power to boost performance of applications such as video editing , 4K UHD transcoding, imaging processing in QTS and performance of virtual machines via GPU passthrough.
GPU Dimension in TS-h686
GPU Dimension in TS-h886
H
L
W
H
L
W
W x H x L: 126mm x 40mm x 261mm
W x H x L: 119mm x 45mm x 266mm

## Slide 36: GPU-accelerated Software
File Station
On-the-fly transcoding & offline transcoding
QuMagie
Photo Station
Video Station
Media Stream Add-on
Video stream transcoding
HD Station
Local display and decode
HD Player
QVR Pro
Virtualization Station
GPU passthrough
QuAI
AI inference acceleration
On-the-fly transcoding & offline transcoding
On-the-fly transcoding
On-the-fly transcoding
Local display and decode
Local display and decode

## Slide 37: GPU-accelerated Application- Multimedia Workers
HD Station
HDMI ouput
File Station
Video preview acceleration
File Station
Offline transcoding and sharing
Media streaming Add-on
Stream acceleration
Material Ingest
AppTV/ Chrome Cast/ smart TV

## Slide 38: GPU-accelerated Application- AI Inference NAS
The last step of the AI is built up an inference host according to the Deep Learning model. GPU cards have been widely adopted to accelerate the inference process. QNAP QuAI SDK and GPU assist accelerate technology has been used in Medical Inference successfully.

## Slide 39: GPU-accelerated Applications - Virtualization Station
With Virtualization Station, you can create multiple virtual machines to run various operating systems such as Windows, Linux, UNIX and Android on a QNAP NAS.
Operate VM via remote desktop
VM Import/Export
VM backup and snapshot
Virtual switch: support multiple network modes
Support USB device connection
GPU passthrough with an external graphics card for VM

## Slide 40
is your best choice!
Copyright © 2020 QNAP Systems, Inc. All rights reserved. QNAP® and other names of QNAP Products are proprietary marks or registered trademarks of QNAP Systems, Inc. Other products and company names mentioned herein are trademarks of their respective holders.