## Slide 2: Upgrade to 2.5GbE+ to unlock the business networking potentials and remove bottlenecks
100 Mbps
1 Gbps
2.5 Gbps
5 Gbps
10 Gbps
 | CAT 5e | CAT 6 | CAT 6A
100M | ✓ | ✓ | ✓
1G | ✓ | ✓ | ✓
2.5G | ✓ | ✓ | ✓
5G | ✓ | ✓ | ✓
10G | X | ✓(55m) | ✓
Increasing wireless devices, video and audio contents, large data backup, file access and real-time communication and video conferences all can cause the existing 1GbE network to be congested, thus slowing down the network speed or having jitters or pauses in video conferences.
Businesses can leverage the current CAT 5e cable infrastructure with the right switches and adapters for 2.5GbE & 5GbE upgrade!

## Slide 3: QNAP 10/5/2.5GbE networking and storage solutions are here to solve slow network issues
PCs/Servers upgrade to 2.5G/5G/10GbE
Rackmount NAS/Server
in the server room
2.5G/5G/10GbE NAS
(integrated or optional upgrade)
Laptops upgrade to 5GbE
Mac upgrade to 10GbE
Base-T
Base-T
Base-T
Base-T/SFP+
SFP+
QNAP switches supporting 10GbE/5GbE/2.5GbE/1GbE
QNA-UC5G1T
QNA-T310G1T
QNA-T310G1S

## Slide 4: TS-x32PXU NAS front view
LEDs:
Status,
Network,
Expansion
Power button
Drive status LED
4/8/12 x 3.5-inch/2.5-inch SATA 6Gb/s drive bays
TS-432PXU, TS-432PXU-RP
TS-832PXU, TS-832PXU-RP
TS-1232PXU-RP

## Slide 5: TS-x32PXU NAS rear views
Internal system smart fans
Reset
button
2 x 2.5GbE Multi-Gig
(2.5G/1G/100M) RJ45 ports
4 x USB 3.2 Gen1 port
2 x 10GbE
SFP+ ports
1 x low-profile PCIe Gen2 x2 slot
AC 100-240V power
Single PSU (250W)
  TS-432PXU
  TS-832PXU
Dual PSU (2 x 250W)
  TS-432PXU-RP
  TS-832PXU-RP
  TS-1232PXU-RP
AC 100-240V 電源輸入
單電源 (250W)
  TS-432PXU
  TS-832PXU
雙電源 (2 x 250W)
  TS-432PXU-RP
  TS-832PXU-RP
  TS-1232PXU-RP
Note: Do not connect the NAS to a network port that supplies power to prevent damages to the network port surge protection function on the NAS.

## Slide 6: Easy to install HDDs & SSDs
2.5-inch HDD / SSD
3.5-inch HDD

## Slide 7: 64-bit quad-core 1.7 GHz power efficient processor crafted for storage servers
Operates with 128-bit SIMD registers for multiple encryption/decryption instructions per cycle
Annapurna Labs SoC integrates 10GbE, SATA 6Gbps, PCIe lanes in a small 27 x 27 mm BGA form
2 x 10GbE SFP+ and 2 x 2.5GbE RJ45 with enhanced floating-point operations and 31 64-bit registers for reduced redundant data access
Cryptography
Integrated I/O
10GbE & 2.5GbE
AARCH64 architecture
ARM Cortex-A57 Quad-core 1.7GHz AL-324 CPU with 64-bit instructions for high performance and energy saving​
TS-1232PXU-RP
Notes: Slot x

## Slide 8: Expand up to 16GB DDR4 memory easily
1 x DDR4 UDIMM slot, expand up to 16GB
QNAP accessories
4GB, 8GB, 16GB RAM
With 1 x 4GB DDR4 UDIMM:
TS-432PXU-4G
TS-432PXU-RP-4G
TS-832PXU-4G
TS-832PXU-RP-4G
TS-1232PXU-RP-4G

## Slide 9: All models are built with dual 10GbE SFP+ & 2.5GbE ports​
2 x 10GbE SFP+ & 2 x 2.5GbE Multi-Gig RJ45 ports delivering a major speed increase for fast backup & restoration, large-data applications, and container application tasks.
2 x 2.5GbE
Multi-Gig RJ45 (2.5G/1G/100M)
2 x 10GbE
SFP+

## Slide 10: Gen2 PCIe slot for flexible network deployment and adding SSD cache
1 x PCIe Gen2 x2
TS-x32PXU provides a low-profile PCIe Gen2 expansion slot
QXG-5G1T-111C
1 x 5G/2.5G/1G/100M port
QXG-2G1T-I225
1 x 2.5G/1G/100M port
QWA-AC2600
Wi-Fi 5 2.4GHz/5GHz AP function
QM2-2S-220A
2 x M.2 2280 SATA 6Gb/s slots

## Slide 11: TS-x32PXU with a QM2 PCIe to add M.2 SSDs for SSD cache or Qtier
QM2-2S-220A
2 x M.2 SATA 6Gb/s
QM2-2P-244A
2 x M.2 NVMe PCIe Gen2
QM2-2S-10G1TA
2 x M.2 SATA 6Gb/s
1 x 10G/5G/2.5G/1G
QM2-2P10G1TA
2 x M.2 NVMe PCIe Gen2
1 x 10G/5G/2.5G/1G

## Slide 12: Qtier auto-tiering for speed and capacity​
SSD cache capacity is not limited by RAM size​
Automatically moves data between different tiers​
熱資料
暖資料
冷資料
分層前
頻繁存取資料效能未優化
開始分層
分層後
頻繁存取資料效能已優化
Qtier
引擎
1
分層前
頻繁存取資料效能未優化
開始分層
2
3
分層後
頻繁存取資料效能已優化
4
資料存取行為改變
Hot data
Warm data
Cold data
Qtier
engine
Before tiering
Frequently accessed data
is not optimized
Start tiering
After tiering
Data is optimized
Changes in data access pattern

## Slide 13: Optimize performance and capacity with Qtier
8 x 3.5-inch HDDs for high-capacity storage​
Install a QM2 adapter with dual M.2 SATA or NVMe SSDs and setup Qtier​
Benefited from 8 x 14TB HDD + 2 x 1TB M.2 SSD
capacity and performance boost!

## Slide 14: Upgrade to Qtier anytime when performance is needed​
Select SSDs and upgrade​
to Qtier pool​
Install a QM2 adapter and M.2 SSD
Scenario
When the HDD-based storage pool cannot provide enough performance…​
２
步驟
1
步驟

## Slide 15: 2.5GbE provides twice more speed over 1GbE for a single client
(MB/s)
1 x 2.5GbE Windows sequential transfer
1 x 2.5GbE Windows sequential transfer
encrypted NAS volume
* Tested in QNAP Labs. Figures may vary by environment.​​
Test environment NAS | TS-1232PXU-RP, QTS 4.4.2, 12 x Samsung 850 Pro 512GB, RAID 5, thick volume
Client PC | Windows 10 Pro, Intel Core i7-6700 3.4 GHz, 32GB RAM
IOmeter | RAM*4, 30-sec ramp up time, 3-min seq. run time, 2 workers, 64-outstanding, 1MB
295
254
252
261
0
50
100
150
200
250
TS-1232PXU-RP
Read
TS-1232PXU-RP
Write
TS-1232PXU-RP
Read
TS-1232PXU-RP
Write

## Slide 16: 2 x 2.5GbE ports for the multi-user/device environment for the future business growth​
In addition to Jumbo Frame support, port trunking /
link aggregation provides enhanced performance.​
488
588
0
100
200
300
400
500
482
325
(MB/s)
TS-1232PXU-RP
Read
TS-1232PXU-RP
Write
TS-1232PXU-RP
Read
TS-1232PXU-RP
Write
* Tested in QNAP Labs. Figures may vary by environment.​​
Test environment NAS | TS-1232PXU-RP, QTS 4.4.2, 12 x Samsung 850 Pro 512GB, RAID 5, thick volume
Client PC | Windows 10 Pro, Intel Core i7-6700 3.4 GHz, 32GB RAM
IOmeter | RAM*4, 30-sec ramp up time, 3-min seq. run time, 2 workers, 64-outstanding, 1MB
2 x 2.5GbE Windows sequential transfer
2 x 2.5GbE Windows sequential transfer
encrypted NAS volume

## Slide 17: Achieve the best performance with​ the integrated 2 x 10GbE SFP+​
(MB/s)
2 x 10GbE Windows sequential transfer
2 x 10GbE Windows sequential transfer
encrypted NAS volume
2288
839
1732
442
0
500
1000
1500
2000
2500
TS-1232PXU-RP
Read
TS-1232PXU-RP
Write
TS-1232PXU-RP
Read
TS-1232PXU-RP
Write
* Tested in QNAP Labs. Figures may vary by environment.​​
Test environment NAS | TS-1232PXU-RP, QTS 4.4.2, 12 x Samsung 850 Pro 512GB, RAID 5, thick volume
Client PC | Windows 10 Pro, Intel Core i7-6700 3.4 GHz, 32GB RAM
IOmeter | RAM*4, 30-sec ramp up time, 3-min seq. run time, 2 workers, 64-outstanding, 1MB

## Slide 18: Short-distance 10GbE SFP+ DAC cable​ for direct connection without a transceiver​
3.0M SFP+ 10GbE​
direct attached copper (DAC) cable​
1.5M SFP+ 10GbE ​
direct attached copper (DAC) cable​
Part number:
CAB-DAC15M-SFPP
Part number:
CAB-DAC30M-SFPP

## Slide 19
2.5GbE & 10GbE Performance
Memory
Upgrade

## Slide 20: Backup the data from your computers​ against viruses and ransomware
NetBak
Replicator
Time
Machine
macOS
Windows
Scheduled or instant backup to counter against viruses and ransomware​
TS-1232PXU-RP

## Slide 21: HBS 3 (Hybrid Backup Sync 3) for NAS data backup and recovery
Use HBS 3 (Hybrid Backup Sync 3) to easily transfer your data to local, remote and cloud storage spaces as a comprehensive data storage and disaster recovery plan.
Notes: Carry and use 在不同地點

## Slide 22: QNAP snapshot for file recovery, up to 256 versions​
Fully supports all storage configurations at the storage pool level.​
Easily take, manage and restore snapshots.​
Using the mature Ext4 file system for "out of volume" snapshots.​
File level
Block level
A
B
C
B’
C’
A’
D’
E’
D
E
RAM size | Maximum total snapshot numbers per NAS​ | Maximum snapshot number per volume/LUN​
4GB and above | 256 | 64
Removeable drives
Local drives
Cloud /
NAS

## Slide 23: Qsirch 5.0 for NAS advanced file search and management
QNAP file management and search solution
Qfile
Auto uploads
NAS data
Data indexing
Exclusion
File Station
uploads
Qsync
Data sync
Other backup methods
Data search and filter
Image
Document
Video
Music
PDF
Email
Data preview
Share
Filing and archiving the search results
Music, photo, video preview
Document and keyword
Mac Finder
Web
Browser
Mobile

## Slide 24: QuMagie photo management with​ object and face auto-classification​
Albums and Smart Albums​
Album view
Folder view

## Slide 25: Connect to home or office NAS with​ myQNAPcloud and QNAP ID (QID)
Register and login with Email or phone number
Anytime / Anywhere

## Slide 26: Connect to Dropbox, OneDrive, Google Drive and more​
Qfile
File Station
Local NAS
Remote NAS
Cloud storage
網頁瀏覽
手機瀏覽

## Slide 27: QNAP QVPN and QBelt protocol for anywhere access​
Secure Encrypted
Connection:​ DTLS + SSL + ​
AES-256 encryption
New VPN protocol:
Decreases the chance of being detected
Works on desktop & mobile devices:​
Windows, macOS,
Android, iOS​

## Slide 28: Active notifications and centralized settings with Notification Center
Centralized setting
One interface to integrate all notification settings and operations
Support multiple notification methods
Meet your various notification scenarios
Highly flexible rule setting
Easily filter important messages you want to receive
Multi-language support
Support 23 language & composed by professionals
Double insurance
Notification history and test function ensure you don't miss one message

## Slide 29: Enhance efficiency with online collaboration
Notes Station 3
Note taking
Image editing
Link
File
Cut
Brush
Pixelation
Shapes
Rotate/
Flip
Text
YouTube
Image
Check list
Table
Chrome extension
Mobile
Apps

## Slide 30: Make NAS your team workspace central and easily collaborate with File Station
 | 以 Office Online 編輯 | 在 Google Docs 中檢視 | 以 Google Chrome 擴充功能開啟
必要設定 | 啟用 MyQNAPCloud CloudLink | 啟用 MyQNAPCloud CloudLink | 以 Chrome 瀏覽器開啟，並安裝擴充功能：Office Editing for Docs, Sheets & Slides
支援格式 | .docx, .pptx, .xlsx | .doc, .ppt, .xls .docx, .pptx, .xlsx | .doc, .ppt, .xls .docx, .pptx, .xlsx
支援能力 | 文件共同編輯與同步至 NAS 檔案 | 文件檢視 可轉成 Google 文件進行編輯 | 文件檢視 可轉成 Google 文件進行編輯
到 設定>文件 裡，選擇你習慣的預設開啟方式吧！
檔案即時同步並回存至NAS中
支援多人線上編輯
 | Edit with Office Online | View in Google Docs | Open with Chrome Extension
Requirement | CloudLink needs to be enabled | CloudLink needs to be enabled | Use Chrome with extension “Office Editing for Docs, Sheets & Slides” to open
Supported formats | .docx, .pptx, .xlsx | .doc, .ppt, .xls .docx, .pptx, .xlsx | .doc, .ppt, .xls .docx, .pptx, .xlsx
Capabilities | File collaboration Auto save to NAS in real time | Document preview Convert to Google docs for editing & saving in your Google Drive | Document preview Convert to Google docs for editing & saving in your Google Drive
Save to NAS in real time
Multi-user online editing
In File Station, go to Settings > Documents to set the default file opening policy

## Slide 31: Surveillance Station 24x7 monitoring with IP cameras
Surveillance Station 5.1
TS-1232PXU-RP
Max*: 16
Vmobile
Recording channels
Free: 2
*Additional license purchase.

## Slide 32: Quad-core 1.7GHz w/ max 16GB RAM, best for Container Station to show your creativity​
Built-in Docker® Hub marketplace
Easy to download
Easily import/export containers​
Imports images or containers from PC or NAS​
Exports images or containers to NAS as backup​
​
AI, IoT, Commonly-used Container Recommendation​
One-click installation wizard helps you quickly setup​
Supports Docker Compose YAML format to create applications​
Notes: Max 8GB RAM for x31P3/431X3

## Slide 33: HybridMount provides two modes for file-based cloud storage gateway
 | Network drive mount | File Cloud Gateway
Setup Method | Mount cloud drives and file servers | Select “File Cloud Gateway” mode and create a dedicated cache space
Connections | No limit | 2 free and perpetual connections. Purchase license for more connections
Access Performance | Depends on network speed | High performance thanks to caching
Access in File Station | Supported | Supported
Access through SMB / NFS / AFP | Partially supported | Supported
Sync with the cloud | Sync only when browsing | Sync constantly for quick access
Integration with QTS Apps | Not supported | Supported
Online collaboration
File data analysis
NAS
cache
META
DATA
Internet
Slower
LAN
Faster
1
2
3

## Slide 34: Business-class LUN backup: VJBOD Cloud block-based gateway
VJBOD Cloud Gateway
快照
Cloud Volume
/Shared folder
Cloud LUN
Target
Application
Server
Initiator
SMB/NFS/AFP/
FTP/WebDAV
iSCSI
Client
雲端物件
儲存空間
Initiator
iSCSI
快照
Local user
Local user
VJBOD Cloud Gateway
Snapshot
Cloud Volume
/Shared folder
Cloud LUN
Target
Application
Server
Initiator
SMB/NFS/AFP/
FTP/WebDAV
iSCSI
Client
Cloud object storage space
Initiator
iSCSI
Snapshot
Local user
Local user

## Slide 35: Use network-based VJBOD to expand other NAS capacity
QNAP x86 NAS (Intel/AMD processor)
TS-1232PXU-RP
TS-451DeU
Setup free space for multiple QNAP NAS devices to connect
iSCSI

## Slide 36: Various NAS accessories for installation or expansion
2 x 2.5-inch SATA 6Gb/s to 1 x 3.5-inch
SATA 6Gb/s hardware RAID 0/1 adapter
Optional rail-kit that is compliant with ANSI/EIA-RS-310-D.
Flexibly use USB or PCIe to multi-channel SATA to expand NAS storage space
TR-004U
TL-R1200C-RP
TL-R400S
TL-R1200S-RP
RAIL-B02
QDA-A2AR
TR & TL expansion enclosures

## Slide 37: Economical and flexible QNAP expansion enclosures for multi-platform usage
Better compatibility: NAS or PC/Server
  Expand NAS or server storage capacity or data migration between different hosts
  QNAP External RAID Manager and JBOD Manager for monitoring the JBOD status
*TS-x32PXU can be installed with an USB 3.2 Gen 2 PCIe expansion adapter (QXP-10G2U3A) for dual USB 3.2 Gen 2 10Gbps ports.
USB Interface
PCIe to SFF-8088 multi-channel SATA interface
QNAP TR RAID and TL JBOD enclosures have many advantages for NAS capacity expansion.
Higher speed
  USB 3.2 Gen 1 5Gb/s, USB 3.2 Gen 2 10Gb/s or up to 64Gb/s with multiple miniSAS SFF-8088 6Gb/s cables
Bigger capacity
  4 & 12-bay choices
  NAS may support up to two enclosures
TR-004U
TL-R1200C-RP
TL-R400S
TL-R1200S-RP

## Slide 38: One enclosure for two different uses: internal expansion or external disk mode
The storage is individual for each disk, it will show 8 independent external disks with TL JBOD or as a single disk with IR RAID unit. This mode is also for cross-platform compatibility among various O.S.
All disks of TR & TL expansion units would be identified by Storage & Snapshot manager, then configure as a RAID of storage pool.
TL & TR units cannot be configured as a RAID group with those internal disks from NAS.
TR units can only support RAID 0/1/5/10 and JBOD modes.
RAID & Storage Pool
External Disk Mode
TL-R1200C-RP

## Slide 39: Two-year extended warranty option for the worry-free coverage
3-year standard warranty service that comes in effect at the time of purchase.
Free repair and part replacement for products under normal use during warranty period. (Spare parts and consumables are excluded)
Extending your warranty with this paid service, available within 90 days of the initial unit purchase.
Offers identical service to standard warranty.
Provide up to 5 years of warranty coverage
3-year Standard Warranty
Optional 2-year Extended Warranty
Part number:
EXTW-ORANGE-2Y

## Slide 40: The upgraded x32PXU with dual 2.5GbE ports for a more agile business
NAS Model | TS-x32PXU | TS-x32XU
Processor | 64-bit Annapurna Labs AL-324 4-core 1.7 GHz | 
Memory | 4GB DDR4 (1 x UDIMM, expandable to 16 GB) | 
PCIe Slot | 1 x PCIe 2.0 x2 slot | 
1GbE LAN | --- | 2
2.5GbE LAN | 2 | ---
10GbE LAN | 2 x 10GbE SFP+ | 
USB Port | 4 x USB 3.2 Gen 1 Type-A | 
SSD Cache | Yes (also supports PCIe QM2 M.2 SSD expansion card) | 
Ordering SKUs | TS-432PXU-4G TS-432PXU-RP-4G TS-832PXU-4G TS-832PXU-RP-4G TS-1232PXU-RP-4G | TS-432XU-4G TS-432XU-RP-4G TS-832XU-4G TS-832XU-RP-4G TS-1232XU-4G TS-1232XU-RP-4G
Upgrade
NEW

## Slide 41
Copyright © 2020 QNAP Systems, Inc. All rights reserved. QNAP® and other names of QNAP Products are proprietary marks or registered trademarks of QNAP Systems, Inc. Other products and company names mentioned herein are trademarks of their respective holders.
Made for the future business growth
Quad-core 1.7GHz,
Dual 10GbE SFP+ & 2.5GbE ports