## Slide 2: SR-IOV Reduce network bandwidth loss

## Slide 3: The network problem of enterprise
VM service requires immediate response
VM service requires a stable network

## Slide 4: How to reduce the network bandwidth loss of VM?
VM service requires immediate response
VM service requires a stable network

## Slide 5: SR-IOV- Single Root I/O Virtualization
A physical network card (Physical Function, PF) can virtualize multiple lightweight PCI-e physical devices (Virtual Function, VF), which can be allocated to virtual machines.
In fact, the VMs uses the VF on the physical network card directly and enjoy the network speed from the network card.
SR-IOV

## Slide 6: SR-IOV Architecture

## Slide 7: The network speed used by SR-IOV is enhanced 20%
 | VM NAS (Client) to NAS(server) None SR-IOV | VM (VF)NAS (Client) to NAS(server) - SR-IOV | 
NAS CPU Usage | 97% | 95% | Reduce CPU usag
VM OS CPU Usage | 13% | 12% | Reduce CPU usage
Transfer speed | 1GB/s | 1.21 GB/s | Enhance performance 20%
Test environment setting | VM
TS-h868 (Client) / FW 4.5.1.1427 + NIC QXG-10G2SF-CX4 | OS : windows server 2016
TS-h668 (Server) / FW 4.5.1.1427 +NIC QXG-10G2SF-CX4 | Cores : 8 (NAS cores )
QVS 3.5.1_20200914 | Memory : 3GB
VM /NAS Client to Server data transfer test
Build 8 VM ,8 VF in QXG-10G2SF-CX48 allocate 1 VF to 1 VM use
Client
Server

## Slide 8: QAT technology doubles compression performance
 | ubuntu-18.04.1-desktop-amd64.iso (1.81GB) -None QAT | ubuntu-18.04.1-desktop-amd64.iso (1.81GB) - QAT | 
Compression Time | 122.64s | 62.28s | Double Compression Speed!
NAS CPU useage | 95% | 93% | CPU useage almost the same
8 VM,each VM allocate 1 QAT VF compression test at the same time.
Test environment setting | VM
Test model: TS-h886 | VM OS: ubuntu 18.04
QVS 3.5.3 | Cores : 8 (NAS cores )
 | Memory : 1GB
VM3
VM1
VM4
VM5
VM8
VM6
VM2
VM7

## Slide 9: The visual UI is more easy to use

## Slide 10: SR-IOV advantages and benefits for user
  Let the services on your virtual machine enjoy the physical network speed.
  If you need real-time service needs, such as ticket booking service, cash flow service, audio-visual service, you can directly enjoy the speed of the hardware network card, reducing network delay.
  Reduce the usage of the host's CPU.
  Increase network efficiency by at least 20%.
Benefits
Advantage

## Slide 11: SR-IOV

## Slide 12: SR-IOV Support list
  TS-h686(Q05SAR01)/TS-h886(Q05SAR01)
  TS-1886XU-RP(Q047AR03)/ TS-h1886XU-RP(Q047AR03)
  TDS-16489U(QX31AR19)/TDS-16489U-R2(QX31AR19)
  QGD-1602P(Q03OAR05)
  TS-h2490FU(Q03XAR15)
SR-IOV support model list and BIOS Version :
  QGD-1602P
QAT support model :
  Intel : LAN-10G2T-X550
  Mellanox :LAN-10G2SF-MLX/LAN-40G2SF-MLX
  Mellanox :QXG-10G2SF-CX4/QXG-25G2SF-CX4
NIC Card :

## Slide 13: SR-IOV notice
SR-IOV needs to be matched with a supported model, BIOS version and supported network card to support it.
SR-IOV support SW version QTS 4.5.2 & QVS 3.5.3.
QAT needs to install the corresponding virtual function driver in the Guest OS.
  Currently, the downloadable driver version on the official website is Linux and FreeBS.
    Intel driver download link - https://01.org/intel-quick-assist-technology/downloads
The VM Live Migration function cannot be used when using SR-IOV (Device Passthrough).
Because the physical device used by the VM will not recognize the original physical device ID after VM Live migration.