## Slide 2
01. QNAP high-speed NIC products,
lead to next generation of faster ethernet
03. QTS / QuTS hero support FEC configuration
02. Specification & Features
04. Build up 25GbE environment

## Slide 3
QNAP high-speed NIC products,
lead to next generation of faster ethernet

## Slide 4: Fast growing market and performance of SSD
QNAP All-Flash Array
Read 6,200MB/s, Write 4,900MB/s
SAMSUNG 980 PRO
More and more NVMe SSDs are launched.
Speed of Internet should be also increased as the bandwidth of SSD doubles!
Read 6,800MB/s, Write 4,000MB/s
SAMSUNG PM9A3 U.2 SSD
TS-h2490FU / TS-h3088XU-RP
All-flash array provides hundreds of thousands of IOPS, but do you get your I/O devices up to speed?
OK

## Slide 5: SSD generation comes! PCIe 4.0 doubles the bandwidth
2020 Global Shipments of SSDs Surpassed HDDs for First Time!
PCIe Gen4 doubles the speed of Gen3
PCIe 3.0
PCIe 4.0
PCIe 5.0
32 GT/s
Solid-state drive shipments surpassed those of traditional hard drives by a significant margin in 2020 but spinning media retained the crown in terms of overall capacity served. As pricing continues to plummet and capacity increases, we can expect to see the ratio become even more skewed.
According to data storage research and consulting firm TrendFocus (per Storage Newsletter), manufacturers shipped 333.12 million solid-state drives in 2020 – an increase of 20.8 percent year-over-year. Hard drive shipments, meanwhile, were down 18 percent annually to 259.81 million units.
PCIe 3.0 standard bandwidth: 8 GT/s
PCIe 4.0 standard bandwidth: 16 GT/s
16 GT/s
8 GT/s
Source: techspot

## Slide 6: Bottleneck for 10GbE high-speed transmission among multiple users
PC/workstation
Enterprise U.2 NVMe SSD or PCIe Gen4 SSD
10GbE
Transmission
Bottleneck
10GbE Card
Hundreds of thousands of IOPS
OK
QNAP All-Flash Array
TS-h2490FU / TS-h3088XU-RP
10GbE
Transmission
10GbE
Transmission

## Slide 7: Strength of 25GbE – easily upgrade to 50/100GbE
Lower bandwidth than 40GbE, but more easily upgrade to 50/100GbE
Source：Mellanox
Chart: 
| 10G | 25G | 40G | 50G | 100G | 200G
銷售 | 0.78 | 0.07 | 0.11 | 0.02 | 0.02 | 0
78%
7%
11%
2%
2%
Of total Market
22%
25G+ Segment Growing at 38% CAGR
High Speed Adapters 2017
Chart: 
| 10G | 25G | 40G | 50G | 100G | 200G
銷售 | 0.45 | 0.15 | 0.02 | 0.15 | 0.21 | 0.02
45%
15%
2%
2%
15%
21%
Of total Market
55%
OK
Notes: 網址

## Slide 8
Specification &
Features
OK

## Slide 9: Brand new QNAP 25GbE NIC – QXG-25G2SF-CX6
QXG-25G2SF-CX6
Dual-port 25GbE SFP28 NIC
2 x SFP28 connectors
Support 2-speed 25GbE / 10GbE
Mellanox
ConnectX®-6 Lx Controller
Support iSER / RoCE offloads
OK

## Slide 10: QXG-25G2SF-CX6 25GbE hardware specfication
PCIe Gen4 x8 interface
up to 128Gbit/s bandwidth
Dual-port 25GbE (SFP28) ports
Low-profile bracket pre-installed;
full-height and specialized (for selected QNAP NAS) brackets are bundled
Active heatsink for controller chip
25GbE SFP28 DAC
OK
Optional accessory

## Slide 11: Support multiple OS to deploy your 25GbE environment
OK
Download Windows Driver
Download Linux Driver
QTS 4.5.2 and later
QuTS hero 4.5.2 and later
Ubuntu 18.04 and later

## Slide 12: QXG-25F2SF-CX6 v.s QXG-25G2SF-CX4
 | QXG-25G2SF-CX4 | QXG-25G2SF-CX6
PCIe express | Gen3 x8 | Gen4 x8
Message Rate | 70Mpps | 75Mpps
PTP (1588) | N/A | Supported
Secure boot | N/A | Supported
VirtIO acceleration | N/A | Yes
RoCE v1/v2 | Supported | Supported
RDMA | Supported | Supported
SR-IOV | Supported | Supported
Chart: Performance
| CX4 Gen3 x8 | CX6 Gen3 x8 | CX6 Gen4 x4 | CX6 Gen4 x8
Read (Gb/s) | 23.4 | 24.4 | 23.9 | 24.3
Write (Gb/s) | 22.4 | 24.4 | 24.4 | 24.5

## Slide 13: Connector's form-fact from 1GbE to 100GbE
OK
1 GbE
10 GbE
25 GbE
40 GbE
100 GbE
SFP
SFP+
SFP28
QSFP+
QSFP28

## Slide 14: Experience the fastest performance with PCIe 4.0 NAS
Slot 1: PCIe Gen4 x4 Slot 2: PCIe Gen4 x8 or x4 Slot 3: PCIe Gen4 x4 Slot 4: PCIe Gen4 x8 Slot 5: PCIe Gen4 x16 or x8
*Slot 4 and Slot 5 are preinstalled with 25GbE network adapters. Please reserve these slots for the 25GbE adapters for the best performance. **Slot 2 provides the width of PCIe Gen4 x8 when Slot 3 is not in use, and provides the width of PCIe Gen4 x4 when Slot 3 is in use. ***Slot 5 provides the width of PCIe Gen4 x16 when Slot 4 is not in use, and provides the width of PCIe Gen4 x8 when Slot 4 is in use.
TS-h2490FU-7302P-128G
AMD EPYC 16core/32thread, 3.0 GHz (Max. 3.3GHz)
128GB DDR4 RDIMM ECC memory (8 x 16GB)
4 x SFP28 25GbE ethernet ports (25GbE/10GbE/1GbE)
TS-h2490FU-7232P-64G
AMD EPYC 8coew/16thread, 3.1 GHz (Max. 3.2GHz)
64GB DDR4 RDIMM ECC memory (8 x 8GB)
2 x SFP28 25GbE ethernet ports (25GbE/10GbE/1GbE)
TS-h2490FU
Notes: 實際效能

## Slide 15: Upgrade you QNAP High-end NAS with PCIe 3.0 for faster ethernet experience
TS-h3088XU-RP
OK
*Find out full compatibility list on our website!
Intel Xeon W 1250 /1270
2 x SFP28 25GbE ethernet ports (25GbE/10GbE/1GbE)
TS-hx83XU
1U: Gen3 x16 (CPU)
2U & 3U : Slot 2 with Gen3 x8 (CPU)
4U: slot 4 with Gen3 x8 (CPU)
Slot 1: PCIe Gen3 x8 or x4 Slot 2: PCIe Gen3 x4 Slot 3: PCIe Gen3 x4
Intel Xeon E series
2 x SFP+ 10GbE ethernet ports (10GbE/1GbE)
TVS-h1288X
TVS-h1688X
Intel Xeon W 1250 /1270
2 x RJ45 10GbE ethernet ports (10GbE/5GbE/2.5GbE/1GbE/100M)
Slot 1: PCIe Gen3 x8 Slot 2: PCIe Gen3 x4 Slot 3: PCIe Gen3 x4
Notes: 3088xu 83xu
URL

## Slide 16: Offload tasks from CPU with iSER
iSER allows data to bypass general network drivers, the socket layer, and to directly enter memory buffers of the server and storage.
Increasing performance, lower CPU loading
With iSER
Without iSER
OK
*iSER will support in QTS / QuTS hero later

## Slide 17
QTS / QuTS hero support FEC configuration
OK

## Slide 18: Ensure data correction during transmission with FEC
FEC (Forwarded-error-Correction) controlling errors in data transmission over unreliable or noisy communication channels.
FEC must configured the same mode for both switch and NIC side.
Enable FEC (To turn on/off FEC)
Auto-negotiation
(Follow the sequence to negotiation from RS-FEC -> Base-R FEC -> Disable FEC -> 10GbE)
BASE-R FEC (Enable BASE-R FEC)
aka Firecode or Clause 74. Offers simple, low-latency (<100ns) protection against bursty errors.
RS-FEC (Enable RS-FEC)
aka Reed Solomon or Clause 91. Offers better error protection but adds latency (~250ns)
Configure FEC option require QTS 4.5.3 / QuTS hero 4.5.2 and later
*Older QTS/QuTS hero, FEC are set as Auto-negotiation.
*Switch and NIC require the same FEC configure in order to work properly.
OK

## Slide 19: Support FEC configuration for all models above 25GbE
For QTS 4.5.3 / QuTS hero 4.5.2 and later, you could configure FEC mode depends on your network environment in NIC setting page
QXG-10G2SF-CX4
QXG-25G2SF-CX4
QXG-100G2SF-E810
LAN-40G2SF-MLX
OK
QXG-25G2SF-CX6

## Slide 20: Configure FEC mode with ethtool in Windows / Linux
Show current FEC mode
ethtool --show-fec devname
configure FEC mode
Auto: ethtool --set-fec devname encoding auto
Off: ethtool --set-fec devname encoding off
RS-FEC: ethtool --set-fec devname encoding rs
BASE-R FEC: ethtool --set-fec devname encoding baser
＊Driver for Windows / Linux are required.
OK
Windows: https://www.mellanox.com/products/adapter-software/ethernet/windows/winof-2
Linux: https://www.mellanox.com/products/infiniband-drivers/linux/mlnx_ofed

## Slide 21
Performance
OK

## Slide 22: 25GbE Performance
TS-x83XU
PC:
Intel® CoreTM i7-6700 3.40GHz.
Windows 10, 64GB RAM, QXG-25G2SF-CX4 on board,
Samsung SSD 960 PRO 1TB NVMe
NAS:
1283XU. Intel® Xeon® E-2124 CPU @ 3.30GHz.
QTS 4.3.6.0805, 4GB RAM, QXG-25G2SF-CX4 on board,
Samsung SSD850 Pro 512GB*12 (RAID 0)

## Slide 23
Build up 25GbE environment
OK

## Slide 24: QNAP makes your network environment faster!
VM
Media Workstation
QNAP 100GbE NIC
QXG-100G2SF-E810
18x 10/25GbE SFP+/28 ports
4x 40/100GbE QSFP+/28 ports
QNAP High-end NAS
Or Server
OK
25 GbE
Mellanox SN2010 25/100 GbE switch
25 GbE
25 GbE
100 GbE

## Slide 25: Connect to 100GbE/50GbE environment with break-out cable
OK
QSFP28 break-out cable
4 x SFP28 connector
4 x 100GbE ports
TRX-25GSFP-SR
25GbE SR Transceiver
TRX-10GSFP-SR-MLX
10GbE SR Transceiver
Support 25GbE Transceiver
Compatible 10GbE Transceiver

## Slide 26: Accessories for 10GbE / 25GbE / 100GbE
QXG-25G2SF-CX6
QXG-100G2SF-E810
TRX-10GSFP-SR-MLX
CAB-DAC30M-SFP28
CAB-DAC15M-SFP28
CAB-DAC15M-QSFP28
CAB-DAC15M-QSFP28-B4
25GbE SFP28 DAC
100GbE QSFP28 DAC
10GbE SR Transceiver
TRX-25GSFP-SR
25GbE SR Transceiver
OK

## Slide 27: Upgrade to 25GbE environment now!
Upgrade to 25GbE / 100GbE now!
QNAP
High-end NAS
OR Server
Mellanox SN2010 25/100 GbE switch
QXG-25G2SF-CX6
CAB-DAC30M-SFP28
OK
1
2
3

## Slide 28
Your best choice!
Copyright © 2021 QNAP Systems, Inc. All rights reserved. QNAP® and other names of QNAP Products are proprietary marks or registered trademarks of QNAP Systems, Inc. Other products and company names mentioned herein are trademarks of their respective holders.