## Slide 2: Build your 10G environment with NEW QNAP NIC

## Slide 3: QNAP New 10GbE Network Interface Card QXG-10G2T-X710
QXG-10G2T-X710
Dual-port 10GbE BASE-T low profile NIC
2 x RJ45 10GBASE-T
5-speed; 10/5/2.5/1GbE, 100M
Intel
Ethernet Controller 700
SR-IOV
Intel® Data Direct I/O Technology

## Slide 4: QXG-10G2T-X710 10GbE NIC overview
PCIe Gen3 x4 interface
Dual-port 10GbE (BASE-T) connector
(10/5/2.5/1G,100M)
Pre-install Low profile bracket
include Full height special bracket for selected QNAP NAS
Heatsink & fan for controller chipset
OK

## Slide 5: QXG-10G2T-X710 Hardware specification
 | QXG-10G2T-X710
網路控制晶片 | Intel Ethernet Controller 700
傳輸速度 | 10/5/2.5/1GbE, 100M
連接埠 | NBAST-T; RJ45
埠數 | 2
支援 QNAP 作業系統 | QTS 4.5.2 或之後的版本 QuTS hero 4.5.1 或之後的版本
支援其他作業系統 | Windows/Windows Server/Linux
PCIe 介面 | PCI Express 3.0 x4
包裝內容 | 1 x QXG-10G2T-X710 1 x QIG (快速安裝指南) 3 x 擋版 (出貨時預先安裝短擋版於網路擴充卡上)
 | QXG-10G2T-X710
Ethernet Controller | Intel Ethernet Controller 700
Transmission Speed | 10/5/2.5/1GbE, 100M
Connector | NBAST-T; RJ45
Port# | 2
Support QNAP OS | QTS 4.5.2 and later QuTS hero h4.5.1 and later
Support 3rd party OS | Windows/Windows Server/Linux
PCIe interface | PCI Express 3.0 x4
Package content | 1 x QXG-10G2T-X710 1 x QIG (Quick Installation Guide) 3 x brackets (pre-install half-height on NIC when shipping)

## Slide 6: SR-IOV advantages and benefits for user
Advantage
  Let the services on your virtual machine enjoy the physical network speed.
Benefits
  If you need real-time service needs, such as ticket booking service, cash flow service, audio-visual service, you can directly enjoy the speed of the hardware network card, reducing network delay.
  Reduce the usage of the host's CPU.
  Increase network efficiency by at least 20%.

## Slide 7: SR-IOV Support list
SR-IOV support model list and BIOS Version:
  TS-h686(Q05SAR01)/TS-h886(Q05SAR01)
  TS-1886XU-RP(Q047AR03)/ TS-h1886XU-RP(Q047AR03)
  TDS-16489U(QX31AR19)/TDS-16489U-R2(QX31AR19)
  QGD-1602P(Q03OAR05)
  TS-h2490FU(Q03XAR15)
QAT support model:
  QGD-1602P
NICs:
  Intel: LAN-10G2T-X550/QXG-100G2SF-E810/QXG-10G2T-X710
  Mellanox:LAN-10G2SF-MLX/LAN-40G2SF-MLX
  Mellanox:QXG-10G2SF-CX4/QXG-25G2SF-CX4/QXG-25G2SF-CX6

## Slide 8: SR-IOV notice
SR-IOV needs to be matched with a supported model, BIOS version and supported network card to support it.
SR-IOV support SW version QTS 4.5.2 & QVS 3.5.3 .
QAT needs to install the corresponding virtual function driver in the Guest OS
  *Currently, the downloadable driver version on the official website is Linux and FreeBSD Intel driver download link - https://01.org/intel-quick-assist-technology/downloads
The VM Live Migration function cannot be used when using SR-IOV (Device Passthrough) Because the physical device used by the VM will not recognize the original physical device ID after VM Live migration.

## Slide 9: Easily upgrade to 10GbE environment with BASE-T connector
10Gbps
10GBASE-T recommend use CAT 6 cable！
Support Multi-Gigabit
NBASE-T Standard
 | CAT 5e | CAT 6 | CAT 6A
100M | V | V | V
1G | V | V | V
2.5G | V | V | V
5G | V | V | V
10G | X | V (55m) | V
1/2.5/5 Gbps
CAT 5e
CAT 6
TS-x73A
TS-x73A
10GbE
NIC

## Slide 10: Build your 10GbE environment easily across multiple Operating System
OK
Download Windows Driver
Download Linux Driver
QTS 4.5.2 and later
QuTS hero h4.5.1 and later
Ubuntu 18.04 and later

## Slide 11: Extend your QNAP NAS with 10GbE NIC
TS-873AU/1273AU/1673AU
OK
*Find out supported QNAP model on our Compatibility list.
AMD Ryzen™ V1500B quad-core
2 x 2.5GbE ports (2.5/1GbE, 100/10M)
TS-473A/673A/873A
Slot 1: PCIe Gen 3 x4
Slot 2: PCIe Gen 3 x4
Slot 1: PCIe Gen3 x4
Slot 2: PCIe Gen3 x4
AMD Ryzen™ V1500B quad-core
Built in 2.5GbE port
TS-h686
TS-h886
Intel Xeon D series
4 x RJ45 2.5GbE ports
Slot 1: PCIe Gen3 x8 Slot 2: PCIe Gen3 x8
Notes: 3088xu 83xu
URL

## Slide 12: Up to 1000+MB/s Read/Write performance
PC install QXG-10G2T-X710 transfer file to TS-977
PC spec:
1. CPU: Intel (R) Xeon W
2. OS: Windows Server 2019
3. Memory: 64 GB.
4. 1GbE NIC On board
5. 10GbE NIC: QXG-10G2T-X710
MB/s
1GbE
10GbE
Download:
118MB/s
Upload:
118MB/s
Download:
1103MB/s
Upload:
1127MB/s
Notes: PC安裝QXG-10G2T-107 透過QSW-1208-8C傳輸10GB檔案至TVS-672N,
CPU: Intel (R) Core(TM) i7-6700 CPU@ 3.40GHz. 2. OS: Windows 10. 3. Memory: 64 GB. 4. 1GbE NIC On board 5. 10GbE NIC: QXG-10G2T-AQC107

## Slide 13: LAN-10G2T-X550 vs. QXG-10G2T-X710
 | LAN-10G2T-X550 | QXG-10G2T-X550
PCIe express | Gen3 x4 | Gen3 x4
Ethernet Controller | 500 Series | 500 Series
SR-IOV | Supported | Supported
Power consumption | Higher | Higher
Support Speed | 5-speed; 10/5/2.5/1G, 100M | 
Chart: Performance
| LAN-10G2T-X550 | QXG-10G2T-X710
Upload | 1159 | 1103
Download | 1170 | 1127
1159
1170
MB/s
1103
1127
 | LAN-10G2T-X550 | QXG-10G2T-X710
PCIe express | Gen3 x4 | Gen3 x4
Ethernet Controller | 500 Series | 700 Series
SR-IOV | Supported | Supported
Power consumption | Higher | Lower
Support Speed | 5-speed; 10/5/2.5/1G, 100M | 5-speed; 10/5/2.5/1G, 100M
Notes: PC安裝QXG-10G2T-107 透過QSW-1208-8C傳輸10GB檔案至TVS-672N,
CPU: Intel (R) Core(TM) i7-6700 CPU@ 3.40GHz. 2. OS: Windows 10. 3. Memory: 64 GB. 4. 1GbE NIC On board 5. 10GbE NIC: QXG-10G2T-AQC107

## Slide 14: QXG-10G2T-X710 vs. QXG-10G2T-107
 | QXG-10G2T-107 | QXG-10G2T-X550
PCIe express | Gen2 x4 | Gen3 x4
Ethernet Controller | Marvell AQC107 | Intel 700 Series
SR-IOV | Not-supported | Supported
Support OS | Windows 8/10 Linux | Windows 8/10 Windows Server Linux Ubuntu RHEL
Support Speed | 5-speed; 10/5/2.5/1G, 100M | 
Chart: Performance
| QXG-10G2T-X710 | QXG-10G2T-107
Upload | 1103 | 1134
Download | 1127 | 1157
MB/s
1103
1127
1134
1157
 | QXG-10G2T-107 | QXG-10G2T-X710
PCIe express | Gen2 x4 | Gen3 x4
Ethernet Controller | Marvell AQC107 | Intel 700 Series
SR-IOV | Not-supported | Supported
Support OS | Windows 8/10 Linux | Windows 8/10 Windows Server Linux Ubuntu RHEL
Support Speed | 5-speed; 10/5/2.5/1G, 100M | 5-speed; 10/5/2.5/1G, 100M
Notes: PC安裝QXG-10G2T-107 透過QSW-1208-8C傳輸10GB檔案至TVS-672N,
CPU: Intel (R) Core(TM) i7-6700 CPU@ 3.40GHz. 2. OS: Windows 10. 3. Memory: 64 GB. 4. 1GbE NIC On board 5. 10GbE NIC: QXG-10G2T-AQC107

## Slide 15: Windows file transfer – 10GB file

## Slide 16: QNAP Multi-Gig NIC, switch and accessories

## Slide 17: QNAP Multi Gig NICs – Intel
10GbE
2.5GbE
4-speed Multi- Gig
5-speed Multi- Gig
LAN-10G2T-X550
Intel X550
Dual-port 10GbE NBase-T
PCIe Gen3 x4
Low Profile
QXG-2G1T-I225
QXG-2G2T-I225
QXG-2G4T-I225
Intel I225-LM
1/2/4-port 2.5GbE NBase-T
PCIe Gen3x1, Gen3 x2, Gen3 x4
Low Profile

## Slide 18: QNAP Multi Gig NICs – Marvell Aqtion
10GbE
5GbE
4-speed Multi- Gig
5-speed Multi- Gig
QXG-10G1T
QXG-10G2T-107
AQtion AQC107
Single-port 10GbE NBase-T
PCIe Gen3 x4
Low Profile
AQtion AQC107S
Dual-port 10GbE NBase-T
PCIe Gen2 x4
Low Profile
QXG-5G1T-111C
QXG-5G2T-111C
QXG-5G4T-111C
AQtion AQC111C
1/2/4-port 5GbE NBase-T
PCIe Gen2 x1, Gen3 x2, Gen3 x4
Low Profile

## Slide 19: QNAP Multi Gig Accessories
For PC and laptops, upgrade to 5Gbps ethernet with USB 3.2 Gen 1
For Thunderbolt3 Ｍac/PC upgrade to 10Gbps ethernet easily.
5G/2.5G/1G/100M 4-speed
RJ45 NBASE-T connector
10G/5G/2.5G/1G/100M 5-speed
RJ45 NBASE-T connector
Host with USB 3.2 Gen1
Host with Thunderbolt 3
QNA-T310G1T
QNA-UC5G1T
Notes: QSW-308

## Slide 20: Faster, and faster!
Cat 6
Cat 6
Upgrade to 10GbE
Cat 5e
1GbE
Cat 5e
1GbE
Cat 5e
1GbE
TS-x73A
Upgrade to 10GbE
PC+ 10G2T-X710
1/2.5GbE switch
Cat 6
10GbE
10GbE
10GbE switch
QSW-M1208-8C
Web-management 10GbE switch
10GbE
10GbE
10GbE
QXG-10G2T-X710
or QNA-T310G1T/1S

## Slide 21: Build your 10G environment with switch
搭配交換機打造 10GbE 環境
OK

## Slide 22: QNAP QSW-M1208 managed 10GE switch for multi-10GbE aggregated multi-user editing
4 x 10GbE SFP+ ports
8 x 10GbE SFP+ & RJ45 Combo ports
8 x 10GbE SFP+ ports
4 x 10GbE SFP+ & RJ45 Combo ports
QSW-M1204-4C
4 x 10GbE SFP+ ports
4 x 10GbE SFP+ & RJ45 Combo ports
QSW-M804-4C
QSW-M1208-8C

## Slide 23
Wireless connectivity: support WiFi 6 (802.11ax)
Dual-port 10GbE flexible for WAN/LAN
Optimized Eight omnidirectional internal high gain antenna
Enable subscription-free QNAP SD-WAN on QHora-301W
QHora-301W
New Generation WiFi 6 and Dual 10GbE SD-WAN Router