## Slide 2: Maker x Backup x Sharing x Work x Entertainment everywhere
B5 size
30 x 230 x 165 mm
1.18 x 9.06 x 6.50 inch (H x W x D)
740g / 1.63lbs
Light weight for portability
Thin & light; use it everywhere

## Slide 3: M.2 SSD for the best performance
4 x M.2 2280 NVMe Gen 3 x 2 SSD slots
(optional SSD purchase)

## Slide 4: QTS 5.0 + Linux kernel 5.10
To provide the best performance of Intel® Celeron® N5105/N5095, TBS-464 is shipped with QTS 5.0, using the new Linux kernel 5.10. QTS 5.0 optimizes overall system performance and NVMe SSD over-provisioning & cache performance to enhance TBS-464 functionality.
2.9GHz
Burst
N5105/ N5095
Jasper Lake
4-core
4-thread
AES-NI encryption
Volume & folder support
GPU up to 800 MHz
UHD Graphics

## Slide 5: What is SSD over-provisioning
SSD Over-provisioning reserves space in the SSD to decrease write amplification & increase consisted performance and endurance.
Reason: to avoid Garbage Collection in any giving point of time
D | D
D | D
D | D
6 pages of new data cannot all be stored to the SSD
N | New Data
D | Valid Data
 | Invalid Data
 | OP
 | OP
N | N
N | N
N | N
With more reserved block, the GC is not required
Unless the SSD conduct GC internally first
N | N
D | 
D | 
N | N
N | N
D | D
D | D
D | D
With limited OP, 4 more write is needed. With more OP the GC is not required.

## Slide 6: Choosing SSD is hard, choosing QNAP is simple
SSD consisted performance can only be observed after long time of usage.
QNAP has provided the unique SSD Profiling Tool to help user measure the performance difference with different over-provisioning amounts.
Not just IT manager, home user can also evaluate the capability of SSD.
Using SSD Profiling Tool to identify the best OP amount.

## Slide 7: Create a tighter hybrid cloud system
Light storage in NAS + Unlimited storage in Cloud
= Everything is Possible
File-level Gateway
HybridMount
Block-level Gateway
VJBOD Cloud
Capacity
Unlimited Expansion
HybridMount
VJBOD Cloud

## Slide 8: HybridMount: enable cache to enhance cloud experience
File Management
Editing Tool
Multimedia
Application
Access with
Network Protocol
Mount space of 20 cloud providers​​
Enjoy QTS applications with your cloud data

## Slide 9: VJBOD Cloud + public cloud frees the private cloud from its limitation
Using the public cloud storage space just like a volume (or iSCSI LUN) on the NAS.
Compared to file-level HybridMount, the block-level VJBOD Cloud increase the efficiency of transferring random data and large files to the cloud to provide business-level gateway solution.
With Block-level solution， the uploaded data cannot be recongized by the cloud or its applications
In file-level, a modified file need to be re-upload in full.
In block-level, only the modified block needs to be uploaded to the cloud.
Modified Data
Oringial Data

## Slide 10
Using VJBOD Cloud to create a reliable database
Even the best RAID protection cannot stand again physical shock!
For files, they can be upload to cloud, how about iSCSI LUN?
With VJBOD Cloud, an iSCSI LUN can be created at Cloud and shared via NAS. Using the edge solution to accelerate performance while allowing new device to connect & share the LUN at any time!
Using Different NAS to share the LUN when needed
Cloud LUN as Object
Having a reliable database backup solution for your application
* One Cloud LUN can only be connected by one NAS at a time

## Slide 11: 2.5GbE Bandwidth brings out SSD potential
Test environment: TBS-464: 4 x Seagate Ironwolf 510 M.2 2280 NVMe SSD, RAID 5, QTS 5.0, onboard 8GB RAM
Client PC: Windows Server 2019, Intel Xeon W-1250, 32GB RAM, onboard 2.5GbE (Intel i225)
Upload
Download
Upload
Download
294
287
586
574
0
100
200
300
400
500
600
700
(MB/s)
2 x 2.5GbE port trunking
1 x 2.5GbE

## Slide 12: TBS-464 front view
USB OTC button
USB 3.2 Gen 1 ports
M.2 SSD status LEDs
Power button and status LED
IR receiver

## Slide 13: TBS-464 side views
USB 2.0 port
Right side
Left side
USB 2.0 Port

## Slide 14
TBS-464 rear views
2.5GbE ports
USB 2.0 ports
HDMI ports (up to 2.0)
Kensington lock
reset
Power input

## Slide 15: M.2 NVMe SSD installation
4 x M.2 2280 NVMe
SSD slots
(SSDs not included)

## Slide 16: Smart ‘n quiet fan with optimal thermal design
Air flow brings out excessive heat
Brand new M.2 SSD heatsink
Include thermal pads for single & dual-sided M.2 SSD

## Slide 17: HDMI 2.0 4K 60FPS sharp picture quality

## Slide 18: HybridDesk Station for various A/V needs
Qremote App
Mouse &
Keyboard
USB
HDMI
Network

## Slide 19: Versatile HybridDesk Station apps
System Mgmt.
Multimedia Mgmt.
Multimedia
Surveillance
Browser & Productivity
Comm. & Social
QTS
FileStation HD
QVR Pro Client
Skype
Facebook
HD Player
Clementine
Spotify
TuneIn Radio
PhotoStation HD
VideoStation HD
MusicStation HD
Chrome
Firefox
LibreOffice

## Slide 20: Qbutton: customize remote button actions
Optional purchase of QNAP RM-IR004 IR remote control
Play your favorite music playlist with a single button or set other buttons to play the previous or next song
View pre-selected channels on Surveillance Station for quick surveillance monitoring
Set a button to restart or power off your NAS for greater convenience

## Slide 21: Linux Station turns NAS into a Ubuntu PC
Ubuntu 18.04
Ubuntu 20.04
HDMI output from NAS to a monitor
1
Connect a USB keyboard and a mouse to the NAS to start using Ubuntu
2
Multi-version Ubuntu

## Slide 22: Streaming & accelerated transcoding
4K H.264 decoding & encoding for real-time or offline 4K video transcoding on various client players for smooth playback and support more clients
HDMI output for 4K Ultra HD (3840 x 2160, 60FPS) content
Stream content through DLNA, AirPlay, Chromecast and Plex

## Slide 23: Use PLEX to stream media collections
TV & PC
Mobile
Phone
Tablet
PC
SmartTV
Players

## Slide 24: Backup or sync data at your choice
NetBak Replicator
Qsync
macOS
Windows
Scheduled or real-time backup/sync
Time Machine
Qsync
Protection against ransomware!

## Slide 25: Business-level snapshot
Best
Snapshot # Volume/LUN
Snapshot # per NAS
---------------------------------------------------------
1024
256
choice!

## Slide 26: Backup the NAS data
Hybrid Backup Sync
Cloud
Local
Remote

## Slide 27: QVR Pro 24/7 surveillance solution
6,000+ IP cameras
8 free channels
128 ch max channels (license)
QUSBCam2 for webcam recording

## Slide 28: Expand storage via VJBOD
iSCSI
Max 8 remote NAS
Use other NAS capacity to expand own capacity via network connection
10GbE / 1GbE mount
VJBOD
2.5GbE
iSCSI

## Slide 29: TR-004 RAID box for expansion or data sharing
Two use cases:
1. NAS, Windows, macOS & Linux cross-platform external device mode 2. QNAP NAS capacity expansion mode
Pool
External
device
USB 3.0
USB 3.0
TR-004
Two modes
TBS-464

## Slide 30: QuMagie
What is QuMagie?
  QuMagie is an AI-powered photo management solution with flexible storage space
  QuMagie is a free application within QNAP NAS system
Browse, Manage Photos
手持裝置
手持裝置
手持裝置
Upload, Backup Photos
Share Photos
Mobile
Camera
PC
QNAP NAS
QuMagie
Mobile
PC
Social Media
QNAP AI Core

## Slide 31: Coral M.2 Accelerator B+M key
Coral M.2 Accelerator B+M key
  Coral P/N: G650-04686-01
  4 TOPS total peak performance (int8)
  2 TOPS per watt (TOPS = trillion operations per second)
  M.2 2280 B+M key form factor
  PCIe Gen 2 x 1 interface
QNAP P/N: G650-04686-01-QNAP
  Package contents
    Coral M.2 Accelerator B+M key
    QNAP Heatsink
    NAS Installation guide

## Slide 32: Coral USB Accelerator
Coral USB Accelerator
  Coral P/N: G950-06809-01 & G950-01456-01
  4 TOPS total peak performance (int8)
  2 TOPS per watt (TOPS = trillion operations per second)
  No extra power adapter needed
  USB 3.2 Gen 1 (USB 3.0) Type-C interface (data/power)
QNAP P/N: G950-06809-01-QNAP
  Package contents
      Coral USB Accelerator
      NAS installation guide
65 mm
(2.56 inches)
30 mm (1.18 inches)

## Slide 33
QVR Face helps users build intelligent face recognition QVR Human proactively calculates the number of people passing through a specific region
QVR Face / Human

## Slide 34
Improve NVMe SSD Performance
With the new kernel, NVMe usage efficiency is greatly improved Optimized cache module, SSD space can be used more efficiently, and memory usage is less then before Improve the efficiency of multi-users access to the same folder

## Slide 35
Increase the level of security
Support TLS 1.3 The admin account is disabled by default Advanced encryption suite support adjusted safety settings and more stronger safety protection options SSH Key login Firmware automatic updates (recommended updates, automatic updates) App automatic updates (recommended updates, automatic updates)

## Slide 36: TBS-464 v.s. TBS-453DX
Model | TBS-464 | TBS-453DX
CPU | Intel® Celeron® N5105/N5095 4-core/4-thread processor, burst up to 2.9 GHz | Intel® Celeron® J4115 4-core/4-thread processor, burst up to 2.5 GHz
M.2 slots | 4 x M.2 2280 NVMe Gen3 x2 slots | 4 x M.2 2280 SATA 6Gb/s slots
Ethernet ports | 2 x 2.5GbE | 1 x 10GbE 1 x 1GbE
HDMI output | 2 x HDMI (up to 2.0 resolution 3840 x 2160 @ 60Hz) | 1 x HDMI 2.0 (up to resolution 3840 x 2160 @ 60Hz)

## Slide 37
Copyright© 2021 QNAP Systems, Inc. All rights reserved. QNAP® and other names of QNAP Products are proprietary marks or registered trademarks of QNAP Systems, Inc. Other products and company names mentioned herein are trademarks of their respective holders.