## Slide 1
Click to Add Title

## Slide 2
 | QuCPE-7012-D2166NT-64GB | QuCPE-7012-D2146NT-32GB | QuCPE-7012-D2123IT-8GB | QuCPE-3034-C3758R-16G | QuCPE-3032-C3558R-8G
CPU | Intel Xeon D-2166NT 12 cores, 24 treads 2.0GHz (Max 3.0GHz) | Intel Xeon D-2146NT 8 cores, 16 treads 2.3GHz (Max 3.0GHz) | Intel Xeon D-2123IT 4 cores, 8 treads 2.2GHz (Max 3.0GHz) | Intel Atom C3758R 8 cores, 8 treads 2.4GHz | Intel Atom C3558R 4 cores, 4 treads 2.4GHz
Memory | 64GB DDR4 ECC (4x16GB) | 32GB DDR4 ECC (2x16GB) | 8GB DDR4 ECC (2x4GB) | 16GB DDR4 (2x8GB) | 8GB DDR4 (2x4GB)
Port | 10GbE SFP+ x4 2.5GbE RJ45 x8 | 10GbE SFP+ x4 2.5GbE RJ45 x8 | 10GbE SFP+ x4 2.5GbE RJ45 x8 | 10GbE SFP+ x4 2.5GbE RJ45 x8 | 10GbE SFP+ x2 2.5GbE RJ45 x8
Network Module | 1 | 1 | 1 | - | -
PCIe Slot | 1x PCIe Gen3 x8 | 1x PCIe Gen3 x8 | 1x PCIe Gen3 x8 | - | -
HDD Slot | 2x 2.5” SATA slots | 2x 2.5” SATA slots | 2x 2.5” SATA slots | - | -
M.2 SSD Slot | - | - | - | 2x 2280 M.2 MVMe | 2x 2280 M.2 MVMe
SR-IOV support | V | V | V | V | V

## Slide 3: Inside the QuCPE
Inside the QuCPE
Xeon D-2123IT
Xeon D-2146NT
Xeon D-2166NT
Intel® Xeon® D
Dual 300W Power (Main/Backup)
1 x PCIE Gen3 x 8 FH/HL
1 x Network module Expansion for 10GbE / 25GbE
8 x 2.5GbE RJ45 ports
8 x DDR4 Slots, up to 128GB (U-DIMM) & 256GB (R-DIMM)
2 x 2.5” slots Support SATA 6Gbps
4 x 10GbE SFP+ Fiber (SR-IOV supported)

## Slide 4: High speed expansion with Network module
 | PulM-10G4SF-XL710 | PulM-10G4SF-MLX | PulM-25G2SF-MLX
Speed | 10 GbE | 10 GbE | 25 GbE
Ports | 4 | 4 | 2
Interface | SFP+ | SFP+ | SFP28
Processor | Intel XL710 | Nvidia Mellanox ConnectX-4 | Nvidia Mellanox ConnectX-4
Bus | PCIe 3.0 x8 | PCIe 3.0 x8 | PCIe 3.0 x8

## Slide 5
What is SR-IOV?
With a smart NIC support SR-IOV. It allow the network adapter can be shared and direct attached to virtual environment. With PF (Physical function) and VF (Virtual function) supported. It give the possibility to VNF (virtual network function) to access the physical interface directly without non-essential packet process on host OS.
The result comes after is to increase the packets forwarding capability and reduce the CPU utilization on the host system.

## Slide 6
SR-IOV test Topology
QuCPE
VNF
NIC
NIC
NIC
NIC
Client-A
Client-C
Client-B
Client-D

## Slide 7: Packet Forwarding Flow
NIC
NIC
NIC
NIC
Linux-Kernel Forwarding Process
OVS
OVS
OVS
OVS
QNE OS
PCI-e
PCI-e
PCI-e
PCI-e
Hardware
Guest OS
V-NIC
V-NIC
V-NIC
V-NIC
VNF Forwarding Function
Driver
Driver
Driver
Driver
NIC
NIC
NIC
NIC
Linux-Kernel Forwarding Process
OVS
OVS
OVS
OVS
PCI-e
PCI-e
PCI-e
PCI-e
VF
VF
VF
VF
VNF Forwarding Function
PF
PF
PF
PF

## Slide 8: PF/VF
PF (Physical Function)
VF (Virtual Function)
With SR-IOV supported smart network adapter. A single PF (physical function) mapping to a single Ethernet port. Take an example on QuCPE 7012, build in 4 ports 10GbE SFP+ powered by Intel X722 Ethernet controller support 4 PF (physical function) by default. Can be expand up to 4 10GbE SFP+ and 4 PF (physical function) by additional expansion card.
VF (virtual function) functioning as a virtual NIC on virtual machine which allow virtual machine access to PF (physical function) directly through SR-IOV technology. A single PF (physical function) can map to multiple VF (virtual function) depending on Ethernet controller. Take an example on QuCPE 7012, with Intel X722 Ethernet controller. One single PF (physical function) can map to 32 VF (virtual function). But the total bandwidth still limited by physical link speed which is up to 10GbE (single direction) maximum for one single PF (physical function)
NIC
VNF Function
PCI-e
VNF Function
PF
VF
VF
VF
VF
User Space
Linux-Kernel Space

## Slide 9: Application Notes
Each of VF need to mapping to a PF. Which that means the SR-IOV cannot enable on the links between VNFs/VMs when a single chain topology are required as the diagram above. But the VF and virtual NIC can be enable on the same gust OS at the same time. The packets will be process as the diagram shown on the right in this case.
VNF Function
VNF Function
NIC
NIC
Linux-Kernel Forwarding Process
OVS
OVS
PCI-e
PCI-e
VF
V-NIC
V-NIC
VF
PF
PF
OVS
QuCPE
VNF
NIC
NIC
VNF
Notes: 每個VF必須對應到一個PF，也就是說當需要將多個不同的VNF串接再一起的時候(如下圖)，因為VNF與VNF中間的虛擬網卡並無直接對應到任何實體網卡，因此無法啟用SR-IOV在VM與VM中間的連線，但VF跟V-NIC可混和搭配使用在同一個VNF中，實際上的packet flow就會如右圖所示。

## Slide 11: Test Setup – without SR-IOV
NIC
NIC
NIC
NIC
Linux-Kernel Forwarding Process
OVS
OVS
OVS
OVS
PCI-e
PCI-e
PCI-e
PCI-e
V-NIC
V-NIC
V-NIC
V-NIC
VNF Forwarding Function
Driver
Driver
Driver
Driver
Client-A
Client-B
Client-C
Client-D
Linux
Virtual Switch 1
PFsence
Native Port 9
Native Port 10
Native Port 11
Native Port 12
System default Virtual Switch

## Slide 12: Test Setup – without SR-IOV
Client
  OS: QNE 1.0.3.q573
  Tool: Iperf 3.1.3
  Client-A: 192.168.61.1/24, connect to QuCPE 7012 port 9 (10GbE SFP+)
  Client-B: 192.168.62.1/24, connect to QuCPE 7012 port 10 (10GbE SFP+)
  Client-C: 192.168.63.1/24, connect to QuCPE 7012 port 11 (10GbE SFP+)
  Client-D: 192.168.64.1/24, connect to QuCPE 7012 port 12 (10GbE SFP+)
QuCPE-7012
  CPU: Intel Xeon-D 2146NT
  RAM: 32GB
  OS: QNE 1.0.3.573
Pfsense:
  CPU assign: Core 3-8 (Total 12 threads)
  RAM: 1G
  HDD: 100G
  Version: 2.6.0 Release
  WAN: DHCP from system default virtual switch for system update
  LAN: 192.168.60.254/24 to Virtual switch 1 (for pfsense Web GUI access)
  OPT1: 192.168.61.254/24, VirtIO to Native Port 9
  OPT2: 192.168.62.254/24, VirtIO to Native port 10
  OPT3: 192.168.63.254/24, VirtIO to Native port 11
  OPT4: 192.168.64.254/24, VirtIO to Native port 12
Client-A
Client-B
Client-C
Client-D
Linux
Virtual Switch 1
PFsence
Native Port 9
Native Port 10
Native Port 11
Native Port 12
System default Virtual Switch
Client
  OS: QNE 1.0.3.q573
  Tool: Iperf 3.1.3
  Client-A: 192.168.61.1/24, connect to QuCPE 7012 port 9 (10GbE SFP+)
  Client-B: 192.168.62.1/24, connect to QuCPE 7012 port 10 (10GbE SFP+)
  Client-C: 192.168.63.1/24, connect to QuCPE 7012 port 11 (10GbE SFP+)
  Client-D: 192.168.64.1/24, connect to QuCPE 7012 port 12 (10GbE SFP+)
QuCPE-7012
  CPU: Intel Xeon-D 2146NT
  RAM: 32GB
  OS: QNE 1.0.3.573
Pfsense:
  CPU assign: Core 3-8 (Total 12 threads)
  RAM: 1G
  HDD: 100G
  Version: 2.6.0 Release
  WAN: DHCP from system default virtual switch for system update
  LAN: 192.168.60.254/24 to Virtual switch 1 (for pfsense Web GUI access)
  OPT1: 192.168.61.254/24, VirtIO to Native Port 9
  OPT2: 192.168.62.254/24, VirtIO to Native port 10
  OPT3: 192.168.63.254/24, VirtIO to Native port 11
  OPT4: 192.168.64.254/24, VirtIO to Native port 12

## Slide 13: Test Setup – With SR-IOV
NIC
NIC
NIC
NIC
Linux-Kernel Forwarding Process
OVS
OVS
OVS
OVS
PCI-e
PCI-e
PCI-e
PCI-e
VF
VF
VF
VF
VNF Forwarding Function
PF
PF
PF
PF
Client-A
Client-B
Client-C
Client-D
Linux
Virtual Switch 1
PFsence
VF b7:02:0
(Native Port 9)
VF b7:06:0
(Native Port 10)
System default Virtual Switch
VF b7:0a:0
(Native Port 11)
VF b7:0e:0
(Native Port 12)
SR-IOV

## Slide 14: Test Setup – With SR-IOV
Test Setup – With SR-IOV
Client
  OS: QNE 1.0.3.q573
  Tool: Iperf 3.1.3
  Client-A: 192.168.61.1/24, connect to QuCPE 7012 port 9 (10GbE SFP+)
  Client-B: 192.168.62.1/24, connect to QuCPE 7012 port 10 (10GbE SFP+)
  Client-C: 192.168.63.1/24, connect to QuCPE 7012 port 11 (10GbE SFP+)
  Client-D: 192.168.64.1/24, connect to QuCPE 7012 port 12 (10GbE SFP+)
QuCPE-7012
  CPU: Intel Xeon-D 2146NT
  RAM: 32GB
  OS: QNE 1.0.3.573
Pfsense
  CPU assign: Core 3-8 (Total 12 threads)
  RAM: 1G
  HDD: 100G
  Version: 2.6.0 Release
  WAN: DHCP from system default virtual switch for system update
  LAN: 192.168.60.254/24 to Virtual switch 1 (for pfsense Web GUI access)
  OPT1: 192.168.61.254/24, connect to port 9 with SR-IOV VF
  OPT2: 192.168.62.254/24, connect to port 10 with SR-IOV VF
  OPT3: 192.168.63.254/24, connect to port 11 with SR-IOV VF
  OPT4: 192.168.64.254/24, connect to port 12 with SR-IOV VF
Client-A
Client-B
Client-C
Client-D
Linux
Virtual Switch 1
PFsence
VF b7:02:0
(Native Port 9)
VF b7:06:0
(Native Port 10)
System default Virtual Switch
VF b7:0a:0
(Native Port 11)
VF b7:0e:0
(Native Port 12)
SR-IOV

## Slide 15
Copyright© 2022 QNAP Systems, Inc. All rights reserved. QNAP® and other names of QNAP Products are proprietary marks or registered trademarks of QNAP Systems, Inc. Other products and company names mentioned herein are trademarks of their respective holders.​​​​​​​
is your best choice