## Slide 1: TS-h1655XeU-RP
2025/08
3U 12 x 3.5" HDD & 4 x E1.S/M.2 NVMe SSD Hybrid Short-Depth 12-inch Rackmount NAS with Intel Atom® 8-Core 2.8GHz Processor

## Slide 2
Space Efficiency
Short racks offer a compact solution, making them ideal for environments where space is limited, such as small offices or studio settings.
Adapting server solutions: The rise of short racks for diverse needs
Flexibility
They provide the necessary infrastructure without occupying excessive floor area, accommodating various types of equipment in constrained spaces.
Cost-Effective
By reducing the amount of physical space needed, short racks can also help lower setup and operational costs
In today's fast-paced tech landscape, traditional server rooms and data centers often come with significant space and design constraints. In recent years, manufacturers such as Supermicro, ASRock, Dell... and more have also been continuously releasing short-depth server products.

## Slide 3
Network Cabinets/Racks
Media studios, campuses, or small offices can conveniently store short-depth NAS along with network devices in compact cabinets.
(The rails can only be secured if the back of the cabinets can be opened.)
Perfect for space-limited edge environments
Wall-mounted Network Cabinets
In limited space environments like laboratories or factories, short-depth NAS can be placed in wall-mounted cabinets close to computers or servers, facilitating easier access.
Server Racks
Short-depth NAS can also be placed inside standard server racks in the server room, with the saved space used for cable management.

## Slide 4
Power buttonexpansion
LED Indicators:
System status, network, USB
The chassis depth has been reduced to 12 inches
Compared with 3U rackmount NAS in the market
Reduced by 50%+

## Slide 5
Powered by Intel Atom® 8-core processor, 12-inch short-depth rackmount NAS
Maximum 64 GB Memory
Pre-installed 1 x 8G DDR4 SODIMM RAM, support up to 64GB memory (2 x 32GB).
Also support ECC memory
Intel 8-core CPU
Powered by Intel Atom C5125 8-core processor 2.8GHz, providing powerful performance
12-inch short-depth rackmount NAS
30-cm / 12-inch short chassis supports most of the cabinet on the market
4 x E1.S PCIe Gen3 x2 (pre-installed M.2 adapter) slots
Provides 4 x E1.S SSD slots, supporting up to 15mm E1.S. Also comes standard with M.2 adapter to support M.2 2280 NVMe SSD
1 x 10GBASE-T &
2 x 2.5GbE Multi-Gig LAN Ports
Sufficient network bandwidth provides smooth data transmission experience
Dual PCIe Gen3 x4 slots
Provide a variety of expansions including 5/10/25GbE network card, M.2, HBA and other expansion cards
Core
8
DDR4

## Slide 6
Power button
LED Indicators:
System status, network, USB expansion
12 x 3.5-inch/2.5-inch SATA 6Gb/s HDD/SSD bays
TS-h1655XeU-RP front views
Air Intake holes

## Slide 7
TS-h1655XeU-RP rear views
2 x 2.5G RJ45 ports
2 x PCIe Gen3 x4 slots
slot 1 & slot 2 77 x 20 x 220 mm ( H x W x D)
K-Lock
4 x E1.S / M.2 2280 PCIe Gen3 x2 slots, support NVMe SSDs, or 10GBASE-T network port through QXG-ES10G1T accessory
2 x USB 3.2 Gen 1
1 x 10GBASE-T
2 x 300W PSU

## Slide 8
Enhance SSD caching
Install E1.S / M.2 PCIe NVMe drives for SSD caching to accelerate random read/write efficiency (IOPS) and reduce latency, especially beneficial for handling numerous small files.*
Setup SSD high-speed storage pool
Create a data storage pool with E1.S / M.2 PCIe NVMe SSDs to expedite intensive data transfers and access efficiency.
Upgrade to 10GbE high-speed connectivity
Install the QXG-ES10G1T 10GbE network module for immediate access to faster connection capabilities. (Additional purchase)
*​Note :
Installing a 5.9mm E1.S SSD, please remove the built-in E1.S to M.2 adapter in the slot.
Installing a 9.5/15mm E1.S SSD, a QNAP tray TRAY-E1S-01 is required.
Powerful expansion with E1.S / M.2 PCIe NVMe slots

## Slide 9
Remove the M.2 SSD adapter.
Attach the screws that secure the drive to the tray frame.
Place the drive on the TRAY-E1S-01 tray base so that the holes on the drive align with the holes on the tray base.
Then attach the screws that secure the drive to the tray base.
Insert and tighten the tray into the bay
Installing E1.S solid-state drives into TS-h1655XeU-RP
Installing 5.9 mm E1.S solid-state drives​
Installing 9.5 mm and 15 mm E1.S solid-state drives

## Slide 10: QXG-ES10G1T, upgrade your NAS to 10GbE with E1.S slots (Additional purchase required)
Multi-Gig 10GBASE-T Network adapter
Support 10G/5G/2.5G/1G/100M network connectivity.
QXG-ES10G1T

## Slide 11: Supports ECC memory (Error Correcting Code)
TS-h1655XeU-RP supports ECC memory, automatically detecting and timely correcting single-bit errors
System supports up to 64GB ( 2 x 32GB) memory
Reliable memory and avoiding data corruption
The NAS is pre-installed with a 8GB DDR4 SO-DIMM non-ECC memory by default.
ECC memory and non-ECC memory modules cannot be installed together

## Slide 12: Replacing TS-h1655XeU-RP DDR4-SODIMM RAM
Push the retention clips outward simultaneously to release the module.
Then carefully slide the module out of the slot.
Verify that the metal connectors are completely inserted into the slot.
Then press down on the module until the retention clips lock the module into place.
1.
2.
3.

## Slide 13: Integrated 2 x 2.5 GbE and 1 x 10GBASE-T, expand to 4 x 25GbE via QNAP PCIe network interface cards
2 x 2.5 SMB Sequential Throughput (1MB)
4 x 25 GbE SMB Sequential Throughput , 3 Host (1MB)
Write
Read
Write
Read
Environment: NAS | TS-h1655XeU-RP, Hero h5.2.4, 12 x Samsung 870 EVO 1TB, RAID 5, thick volume
PC | 3 host with QNAP QXG-25G2SF-CX4, 32G RAM, Windows Server 2019
IOmeter : RAM*4, 30-sec ramp up time, 3-min seq. run time, 1 workers, 32-outstanding
Tested in QNAP Labs. Figures may vary by environment.
(MB/s)
0
200
400
591 MB/s
588 MB/s
2,552 MB/s
4,926 MB/s
600
2000
2500
3000
3500
4000
4500
5000

## Slide 14
Comprehensive 12-inch(30cm) Short-Depth Solution
High-capacity storage architecture in a limited space. QNAP launches a 3U dual-power solution with a depth of only 30 cm — a model that competitors cannot offer.
 | TS-h1655XeU-RP-8G | TS-855eU-RP | RS1221+
CPU | Intel ® Atom® C5125 8-core processor, 2.8GHz | Intel ® Atom® C5125 8-core processor, 2.8GHz | AMD Ryzen V1500B 4-core 2.2 GHz
Memory | 8 GB non-ECC SODIMM DDR4 (1 x 8 GB) | 8 GB non-ECC SODIMM DDR4 (1 x 8 GB) | 4 GB DDR4 ECC UDIMM
Max. Memory | 64 GB (2 x 32 GB) | 64 GB (2 x 32 GB) | 32 GB (16 GB x 2)
Drive | 12 x 3.5” SATA 6Gb/s + 4 x E1.S/M.2 | 8 x 3.5” SATA 6Gb/s | 8 x 3.5” SATA 6Gb/s
M.2 | (4 x E1.S/M.2) | 2 x M.2 2280 (PCIe Gen 3 x 4) | -
GbE | - | - | 4 x 1GbE
2.5 GbE | 2 | 2 | -
10 GbE | 1 x 10GBASE-T | - | -
PCIe | 2 x PCIe Gen 3 x4 | 2 x PCIe Gen3 x4 | 1 x PCIe Gen3 x8
USB | 2 x USB 3.2 Gen 1 | 4 x USB3.2 Gen 1 | 2 x USB3.2 Gen 1
PSU | 2 x 300W Redundant PSU | 2 x 300W Redundant PSU | 1 x 250W PSU
Dimensions (H x W x D) | 3U Short-depth 133 mm x 432.4 mm x 296 mm | 2U Short-depth 88.6 mm x 432 mm x 296 mm | 2U Short-depth 88 mm x 482 mm x 306 mm

## Slide 15
Rail Kit :
NAS installation and maintenance made convenient
Rail-S01
Mounting post depth: 5" ~ 16.3" / 126 ~ 415 mm
RAIL-B02 (normal rail kits)
Mounting post depth: 18” ~ 32”/ 443 ~ 815 mm
Cannot setup in small cabinet
5" ~ 16.3" / 126 ~ 415 mm
RAIL-B02
RAIL-S01
18” ~ 32”/ 443 ~ 815 mm
Whether for compact racks or standard racks,
QNAP offers corresponding rail kits to choose from.

## Slide 16
TS-h1655XeU-RP is shipped with the QuTS hero operating system, which has powerful data transmission performance and more efficient memory usage, and WORM. You can also change to the QTS operating system according to your needs
 | QuTS hero | QTS
File system | ZFS | Ext4
SSD cache | Read Cache | Read/Write Cache Read Cache Write Cache
Inline Compression | Yes (LZ4 compression, ideal for RAW files and document files) | No
Inline Deduplication | Yes (At least 16 GB RAM required) | No
HBS with QuDedup for Remote Backup | Yes | Yes
Power Failure Protection (Software) | ZIL Copy-on-Write | No
Permission Management | Rich ACL (14 types) | POSIX ACLs (3 types) + certain special permissions
Capacity Expansion | Upgrade RAID capacity Change higher capacity disk drives Attach expansion enclosures/JBODs | Add a disk drive to a RAID group Upgrade RAID capacity Change higher capacity disk drives Attach expansion enclosures/JBODs
Data Security | Better (Self-Healing & Copy-on-Write) | Standard
Recommendation SSD Configuration for Video Editing Applications | Use SSD Pools Note: Set the block size 128K when creating Folders/LUNs | Editing (from original/RAW files): Use SSD Pools Post production: Enable Read/Write cache Note: Set the block size to 32K or 64K when creating Volumes, and choose “All I/O” for cache mode.
Choose between QTS and ZFS based QuTS hero

## Slide 17: WORM (Write Once Read Many times)
WORM is used to avoid modification of saved data. Once this feature is enabled, data in shared folders can only be read and cannot be deleted or modified to ensure data integrity.
Enterprise Mode
remove the shared folder through QuTS hero UI or SSH commands (QCLI).
Compliance Mode
Have to take the Storage Pool offline and remove the Pool if want to destroy data.

## Slide 18
Value-Added solutions for short-depth NAS
HybridMount
Allows users to integrate cloud storage into the NAS system, enabling seamless collaboration between cloud and local storage.
VJBOD (Virtual JBOD)
Allows users to use other QNAP storage devices as virtual drives, extending the storage capacity
myQNAPcloud Storage
QNAP-Hosted cloud storage. Free 16GB storage space available for NAS data backup

## Slide 19
Build a comprehensive surveillance system with a TS-h1655XeU-RP, QVR Pro/Elite, and IP cameras
QVR Pro
6,000+ Compatible cameras
8 embedded monitoring channels
expand up to 128 channels by purchasing QVR Pro licenses*
View USB camera images through QUSBCam2
QVR Pro Client
iOS & Android mobile devices
Support cross-platform ： Windows, Mac, Ubuntu
Use HDMI output and USB keyboard and mouse to control the NAS through installing Graphic card
*The maximum number of channels supported varies by NAS model, network configuration, and camera settings
The flexible subscription QVR Elite can be expanded to a maximum of 192 channels by purchasing licenses*​
QVR Elite

## Slide 20: 1-year+ of continuous surveillance recording storage with 288TB raw capacity in 1 single NAS
8 channels, footage preserved for 365+ days
8 cameras; reserved for 365 days; 1920x1080(h.264/medium quality;30FPS); total 182TB required
24TB x 12 = 288TB raw capacity
QVR Pro
8-channel included
Support up to 128ch*
*The maximum number of channels supported varies by NAS model, network configuration, and camera settings

## Slide 21
Container Station
Virtualization Station
Smart and automatic file management​
Virtualization Station is a fast and reliable hypervisor on QNAP NAS and appliances. You can run multiple virtual machines on Virtualization Station to meet versatile virtualization needs.
Experience LXD and Docker® lightweight virtualization technologies, download apps from the Docker Hub Registry®, import/export containers, and create abundant microservices.
The brand new UI
Recreate containers with ease
Save the frequently used container commands for efficiency
Upload Image and YAML files from cloud or local devices
Multiple network modes

## Slide 22: Snapshots help you fight with Ransomware Threats​
Mitigate the growing threat of ransomware
TS-h1655XeU-RP supports Snapshot , like taking a photo - within seconds the complete status of your NAS system and data is recorded
Step 1 ​ Regularly update, and use Malware Remover​
Step 2​ Routinely back up to your NAS, and create multi-version snapshots​
Step 3​ Back up snapshots to another QNAP NAS​

## Slide 23
All the files and folders stored on your NAS and connected storage spaces are accessible through a familiar interface, and rich search/sort functions are available to help find files.​
File Station : Easy to use, easy to find​
“Recently” sections
Search bar
File Station displays files that have been recently uploaded, accessed, and deleted in the left panel, allowing you to quickly find desired files.
The full-text search engine Qsirch is now supported! You can find files by filename and text in documents.

## Slide 24
Qfiling
Automatically filing and archiving​
Qsirch
The AI-powered search engine for your NAS
Smart and automatic file management​
RAG Search
AI Semantic Search​
Keyword Search
BETA
Using an intuitive interface, you can easily switch between general search (Keyword / AI semanticA search) or RAG search to quickly find files stored on your NAS and gain an advanced data analysis experience.
Source
Schedule
Filter
Edit
Destination
2 type of task: filing task, recycling task​
3 type of scheduling rule: one-time, scheduling, real-time​
9 editing module: AI face blur, encryption and decryption, video transcoding and so on​

## Slide 25
NAS off-site
3 copies
Easy to use HBS fulfilling backup 3-2-1 practice with deduplication
Complete 3-2-1 backup strategy and recovery plan: 3 copies、2 media type、1 remote backup​
HBS (Hybrid Backup Sync)
NAS
Google Drive
2 media type
Copy 2
Copy 1
Copy 3

## Slide 26
Safeguard business data against ransomware.
Airgap+.
Secure NAS data with air-gapped network isolation for backups
QNAP’s next-generation Airgap+ feature uses a logically isolated network to achieve efficient, convenient, and secure backups for enterprises and the media and entertainment (M&E) industry.

## Slide 27: Qsync : Easily Backup or sync files and folders
Qsync is more than just a sync tool — it also lets you back up files on Windows® / Mac® computers to your NAS, ensuring your data is always safe
Worry-free backup for data security
Real-time sync, Always up-to-date files

## Slide 28
Malware Remover
Regularly scan your NAS using the latest malware definitions. When under attack, infected files will be immediately removed to ensure NAS data security.
QuFirewall
You can allow/deny IP addresses and regions to prevent unauthorized access and brute force attacks for safeguarding data and service security.
Data security​​

## Slide 29
TS-h1655XeU-RP is backed by a 3-year warranty at no additional cost. ​​
You can also purchase a warranty extension that extends your warranty coverage up to 5 years total​. (P/N: LIC-NAS-EXTW-BROWN-2Y-EI )
3-year standard warranty covering hardware repair and support services​

## Slide 30
C5125 2.8GHz
8-Core
Processor
2.5GbE
Up to
64GB DDR4 RAM
IntelQAT
3個
PCIe Gen3 x4
擴充槽
Supports both
USB 3.2 Gen2 (10Gbps)
與 One-Touch-Copy
4 x 25GbE
SMB Throughput 1MB, 3 Host
Support 10GBASE-T NIC,
QXG-ES10G1T
2.5GbE X2
TS-h1655XeU-RP
Short-depth 12-inch
4 x E1.S NVMe SSD slots, supporting up to 15mm E1.S, and pre-installed adapter to support M.2 2280 NVMe SSD
ECC memory can also be installed
Up to
5-year
warranty​
WORM Support in QuTS hero (Write Once Read Many times)​
4 x M.2 2280
Up to 4 x M.2 2280 NVMe SSD, Support hot-swapping
10GBASE-T
USB 3.2 Gen 1 port
Write : 2,552 MB/s
Read : 4,926 MB/s
Support QNAP E1.S SSD

## Slide 31: TS-h1655XeU-RP
2025/08
3U 12 x 3.5" HDD & 4 x E1.S/M.2 NVMe SSD Hybrid Short-Depth 12-inch Rackmount NAS with Intel Atom® 8-Core 2.8GHz Processor