## Slide 1: Design Concepts & Capacity Expansions of QNAP RAID 50/60

## Slide 2: Your challenges, our solutions: Insufficient protection of RAID 5? Will performance be degraded when using RAID 50/60?

## Slide 3: Why You Should Use RAID 50/60
Number of disks and their capacities will affect RAID protection level
With ServeTheHome RAID Calculator:
The failing rate of RAID 5/6 in 5 years:
Disk NO. | RAID Type | Disk Capacity | RAID Failing Rate
4 | RAID 5 | 8 TB | 0.07%
8 | RAID 5 | 8 TB | 0.77%
8 | RAID 6 | 8 TB | 0.001%
12 | RAID 6 | 8 TB | 0.01%
24 | RAID 6 | 8 TB | 0.64%
https://www.servethehome.com/raid-calculator/ Best Estimate Real World assuming bit error chance is 10^(-15), 150MB/sec rebuild speed
RAID 5/6 protection can be degraded when NAS capacity increases.

## Slide 4: Better Protection with RAID 50/60
Protect your data with Lower space redundancy
On NAS with 8 bays, QNAP no longer recommends using RAID5
For enterprise models, RAND 6/RAID 10/RAID 60 is recommended:
Take 8TB disks as example:
RAID type | No. of disks | Disk failure tolerance | Raw capacity | RAID failing rate
RAID 6 | 24 | 2 | 176 TB | 0.64%
QNAP RAID 60 | 24 | 4 or more | 160 TB | 0.03%
RAID 10 | 24 | 12 | 96 TB | 0.02%

## Slide 5: QNAP RAID 50/60 Design Concepts
Supported by NAS with 6 or more bays
Supports Storage Pool, Static Volume and Qtier Pool
Stripping Data Block to create RAID 50/60
RAID 50 Storage Pool
A1
A2
B1
B2
C1
C2
RAID 5 #1
RAID 5 #2
Disk 1
Disk 2
Disk 3
Disk 4
Disk 5
Disk 6
RAID 5
Disk 1
Disk 2
Disk 3
Disk 4
Disk 5
RAID 5 Storage Pool
A
B
C

## Slide 6: When expanding, new sub-arrays are not allowed
Number of RAID 50/60 Sub-arrays cannot be changed after creation
No. of disks in Sub-arrays must be equal to avoid space waste
Capacity can be expanded through new RAID 50/60 and JBOD (Liner)
RAID 50 Storage Pool
RAID 5 (1-1)
RAID 5 (1-2)
RAID 5 (2-1)
RAID 5 (2-2)
Liner

## Slide 7: Concept of RAID 50 "Write" Operation
RAID 5 (1-1)
1. Data Block A is striped into A1/A2 for writing operation
2. A1/A2 then are striped again within each sub-array
RAID 5 RMW (Read Modify Write) １Write =
Read Parity+ Read Data + Calculate Parity+ Write Parity+ Write Data
A1
A2
RAID 5 (1-2)
A1*
A1”
P
Disk1
Disk2
Disk3
Disk4
Disk5
Disk6
B1
B2
P
B1*
B1”
C1
C2
C1*
P
C1”
RCW (Read Reconstruct Write) = Read all Chunk Data + Calculate Parity + Write Parity + Write Data
A2*
A2”
P
P
B2*
B2”
C2*
P
C2”

## Slide 8: Performance Comparison For RAID 50/60
Single RAID 0 = Performance can be N (No. of disks)* P (Disk performance)
Single RAID 5 = (N*P) / RMW or RCW operations
Compare RAID 50/60 to RAID 5/6 on HDD, performance can be reduced
HDD : TS-1079 (6) TVS-EC2480U-SAS-RP R2 (12) Seagate ST1000NM0033 through SMB
SSD : TVS-EC2480U-SAS-RP R2 (12 /24) ST200FM0053(SAS) through iSCSI iSER https://www.storagecraft.com/blog/raid-performance/
No. of disks (HDD) | RAID type | Sequential read | Sequential write | No. of disks (SSD) | RAID type | Sequential read | Sequential write
6 | RAID 5 | 687 | 370 | 12 | RAID 5 | 3098 | 1904
6 | RAID 50 (2) | 566 | 305 | 12 | RAID 50(2) | 3092 | 1859
12 | RAID 5 | 1563 | 853 | 24 | RAID 6 | 4606 | 4481
12 | RAID 50 (2) | 1536 | 858 | 24 | RAID 60 (2) | 4607 | 4422

## Slide 9: Performance With RAID 50/60 (HDD)
The random read/write performance for RAID 50/60 can reduce 10% when the RAID is consisted of HDD with more read head operations
RAID 50/60 on HDD is priority for data protection
RAID performance calculating: https://www.storagecraft.com/blog/raid-performance/
No. of disks | RAID type | Disk capacity | RAID failing rate
12 | RAID 5 | 8TB | 2.82%
12 | RAID 50 | 8TB | 0.29%
A RAID 50 can greatly increase RAID protection with little performance impact
RW 4KB
RR 4KB
SR 4KB
SW 4KB
RAID 50 (2 sub-arrays)
RAID 5
RAID 50 (2 sub-arrays)
RAID 5

## Slide 10: Why random RW performance is increased with RAID 50/60 (SSD)
RAID 5-2
A2*
A2’’
P
RAID 5-1
RAID 50/60 with SSD will not suffer from read head operations penalty
With SSD RAID 50, Random Read and Write has increased
Suitable for all flash applications
RAID 50 Storage Pool
A1
A2
A1*
Disk1
Disk2
Disk3
Disk4
Disk5
Disk6
300%↑
Random write
A1’’
P
A1
A2
A1
A2
SW 4KB
SR 4KB
RAID 50 (2 sub-arrays)
RAID 5

## Slide 11: QNAP RAID 50/60 Use Case Suggestion
RAID 50/60 Value: Ensure Protection Level for High Capacity NAS
General Application: RAID 5 is not recommended, 6-14 Bays: RAID 6/10,
Beyond 16 Bays: RAID 60 With SSD Cache
Backup Destination: RAID 50 for NAS higher than 8 bays
RAID Type | RAID 5 | RAID 6 | RAID 10 | RAID 50 | RAID 60
Disk No. Requirement | > 3 | > 4 | > 4 | > 6 | > 8
Disk Fail Tolerance | 1 | 2 | half | 2~5 | 4~10
Capacity | ★★★★ | ★★★ | ★ | ★★★ | ★★
Scenario | Backup | General Usage | VDI or Database | High-Frequency Backup | VDI and Video Editing
Using 8TB disk with 16 bays NAS, RAID 6 5 years failing rate will beyond 0.1%

## Slide 12: How to expand QNAP RAID 50/60?

## Slide 13: Add Disks to All Sub-arrays
In Storage Management select "Expand"
Using dedicated UI to add disk on all sub-arrays at once

## Slide 14: Add new RAID Group for Expansion
Add a new RAID 50/60 with same sub-array count for expansion
Using Expansion Enclosure if Host NAS has no free slots
The new RAID 50/60 must use same RAID type and sub-arrays count (Disk number can be different)
TS-EC2480U
REXP-1600U-RP

## Slide 15: Demo：Expand RAID 50/60 By Adding Disks

## Slide 16: Use RAID 50/60 With Hot Spare
Local and Global Hot Spare can be used for each or all sub-arrays
It is recommended to reserve Global Hot Spare
Create RAID > go to "Disks/VJBOD" and set free disk as spare
Global Spare
RAID 50/60 Pool

## Slide 17: Using Qtier/SSD Cache with RAID50/60
SSD RAID 60 = High capacity/performance video editing server
SSD Cache RAID 10 + HDD RAID 60 = High capacity/performance file server
Qtier SSD RAID 50 + HDD RAID 60 = High capacity/performance VDI server
Qtier SSD RAID 10 + HDD RAID 60 = High capacity/performance Database
QNAP IOAware Qtier + RAID 50 pool
RAID 5 (1-1)
RAID 6
(2-1)
RAID 6
(2-2)
RAID 5 (1-2)

## Slide 18: Thanks for listening