## Slide 2: Your Challenges, Our Solutions: Storage budget is limited, but data growth is not! How to expand storage capacity?

## Slide 3: Why NAS Expansion Important
As your company grows, IT managers will need a solid plan to ensure continued operation
When purchasing NAS with 8+ bays, about 50% of SMBs choose not to fill all bays initially
Primary considerations are budget and flexibility

## Slide 4: QNAP NAS Road to Expansion
Replace disks and system migration
Add new disks to migrate RAID type
Add new disks to expand RAID or upgrade to Qtier
Connect expansion unit or external storage
Use iSCSI VJBOD to share NAS space
RAID 1
RAID 5/6
RAID Expansion
NAS+JBOD
NAS+VJBOD

## Slide 5: NAS grows as your applications expand
Scenario : Mike is a YouTuber and he always stores his materials in the TS-228A. With his followers increasing, he now needs a NAS with more storage to keep more video…
Challenge:
How to expand a 2-bay NAS?
Solution:
Replace Disks One by One, System Migration

## Slide 6: Replace Disk One By One
When planning for expansion, technology advancements need to be evaluated.
Source: https://www.backblaze.com/blog/hard-drive-cost-per-gigabyte/
Disk capacity/price ratio drops year over year
Mainstream size from 2 TB in 2010 to 8 TB now
QNAP NAS RAID 1/5/6/10 support replacing
disk on line

## Slide 7: 3 Steps to Replace Disks
“Replace disk one by one” only supports replacing smaller disk with larger disk
Prepare new disks with the same number as the NAS’s RAID group
Storage & Snapshot > Storage/Snapshot > Manage Storage Pool > Select a RAID Group > Manage > Select “Replace disk one by one”
Following wizard guide to unplug, plug in and sync disk one by one
Use “Priority “ to increase
disk re-sync speed

## Slide 8: System Migration With RAID Auto Re-Ordering
RAID order can be auto detected : No need to worry if plug in the disk with a wrong order
Settings
On QNAP NAS, system configurations will be backed up to disks
When purchasing new NAS, the system settings can be migrated with disk directly
Data

## Slide 9: 3 Steps to Migrate System
System migration may not support migrating NAS from an enterprise model back to an entry one. For details please visit: http://docs.qnap.com/nas/4.3/cat2/en/index.html?system_migration.htm
Initialize new NAS and upgrade to the latest QTS version
Shutdown both NAS and plug original disks into new NAS
Power on new NAS and start QTS

## Slide 10: Advanced Tip: Safety Detach Storage Pool
For non-system volume and storage pool, the space & disk can be safely detached and roaming between NAS
Storage/Snapshot> Storage Pool manage
> Remove > Safely Detach
Remove and plug in disks to new NAS
Storage & Snapshot > Disk/VJBOD
> Recover > Scan all free drives

## Slide 11: Start expanding from only 1 disk
Solution:
Challenge: How to expand a single disk to benefit from RAID protection?
RAID Migration
With method based on “Reshape”
RAID 1 > RAID 5 > RAID 6
Single >

## Slide 12: RAID Migration
Disk
Disk
Disk
Disk
Disk
Disk
Disk
Disk
QTS 4.3.4: Using RAID Reshape to ensure 4 disks can all be used when read data
DSM 6.2: Using RAID Recover for faster migration but the newly added disk will not be used when reading data
D
P1
D
D
D
P1
P1
D
D
P2
P2
P2
D
P2
P1
D
D
P2
P1
D
D
P2
P1
D
The actual performance may differ based on NAS models. RAID 50 /60 do not support direct RAID migration
Supports migrating Single > RAID 1 > RAID 5 > RAID 6
Using Linux RAID Reshape: Requiring longer time to re-sync every disk to ensure post-migration performance

## Slide 13: 3 Steps to Migrate a RAID
Plug in new disks into the NAS
Storage/Snapshot> Pool Management> RAID Manage> Migrate
Follow the wizard to select new disk for migration

## Slide 14
Demo: Use QNAP NAS to perform RAID migration

## Slide 15: Advanced Tip: RAID 1 Parallel Read
D
D
D
M
M
M
D
D
M
M
M
Normal RAID 1
QNAP RAID1 with Parallel Read
D
M
D
D
M
SSD RAID 1 Sequential Read Increase 50%
HDD RAID 1 Sequential Read Increase 10%
The actual performance may differ based on NAS models
QNAP RAID 1 support read data from both disks at the same time
Apart from normal RAID 1, performance can be
boosted even when migrate from Single to RAID 1

## Slide 16: Advanced Tip: move to RAID 50/60 from 5/6
A1
A2
B1
B2
C1
C2
RAID 5 #1
RAID 5 #2
Disk
Disk
Disk
Disk
Disk
Disk
QNAP RAID 50/60 sub-array can only be set up when creating storage pool
To move to RAID 50/60 from 5/6, purchase NAS with doubled bays
Create RAID 50/60 with minimum disks (6/8) and copy data to it
Finally, add old disks to new sub-arrays
RAID 50 Storage Pool

## Slide 17: Bigger Capacity Comes Greater Responsibility
Add new disks to the RAID group
Challenges:
Scenario: Mike has finished system and RAID migration, but the requirement of
capacity, performance and protection also increase as his channel grows
How to increase capacity, performance and protection with the same RAID configuration?
Solutions:
Upgrade to Qtier Pool (With optional QM2 expansion card)
Setup hot spare disk

## Slide 18: RAID 5/6/50/60 Add Disk
RAID 6
Half # of empty bays for RAID 60 expansion
Best-practice under limited budget: load half # of bays first for future 50/60 expansion
RAID 5/6/50/60 support online RAID expansion
RAID 50/60 has dedicated UI to add disks to all sub-arrays at once

## Slide 19: Replace SSD Cache with Qtier 2.0
Application
SSD
HDD
Qtier 2.0 Auto Tiering
The cache space cannot be used as data storage
SSD Cache
The SSD can be used to store hot data directly, resulting to higher ROI from purchased SSD
Cold Data
Hot Data
SSD Cache
Qtier 2.0

## Slide 20: Use QM2 to upgrade to Qtier
QM2 SSD RAID
QM2 Support TS-x31X, 53B and above (with PCIe expansion slots)
QM2 also has T sensor and heat sink to ensure disk health
NAS can be expanded with 2 additional M.2 SSD slots

## Slide 21: 3 Steps to expand RAID group
RAID expansion can be conducted online, while upgrading to Qtier temporarily suspends services to move metadata to SSD
Follow the wizard to select new disks
Insert new disks into NAS
Storage/Snapshot > Storage Pool Management >
Expand Storage Pool > Expand or Upgrade to Qtier

## Slide 22: Add hot spare disks for additional protection
Global
Hot Spare
Hot Spare: When a disk in the RAID becomes unavailable, system
will auto use hot spare disk to replace the faulty disk
RAID 1/5/6/10 support local hot spare
With multiple RAID or RAID 50/60, global hot spare is also supported
RAID 50/60 Pool

## Slide 23: 3 steps to configure hot spare
Insert new disks into NAS
Storage/Snapshot > Storage Pool Management > RAID Group
> Manage >Set Hot Spare
Disk/VJBOD
> Select a free disk
> Action
> Set as Spare

## Slide 24: Add JBOD if one NAS is not enough
Scenario: As Mike's YouTuber career soars, he now needs a storage to
back up and archive data.
Challenge:
When RAID cannot be expanded further, how to expand?
Use USB/SAS/Thunderbolt JBOD
Use USB 3.1/Thunderbolt External Storage
Solutions:

## Slide 25: QNAP Expansion Units
Interface | USB 3.0 (UX) | SAS (REXP) | Thunderbolt 2 (TX)
Major Use for | Tower NAS | Rackmount NAS | Thunderbolt NAS
Maximum Slots | 12 (UX-1200U-RP) | 16 (REXP-1620U-RP) | 8 (TX-800P)
Theory Speed | 5Gb/s | 12Gb/s or 6Gb/s | 20Gb/s
Connection Method | Direct Connect | Direct Connect/Daisy Chain | Direct Connect/Daisy Chain
Scenario | File server expansion or archiving storage | Deploy high capacity storage from the start | Deploy high capacity video editing server
To connect REXP-1620U-RP to 6Gb/s SAS NAS or other 6Gb/s SAS expansion unit, additional 12Gb/s to 6Gb/s converter is required.
Daisy Chain: Connect a JBOD to another JBOD that is already connected to host, so the maximum connection count will not limited to # of physical interfaces of host

## Slide 26: Linear expansion or new storage pool
When using expansion unit as backup or archiving server, new storage pool is recommended
Liner: Combine New RAID with existing RAID
Drawback >Any failed RAID will affect entire storage
New Storage Pool: Independent expansion units can roam between NAS

## Slide 27: 3 Tips to manage expansion units
Chain 2
Chain 1
SAS-12G2E expansion card and mini SAS cable info:
http://shop.qnap.com/index.php?route=product/category&path=35_430
Multiple daisy chains
decrease the chance of storage
being affected by abnormal
connection.
When expanding, use SAS expansion cards for higher performance
Expand as a new storage pool
Use multiple daisy chains and add
new expansion units in turns

## Slide 28: Advanced Tip: USB 3.1 external storage
External device: SanDisk Extreme 900, USB 3.1 Gen 2 Type C; CP command used for testing
QNAP NAS support USB 3.1 Gen 2 Type A dual port USB-U31A2P01 expansion card
QTS4.3.4 TVS-882ST3 with USB 3.1 Gen 2 Sequential Write is faster than RS-3614RPxs USB 3.0 for 25%

## Slide 29: Advanced Tip: Thunderbolt 3 is compatible with USB 3.1 Gen 2
To use QNAP Thunderbolt™ 3 NAS with Thunderbolt™ 2 expansion device, Thunderbolt 3 (USB-C) to Thunderbolt 2 converter is required
Mount TVS-882ST3’s SanDisk Extreme 900 from Windows can reach 700MB/s (with NAS cache)
Thunderbolt3 and USB 3.1 Type C port are the
same, with lighting mark as Thunderbolt supported
Thunderbolt 3 port on supported models support both Thunderbolt & USB 3.1 Type C external storage device, with speed of USB 3.1 Gen2
From windows write data to external disk on NAS
MB/s
Sequential Write
Sequential Read

## Slide 30: Multiple NAS can work together
Scenario: Mike is now a famous YouTuber and works with others in a studio. He finds not all space on every NAS is fully utilized
Challenge
How to share space on
multiple NAS?
Solution
iSCSI Initiator
QNAP Virtual JBOD
TVS-882
REXP-1220U-RP#1
TS-1263U-RP

## Slide 31: Use iSCSI initiator to mount different storage devices
The trademarks belong to respective companies.
iSCSI initiator and target are industry standards
QNAP iSCSI initiator can be used with EMC, NetApp, Synology, QSAN and iSCSI target with special configuration
Utilize different storages space while enjoying QNAP software features

## Slide 32: 3 Steps to use remote disk space
Configure iSCSI LUN and iSCSI target at the storage device with free space
Storage & Snapshot > Remote Disk > Create Virtual Disk
Follow the wizard’s instructions to connect to disk

## Slide 33: Use iSCSI VJBOD to replace JBOD
Create Storage Pool; use snapshot, media indexing, Qsirch and other features
Container Station
2 x 10G SFP+
TS-831X
Virtual Pool
iSCSI LUN
Virtual Pool
RAID
Flexible Ethernet
Use VJBOD to mount other NAS's LUN as local disk

## Slide 34: Build a super storage With JBOD and VJBOD
Over 1 PB
8TB x 8=64TB
USB 3.0
JBOD 8TB x 8 x 6 = 384TB
8TB x 12 x 8 = 768TB
iSCSI
Connect with 8 NAS as
VJBOD disks
Connect 4 UX-800P expansion enclosures
Total Raw Storage Space
can exceed 1 PB

## Slide 35: 3 steps to use QNAP iSCSI VJBOD
After creation, create new Storage
Pool with the VJBOD disk
Storage & Snapshot > Disk/VJBOD >VJBOD >Create VJBOD
Input remote QNAP NAS address and allocate space

## Slide 36
Demo: Use QNAP NAS with
iSCSI VJBOD

## Slide 37: Summary
Scenario | Expand on original NAS |  |  |  | Additional Devices |  |  |  | 
Method | RAID Migration | RAID Expansion | Upgrade to Qtier | Replace Disk | System Migration | JBOD | VJBOD | Remote Disk | External Disk
Empty Bays | Needed | Needed | Needed | - | - | - | - | - | -
Other Benefits | Improve Protection | Improve Performance | Greatly Improve Performance | - | Increase # of Available Bays | Support Storage Pool | Support Storage Pool | Connect and Go | Plug and Go
Notes | Support Single→ RAID 1→5→ 6 | Support RAID 5, 6, 50, 60 | Storage Service Will be paused when upgrading | Replace every disk need re-sync | Advance models may not migrate to entry-level models | Maximum number depends on models | Maximum 8 NAS | Storage Pool Not Supported | Storage Pool Not Supported

## Slide 38: QNAP NAS Road to Expansion
Replace disks and system migration
Add new disks to migrate RAID type
Add new disks to expand RAID or upgrade to Qtier
Connect expansion unit or external storage
Use iSCSI VJBOD to share NAS space
RAID 1
RAID 5/6
RAID Expansion
NAS+JBOD
NAS+VJBOD
QNAP Storage & Snapshot allow the NAS to grow with the user!

## Slide 39: QNAP NAS ,Your best choice!