## Slide 1: Unveiling the new QM2 M.2 SSD/10GbE PCIe Expansion cards
QM2-2S, QM2-2P
QM2-2S-220A, QM2-2P-244A
QM2-2P-344, QM2-2P-384
QM2-2S10G1T
QM2-2P10G1T
QM2-4S-240, QM2-4P-284
QM2-4P-342, QM2-4P-384A

## Slide 2: QM2 M.2 SSD/10GbE expansion cards
QM2-2S
2 x M.2 22110 / 2280 SATA SSD ports
QM2-2P
2 x M.2 22110 / 2280 PCIe NVMe SSD ports
QM2-2S10G1T
2 x M.2 2280 SATA SSD ports
1 x 10GBASE-T 10GbE port
QM2-2P10G1T
2 x M.2 2280 PCIe NVMe SSD ports
1 x 10GBASE-T 10GbE port

## Slide 3: Add SSD slots to NAS with a QM2 card
Accelerates random IOPS
TVS-463
QM2 SSD RAID
QM2-2S
Performance and storage capacity
In QTS 4.3.4, you can freely upgrade a normal pool (configured after 4.2) to a Qtier pool without starting over
SSD cache
SSD tier
Without changing existing configurations

## Slide 4: QTS Supports M.2 SSD Cache Acceleration
Read
Write
HDD storage
SSD storage
Application layer
Read caching
Read/Write caching
Reduce I/O latency
Accelerates IOPS performance
Global read-write cache
Applies SSD cache to all volumes and LUNs with a single setup process, or specified volumes only

## Slide 5: Expand high-speed M.2 SSD tier with Qtier
HDD storage
SSD storage
Application layer
Qtier 2.0
Total capacity = hard drives + SSD
Total capacity = hard drives
Read/Write caching
Sequential
Random
Hot data & reserved block
Cold and archived data
*The following NAS models support Qtier technology (QTS 4.3.4):
x89U, x85/x85U (QTS), x82(U), x80(U), x79(U), x77, x73(U), x71(U), x70(U), x63(U), x53A, x53B(U), x53 Pro
Keep flexibility for accelerating performance of key data and increase cost/performance ratio
I/O aware
Tiering on Demand
Storage space and SSD caching

## Slide 6: Create a RAID 0/1 M.2 SSD tier
Dual-port 10G SFP+
QM2-2S
Configure a RAID 0/RAID 1 M.2 SSD ultra high speed tier with a 10GbE NIC and QM2 card installed together in a NAS that has two PCIe slots.
TS-x80U R2

## Slide 7: Add four M.2 SSDs with a single card
QM2-4S-240
4 x M.2 2280 SATA SSD ports
4 x M.2 2280 PCIe NVMe SSD ports
QM2-4P-284
Adding four M.2 SSDs with one PCIe slot
Bundled with heatsink and brackets that can be used on all NAS models
PCIe 2.0 interface
Create a RAID protection
RAID 5/RAID 6/RAID 10

## Slide 8: QM2-4S-240: 4 x M.2 SATA SSDs

## Slide 9: QM2-4P-284: 4 x M.2 PCIe NVMe SSDs
4 x M.2 2280 PCIe 2.0 x4 NVMe SSD ports
QM2-4P-284
(2.0 x8 card)

## Slide 10: Demo: how to install a QM2-4S-240 card
Remove cooling module.
Remove the protection pads from the card.
Install M.2 SSDs.
Install the cooling module.
Install the QM2 card to the TS-EC880U R2.
Go to Control Panel > System Status or check the QM2 card information at Dashboard.
Go to Storage & Snapshots Manager to check M.2 SSD information.
Configure and expand the SSD tier in the Storage & Snapshots Manager.
QTS configuration
TS-x80U R2
QM2-4S-240
QM2 installation
x4

## Slide 11: QM2-2S cards with compact design
QM2-2S-220A
147 mm
5%
157 mm
5 % less compared with QM2-2S

## Slide 12: QM2-2P cards with compact design
QM2-2P-244A
147 mm
5%
157 mm
5 % less compared with QM2-2P

## Slide 13: Fits with all PCIe slots
2 x QM2-2S-220A / QM2-2P-244A
TS-1677X
PCIe slot 1
Slot 1
PCIe slot 2
PCIe slot 3
Reserved the largest bandwidth for graphics cards
QM2 SSD RAID

## Slide 14: How to fully utilize the PCIe 3.0 bandwidth?
★ 3.0 x4 slot
  TS-x71U (1)
  TS-x73, TS-x73U
  TS-x77 (2)
  TS-x80U (1)
* (1) (2) (3) (4) is the NAS PCIe slot numbering
★ 3.0 x8 slot
  TS-x71 (2), TS-x71U (2)
  TS-x77 (1)
  TS-1282 (1)
  TS-x80, TS-x80U (2)
  TS-x89U (3,4,5)
  TS-1685 (1)
★ 3.0 x16 slot
  TS-682 (1), TS-882 (1)
  TDS-16489U (2)

## Slide 15: Ideal choice to boost performance: M.2 PCIe NVMe SSDs
20Gb/s
32Gb/s
M.2 PCIe 2.0 x4
M.2 PCIe 3.0 x4
16G/s
M.2 PCIe 3.0 x2
Interfaces
Theoretical Speed
★ Mainstream
240GB | USD $150
240GB | USD $150
*Source: Amazon.com (Mar, 2018)
240GB | USD $70
M.2 SATA III
6Gb/s
240GB | USD $70
M.2 PCIe NVMe SSDs
have more than 2X performance enhancement.
★ New choice
Notes: Gen 3 x2: ADATA XPG SX6000, Hikvision E1000 >> 價格都接近 M.2 SATA

## Slide 16: Introducing the high-speed PCIe 3.0 interface to QM2 cards
QM2-2P-344
QM2-2P-384
QM2-4P-384A
QM2-4P-342
2 x
M.2 PCIe NVMe SSD ports
4 x
M.2 PCIe NVMe SSD ports
(3.0 x4 card)
(3.0 x8 card)
(3.0 x4 card)
(3.0 x8 card)

## Slide 17: QM2-2P-344 PCIe 3.0 x4 card: 2 x NVMe SSD
2 x M.2 22110/2280 PCIe 3.0 x4 NVMe SSD ports
QM2-2P-344
(3.0 x4 card)

## Slide 18: QM2-2P-384 PCIe 3.0 x8 card: 2 x NVMe SSD
2 x M.2 22110/2280 PCIe 3.0 x4 NVMe SSD ports
QM2-2P-384
(3.0 x8 card)

## Slide 19: QM2-4P-342 PCIe 3.0 x4 card: 4 x NVMe SSD
4 x M.2 2280 PCIe 3.0 x2 NVMe SSD ports
QM2-4P-342
(3.0 x4 card)

## Slide 20: QM2-4P-384 PCIe 3.0 x8 card: 4 x NVMe SSD
4 x M.2 2280 PCIe 3.0 x4 NVMe SSD ports
QM2-4P-384A
(3.0 x8 card)

## Slide 21: Performance demo: PCIe 3.0 NAS with a QM2 installed
QM2-2P-384
10G NIC
Install a QM2-2P-384 at PCIe 3.0 x8 slot
Install a LAN-10G2SF-MLX
at PCIe 2.0 x4 slot
TVS-1282
Download
Upload
279
1000
500
0
1176
1063
Qtier enabled
HDD volume
365
Download
Upload
(MB/s)
Client PC: Intel® Core™ i7-4770 3.40GHz CPU; 16GB RAM; Intel 10GbE NIC ; Windows® 10 64-bit; 10GB file transfer by Robocopy
Tested in the QNAP lab. Actual results may vary by environments. Test environment: NAS operating system: QTS 4.3
Volume type: RAID 5; 4 x Seagate Enterprise HDD 1TB

## Slide 22: 3rd party operating system support
Low-profile PCIe add-on cards, bundled with full-height bracket.
Self-monitored with thermal sensors to control the speed of smart fan modules.
Compliant with PCIe standards
Note: M.2 SSD compatibility and function supported depends on the hardware design and platform. Please check with your motherboard manufacturer for details.
Active cooling module

## Slide 23: Select the QM2 card you need
QM2-2S
QM2-2S-220A
QM2-2S10G1T
QM2-4S-240
QM2-2P-344
QM2-2P-384
M.2 PCIe Gen 3
M.2 SATA
QM2-2P
QM2-2P-244A
QM2-2P10G1T
QM2-4P-284
M.2 PCIe Gen 2
QM2-4P-342
QM2-4P-384A
Expand four M.2 ports
Support 10GBASE-T port

## Slide 24: Transform your NAS with QM2 expansion cards
QM2-2S, QM2-2P
QM2-2S-220A, QM2-2P-244A
QM2-2P-344, QM2-2P-384
QM2-2S10G1T
QM2-2P10G1T
QM2-4S-240, QM2-4P-284
QM2-4P-342, QM2-4P-384A