## Slide 2: New to the Ryzen NAS Family
TS-x77XU rackmount NAS
TS-x77 desktop NAS
TS-1277
TS-877
TS-677
2 x SFP+ 10G Mellanox CX4 SmartNIC
TS-1677X
2 x 10GBASE-T
New
TS-2477XU-RP
TS-1677XU-RP
TS-1277XU-RP
TS-877XU
TS-877XU-RP
TS-977XU
TS-977XU-RP
Notes: 原標題: Ryzen 戰線成員全員到齊

## Slide 3: TS-x77XU Reborn
Ryzen 1700
# of CPU Cores: 8
# of Threads: 16
Max Boost Clock: 3.7 GHz
Base Clock: 3 GHz
Default TDP / TDP: 65 W
Ryzen 2700
# of CPU Cores: 8
# of Threads: 16
Max Boost Clock: 4.1 GHz
Base Clock: 3.2 GHz
Default TDP / TDP: 65 W
Ryzen 1600
# of CPU Cores: 6
# of Threads: 12
Max Boost Clock: 3.6 GHz
Base Clock: 3.2 GHz
Default TDP / TDP: 65 W
Ryzen 2600
# of CPU Cores: 6
# of Threads: 12
Max Boost Clock: 3.9 GHz
Base Clock: 3.4 GHz
Default TDP / TDP: 65 W

## Slide 4: Coming Soon
TS-877XU-1200-4G
Ryzen 3 1200, 4GB RAM (1x 4GB)
TS-877XU-RP-1200-4G
Ryzen 3 1200, 4GB RAM (1x 4GB)
TS-877XU-RP-2600-8G
Ryzen 5 2600, 8GB RAM (2x 4GB)
TS-1277XU-RP-1200-4G
Ryzen 3 1200, 4GB RAM (1x 4GB)
TS-1277XU-RP-2600-8G
Ryzen 5 2600, 8GB RAM (2x 4GB)
TS-1677XU-RP-1200-4G
Ryzen 3 1200, 4GB RAM (1x 4GB)
TS-1677XU-RP-2600-8G
Ryzen 5 2600, 8GB RAM (2x 4GB)
TS-1677XU-RP-2700-16G
Ryzen 7 2700, 16GB RAM (2x 8GB)
12-bay
16-bay
8-bay

## Slide 5: Complete product portfolio – 1U 9-bay
5 x SSD (inside)
4 x HDD
TS-977XU-RP-1200-4G
Ryzen 3 1200, 4GB RAM (1x 4GB)
TS-977XU-RP-2600-8G
Ryzen 5 2600, 8GB RAM (2x 4GB)
TS-977XU-1200-4G
Ryzen 3 1200, 4GB RAM (1x 4GB)
9-bay
Ready on Sep.- Oct.
Single PSU
250W
Redundant PSU
2 x 300W
Notes: 白手起家款

## Slide 6: Complete product portfolio – 4U 24-bay
TS-2477XU-RP-2600-8G
Ryzen 5 2600, 8GB RAM (2x 4GB)
TS-2477XU-RP-2700-16G
Ryzen 7 2700, 16GB RAM (2x 8GB)
24-bay
Ready on Sep.- Oct.
Redundant PSU
2 x 800W
Notes: 白手起家款

## Slide 7: Supports up to 64 GB Memory
Supports Dual-channel and Long-DIMM x4
Installing memory in pair to take advantage of dual-channel
One module
Two modules
Install in A0 and B0 slots
Install in A0 slot

## Slide 8: TS-x77XU Memory Accessories
Ordering P/N | Specification
RAM-4GDR4A1-UD-2400 | DDR type: DDR4(288PIN) Capacity: 4 GB Manufacturer: ADATA Frequency: DDR4-2400 Manufacturer P/N: AD4U2400W4G17-BSSZ
RAM-8GDR4A1-UD-2400 | DDR type: DDR4(288PIN) Capacity: 8 GB Manufacturer: ADATA Frequency: DDR4-2400 Manufacturer P/N: AD4U240038G17-BSSZ
RAM-16GDR4A1-UD-2400 | DDR type: DDR4(288PIN) Capacity: 16 GB Manufacturer: ADATA Frequency: DDR4-2400 Manufacturer P/N: AD4U2400316G17-BSSZ

## Slide 9: Customized Memory
CTO SKUs have longer lead time
High memory NAS for your project
16 GB, 32GB or 64GB for each SKUs
16
( 4GB x 4 )
32
( 8GB x 4 )
64
( 16GB x 4 )

## Slide 10
TS-x77XU Hardware Introduction

## Slide 11: Enjoy Qtier and SSD cache in a 1U NAS
4 x 3.5”SATA 6Gb/s HDD/SSD ports
LED indicators:
System status, network, disks
5 x 2.5”
SATA 6Gb/s SSD ports
Notes: 白手起家款

## Slide 12: 1U TS-977XU/TS-977XU-RP rear view
Redundant PSU
Single PSU
4 x DDR4
Long-DIMM slots
4 x USB 3.0 ports
2 x 10GbE SFP+ ports
USB 3.1 Gen2 (10G) port
2 x GbE RJ45 ports
250W or
2 x 250W
Low profile PCIe 3.0 x16 slot
Notes: 白手起家款

## Slide 13: TS-977XU SSD Installation
01
02
03
04
05

## Slide 14: 2/3/4U TS-x77XU Front View
24/ 16/ 12/ 8 x 3.5”SATA 6Gb/s HDD/SSD Ports
TS-1277XU / TS-1277XU-RP
TS-877XU / TS-877XU-RP
TS-1677XU / TS-1677XU-RP
TS-2477XU-RP
Notes: 白手起家款

## Slide 15: 2/3/4U TS-x77XU Front View
Power switch
LED indicators: system status, network, external expansion enclosures, disks
2U
3U
4U
Notes: 白手起家款
2U/3U

## Slide 16: 2/3/4U TS-x77XU Rear View
8-bay
Single PSU
Redundant PSU
2 x 10Gb SFP+ SmartNIC ports
4 x USB 3.0
Type-A ports
USB 3.1 Gen2 (10G) Type-A & Type-C ports
2 x 1Gb
Network ports
24-bay
Redundant PSU
Redundant PSU
Single PSU

## Slide 17: Industry-leading PCIe expansion options
QM2 provides 10GBASE-T port and/or M.2 SSD slots for SSD cache or Qtier tiered storage for optimized storage performance.
USB 3.1 Gen 2 expansion cards provide 10Gb/s for external USB devices. Type-A port is also backward compatible with USB 3.0/2.0 devices.
SAS expansion cards are for adding support of REXP expansion units for up to 40 additional SAS/SATA drives.
40GbE/10GbE and wireless network expansion cards
provide high bandwidth, low latency, or wireless AP functionality.

## Slide 18: TS-x77XU PCIe slots
3/4U: full height
1
1
2
3
4
1
2
3
4
1/2U: : low profile
1
2
3
4
Notes: 這頁需要

## Slide 19: Flexible PCIe Allocation (2/3U)
2 x PCIe x8 slot (CPU)
PCIe x8
#4
#3
#2
#1
PCIe x8
4 x PCIe x4 slot (CPU)
PCIe x4
#4
#3
#2
#1
PCIe x4
PCIe x4
PCIe x4
Occupied
Empty

## Slide 20: Flexible PCIe Allocation (4U)
2x PCIe x8 slot (CPU)
PCIe x8
#3
#2
#1
PCIe x8
4 x PCIe x4 slot (CPU)
#4
PCIe x4
#3
#2
PCIe x4
PCIe x4
PCIe x4
#4
#1
Occupied
Empty

## Slide 21: GPU card slots and supported dimensions
 | Slot | size W x H x L (mm)
TS-877XU TS-877XU-RP | Slot 2 | 37 x 68.9 x 214
 | Slot 4 | 37 x 68.9 x 214
TS-1277XU TS-1277XU-RP | Slot 2 | 37 x 68.9 x 214
 | Slot 4 | 37 x 68.9 x 214
TS-1677XU TS-1677XU-RP | Slot 2 | 38.5 x 111 x 214
 | Slot 4 | 38.5 x 111 x 214
TS-2477XU-RP | Slot 2 | 55 x 138 x 312
 | Slot 3 | 55 x 138 x 312
W
H
L

## Slide 22: Do more with graphics cards
QuAI
Support half-high GPU card and required no external power: NVIDIA GT1030, etc.
TS-1677XU-RP
Support full-high GPU card which required external power
3/4U NAS 500W+ power supply
2U NAS 250W/300W power supply

## Slide 23: Add-on GPU Card Applications
QTS/vQTS
Computing Acceleration
Virtualization Station
GPU Passthrough
AI
Computing Acceleration

## Slide 24: Ride the AI wave with "QuAI"
QNAP QuAI
AI Developer Package
QuAI is intended for data scientists and developers to quickly build, train, and optimize their AI models on QNAP NAS.
+
=
QuAI
AI
QNAP NAS
+
GPU accelerated computing

## Slide 25
Virtualization Station
HybridDesk Station, Linux Station
QVR Pro Client (HD Station)
Video Station
Plex Media Server
Smooth Video Experience

## Slide 26: GPU boosts image/video processing
H/W accelerated with GPU to lower CPU usage.
w/ GPU
w/o GPU
For OpenGL & DirectX applications
Tested at QNAP Lab. Results vary by actual environments. NAS：TS-1677X Ryzen 1700
QTS 4.3.4, Seagate ST4000VN0001
nVIDIA GeForce GTX 1060 6GB

## Slide 27: Tool-less rail kit
RAIL-B02
RAIL-A03-57
RAIL-A02-90
Supported NAS:
TS-877XU/1277XU
Max. Load: 20kg
Supported NAS:
TS-1677XU
Max. Load: 57kg
Supported NAS:
TS-2477XU
Max. Load: 90kg

## Slide 28: Hardware upgrade made easy
Pull it out and lift
up the cover

## Slide 29: More Efficient Backup with USB 3.1 Gen 2
5Gb/s
10Gb/s
2X
SPEED UP
USB 3.1
TYPE-C
TYPE-A
USB 3.0
USB 3.1 Gen 2
Notes: Type-A是紅色的

## Slide 30: Super high capacity surveillance
Surveillance Station 5.1
Default: 8 free channels
Max: 80 CH (optional license)
QVR Pro
Default: 8 free channels
Max: 128 CH (optional license)
QUSBCam2
Up to 1080p USB Webcam recording

## Slide 31: 10GbE SmartNIC with offload function
Buit-in Mellanox ConnectX-4 Lx 10GbE SmartNIC
Supports iSER

## Slide 32: Offload tasks from CPU with iSER
iSER (iSCSI Extension for RDMA)
Memory
Socket Layer and Network Drivers
Ethernet
Without iSER
Ethernet
Socket Layer and Network Drivers
Memory
With iSER
Memory
Socket Layer and Network Drivers
Ethernet
Ethernet
Socket Layer and Network Drivers
Memory

## Slide 33: Comes with two 10GbE Ports
10GbE x 2 (Sequential)
1200
600
0
1561
1560
1800
Tested in QNAP Labs. Figures may vary by environments.
Test environment: NAS: TS-1677XU-1700-16G with QTS 4.3.4
Volume type: RAID 5; 16 x Intel S3500 240GB SSDs (SSDSC2BB240G4)
(MB/s)
Read
Write

## Slide 34
One-for-many
Virtual QTS vQTS

## Slide 35: Running vQTS via Virtualzation Station
Conventional VM:
Windows, Linux, UNIX
Virtual QTS - vQTS
Virtualization
Station

## Slide 36: One-for-many
It allows IT admins to flexibly allocate system resources to different departments or groups for different privileges and applications.
Engineers
Management
Finance
Customer
service

## Slide 37: Dedicated resource allocation
Allocation of dedicated HW resources (CPU, RAM, storage space, and Internet) ensures performance quality.
Quad-core
4 GB
250 GB
1
Octa-core
8 GB
500 GB
2

## Slide 38: The best platform for vQTS
Numbers of allowed vQTS instances are based on the numbers of cores of the physical CPU.
AMD Ryzen™ 5 2600 6-core =
AMD Ryzen™ 7 2700 8-core =
2
4

## Slide 39: QTS & virtualization increase productivity
Supports Windows/Linux VMs and containers
QTS 4.3.5
Storage & Snapshot Manager, and new virtualization network functions
Virtualization
Station
Container
Station

## Slide 40
Double the ROI of purchasing SSDs
SSD Over-provisioning, Snapshot Remote Restore
QTS 4.3.5

## Slide 41: SSD Usage In Network Attach Storage
Drive Type | Sequential Access (MB/s) | Random Access (IOPS)
HDD | 100 | 350
SSD | 300 | 60000
https://www.sandisk.com/business/datacenter/resources/white-papers/the-ssd-enabled-pc-total-cost-of-ownership
SanDisk‘s Statistic for Global SSD/HDD Price Trend
SanDisk evaluate the 256 GB SSD per GB price in 2018 is only 30% compare to 2013
SSD can provide high random IOPS for multi-clients sync and business applications that can not be achieved by HDD.
In 2018, SSD price also comes close to the sweet spot.
Besides choosing the right SSD, you should also choose right NAS!

## Slide 42: QNAP SSD Global Cache and Qtier
Storage Pool
Volume
Block-based LUN
HDD
HDD
HDD
HDD
Qtier Pool SSD Tier
HDD
HDD
SSD Cache
SSD
SSD
Qtier Pool HDD Tier
SSD Cache let all data enter cache and read hot data from the storage in real time
Qtier utilizes SSD space and let data block be reallocated based on hot or cold in the storage
Volume
Block-based LUN
IT manager can have different SSD configurations with TS-x77XU
For real-time performance boost, deploy SSD Global Cache or All flash storage
For continued data tiering between hot and cold data, deploy the Hybrid Storage Qtier™ Auto Tiering

## Slide 43: Different SSD has Different Performance!
SSD Write amplification cause performance degradation
In QNAP Lab, engineer use FIO to test different SSD, and all SSD have showed consisted write performance degrade.
Different SSD's controller and Garbage Collection Algorithm will effect the long term performance
Different SSD in QNAP NAS’s FIO consisted performance (IOpattern: RW-4K):
How can storage vendor help to ensure SSD has expected performance ?
Notes: 43

## Slide 44: What is SSD Over-provisioning
D | D
D | D
D | D
6 pages of new data cannot all be stored to the SSD
N | New D
D | Valid D
 | Invalid D
 | OP
 | OP
N | N
N | N
N | N
With more reserved block, the GC is not required
Unless the SSD conduct GC internally first
N | N
D | 
D | 
N | N
N | N
D | D
D | D
D | D
With limited OP, 4 additional write is needed. With more OP the movement is not required.
SSD Over-provisioning reserves space in the SSD to decrease write amplification & increase consisted performance and endurance.
Reason: to avoid Garbage Collection in any giving point of time
Notes: 44

## Slide 45: The Advantage of Software-defined SSD Extra Over-provisioning
With QTS System, user can assign more OP to the SSD RAID.
At QNAP Lab, the effect of over-provisioning can not only be observed on single consumer-level Samsung 850 Pro to gain the performance same as data center SSD, but also be seem on SSDs as a RAID.
Above: Samsung 850 Pro as Single Disk
Below: Micron M1100 as RAID 1
FIO configuration: runtime=1800 ioengine=libaio direct=1 rw=randwrite bs=4k numjobs=1 iodepth=32
2*Micron M1100 RAID 1 Random Write IOPS with Dynamic OP
Notes: 45

## Slide 46: Choose SSD is Hard, Choose QNAP is Simple
IT managers' biggest challenges in deploying SSD is to measure the SSD performance and how it can solve storage bottleneck.
With QNAP SSD Profiling Tool, users can not only set OP, but further test SSD RAID performance with different OP amount.
IT managers can decide the best practice directly on production site
Notes: 46
73652517

## Slide 47
Using SSD Profiling Tool on TS-x77XU

## Slide 48: QNAP Global SSD Cache
The QNAP SSD Cache can be applied to multiple volume / LUN
Read-Only Copy frequently used data to SSD
Read-Write Not only copy data, new data can also be temporarily stored in SSD
(New)Write-Only  Only new data will be written into the cache
Data from clients and storage will both be cached
How Read-write Cache work:
When SSD Space not enough
Read
Write
Read
Write
HDD
IO Intensive
Application
SSD
Cache Type

## Slide 49: The Write-only Cache Increase ROI of SSD Cache with high Writing Demand
Write-only cache is promoted by Microsoft for endurance control.
QNAP believe Write-only Cache can increase the ROI of purchasing SSD in below scenario:
https://docs.microsoft.com/en-us/windows-server/storage/storage-spaces/understand-the-cache
SSD
SSD
NVMe
SSD
SSD
NVMe
Writes are cached
Reads are NOT
File Server focusing on write operations
Database with more write operation (Such as IOT monitoring server)
Use high endurance SSD (Intel Optane™) with other SSD
Notes: 49

## Slide 50: Qtier (Auto-Tiering) Increase Capacity and Performance at the Same Time
Hot Data
Warm Data
Cold Data
Access Pattern Change
Before Tiering
Data place not optimized
Start Tiering
After Tiering
Performance optimized
Qtier
Engine
Beside SSD Cache,
Qtier™ can migrate
data between SSD and
HDD directly
SSD capacity can be
utilized with limited
memory requirement.
Notes: 50
93325809

## Slide 51: Qtier 2.0 IO Aware tiering for real time performance boost
Beside tiering on
schedule, Qtier now
can simulate SSD
Cache behavior
It can utilize SSD
capacity while boost
performance in real
Time thus increase SSD
ROI
SSD Tier
C、D data block be written to HDD due to SSD full
HDD Tier
A
B
C
D
Block | Hit
C | 50
D | 50
D data block be promoted as access frequency increase
HDD Tier
A
B
C
Data
Blank
D
SSD Tier
Block | Hit
C | 50
D | 200
Notes: 51
93325809

## Slide 52: TS-x77XU SSD Multiple Configurations
In addition to acting as a backup server, SSD Over-provisioning, Global Cache and Qtier let TS-x77XU be deployed as production server
Scenario | File Server | Web, Application, Virtualization Server | Synchroni-zation, Vi-deo Editing | Surveillance, Backup, Log Server | Business-Critical Database
SSD Config | Qtier™ | Qtier™ | Read-Write Cache | Write-Only Cache | SSD RAID
SSD RAID | RAID 6 | RAID 10 | RAID 5 | RAID 10 | RAID 10
SSD OP | 10% | 20% | 20% | 30% | 30%
With 5 x 2.5”
SATA 6Gb/s SSD 1U Rackmount can use SSD too!
Notes: 52

## Slide 53: Businesses need lower RTO
Taiwan IThome survey 2017
Data Backup Time
Server Online
Disaster Happen
Recover Point Objective
Recover Time Objective
TIME
Can businesses only manually transfer data back from the remote end when disaster happen?
In the survey of 300 Enterprises and SMBs at Taiwan:
60% has used Remote Replication as Backup Plan.
50% of businesses expected the recovering time should be within 1 Hour.
But also 50% of businesses experience actual recovering exceed 1 Day!
Notes: 53
39094200

## Slide 54: Restore From Remote Snapshot Vault
The Snapshot Manager is now actively connected to Snapshot Vault
Support monitor and restore selected folders and files from the source NAS directly!
Both the source and destination NAS must be upgraded to 4.3.5 to support this function
Notes: 54

## Slide 55: Drastically Reduce Recover Time With 10GbE Network
The Remote Snapshot Vault Recovering is based on Ethernet service.
Using 1GbE network, recovering large data still takes hours.
Pair the Snapshot Replica Solution with 10GbE or even faster interfaces to increase both the backup and recovery speed !
Using QNAP 10GbE Switch to replace old 1GbE for reducing RTO dramatically
Notes: 55

## Slide 56: The Forth Way: Snapshot Export/Import
Export a snapshot from snapshot manager or snapshot vault
Using external storage device, the exported imaged can be imported to another NAS to create new volume or LUN
The same image can also be used to revert source volume or LUN
When network speed is limited, user can still import snapshots for reverting
Snapshot Reverting
Notes: 36588464

## Slide 57: With QTS 4.3.5 Power of Storage:
01
Software-defined SSD Extra OP
Measure & set unique over-provisioning amount on the NAS
02
SSD Global Cache & Qtier™
Using Cache or Auto Tiering to maximum SSD ROI
03
Remote Snapshot Restore
Using 10GbE network to reduce RTO
Notes: 36588464

## Slide 58
©2018著作權為威聯通科技股份有限公司所有。威聯通科技並保留所有權利。威聯通科技股份有限公司所使用或註冊之商標或標章。檔案中所提及之產品及公司名稱可能為其他公司所有之商標 。
Copyright © 2018 QNAP Systems, Inc. All rights reserved. QNAP® and other names of QNAP Products are proprietary marks or registered trademarks of QNAP Systems, Inc. Other products and company names mentioned herein are trademarks of their respective holder ​