## Slide 2: How many users?
Maximum user account count
  NAS local user accounts: 600 to 4,096
  NAS domain (AD/LDAP) user accounts: unlimited. For more powerful NAS, more users can be supported.

## Slide 3: How much capacity?
Capacity: GB? TB?
  Additional expansion unit needed?
  RAID configuration?
                =N-1 drive capacity: RAID 1/5
                =N-2 drive capacity: RAID 6
                >=N-2 drive capacity: RAID 10/50/60

## Slide 4: Which form factor?
  Rackmount
  Desktop
  1U (1.75 inch/44 mm) to 4U height, 19 inch (480 mm) width
  Single & redundant power options
  Low noise level with versatile exterior designs
  Multifunction & value

## Slide 5: Which processor? It matters!
64-bit x86 processors
  Intel Xeon, Core i7/i5/i3, Celeron multi-core 1.5 GHz+
  AMD Ryzen, R-series, G-series multi-core 2.0 GHz+
64-bit & 32-bit ARM processors
  64-bit Marvell 8040 quad-core 1.6 GHz
  64-bit Annapurna Labs AL-324 quad-core 1.7 GHz
  32-bit Annapurna Labs AL-314 quad-core 1.7 GHz / AL-212 dual-core 1.7 GHz
  64-bit Realtek RTD1295/1296 quad-core 1.4 GHz

## Slide 6: How much memory do I need?
For every snapshot of an 1 TB volume/LUN, 0.5 MB of RAM is needed to mount each snapshot.
CPU | RAM size | Maximum snapshots (NAS overall) | Maximum snapshots (single volume/LUN)
AMD/Intel (x86) | 4 GB or more | 1,024 | 256
Annapurna Labs/ Marvell/Realtek (ARM) | 4 GB or more | 256 | 64
Any | 2 GB | 64 | 32
Any | 1 GB | 32 | 16
TS-x51/x51+ total snapshot count is 256 only instead of 1,024. For ARM models to use snapshots, you need to update to QTS 4.3.4 (and later) and re-create the storage pool.

## Slide 7: Which kind of connection?
  USB 3.0 USB 3.1 Gen 2
  Thunderbolt 2 / Thunderbolt 3
DAS (External Storage)
NAS
  Thunderbolt 2 / Thunderbolt 3
  USB QuickAccess

## Slide 8: Go faster! Upgrade to 10GbE
Use QNAP NAS with the QNAP QSW unmanaged 10GbE switch series (optional; sold separately) and upgrade your network infrastructure to enjoy faster transfer speeds and to accelerate bandwidth-demanding applications.

## Slide 9: Multi-Gigabit 10GBASE-T
Mutiple speeds
Enjoy faster speeds with existing cables with Multi-Gigabit NBASE-T standard support

## Slide 10: 10GbE SFP+ ports
Supports 10GbE fiber-optic transceiver or use 1.5M/3M/5M SFP+ direct attached copper (DAC) cables

## Slide 11: USB QuickAccess direct connection to your PC/Mac
Dedicated USB cable between PC/Mac & NAS
1st time installation
Direct data access
QNAP Qfinder Pro for Windows & Mac
for quick connection
Max
100MB/s !

## Slide 12: M.2 2280 & 2.5-inch SATA SSD ports
Multiple M.2 2280 /2260 SATA 6Gb/s SSD slots
Multiple 2.5-inch SATA 6Gb/s SSD ports
  SSD cache or storage space
  Qtier tiered storage solution

## Slide 13: SSDs for auto-tiered hybrid architecture
Performance & cost efficiency
Capacity & performance
5 x 3.5-inch HDD Large capacity
Boost application's random IO
access performance!
All in one for SMB
2 x SSD for caching
RAID1
Boost both sequential and random
access performance!
High capacity file and
media server
RAID5

## Slide 14: Display 4K content via HDMI
The best compatibility with HDMI certification
Supports QNAP RM-IR004 remote control with QButton application!

## Slide 15: 4K video real-time transcoding
Provide multiple channels of H.264 video playback and transcoding via integrated GPU or a PCIe graphics card*
*model depedent

## Slide 16
PCIe slot for versatile expansion
With 1 or more PCIe slots for various expansion cards
10G/1G network card
USB 3.1 Gen2 10G card
QM2 M.2/10G card
QWA-AC2600 wireless card
SAS 12G card
Graphics card

## Slide 17
TS-1685
TS-1677X
AMD Ryzen 1200/1600/1700 up to 8 cores, 3GHz+
2 x 10GbE 10GBASE-T
Up to 64 GB (4 x DDR4) RAM
4 x 2.5” SATA SSD bays
12 x 3.5" SATA HDD bays
3 x PCIe slots
Intel® Xeon® D-1531/D-1521 up to 6 cores, 2.2~2.4GHz
2 x 10GbE 10GBASE-T
Up to 128 GB (4 x DDR4) RAM
6 x M.2 SATA SSD slots + 4 x 2.5” SATA SSD bays
12 x 3.5" SATA HDD bays
3 PCIe slots
Enterprise 16-bay NAS
Multi-core for running many virtual machines
Optional PCIe graphics card for Virtual Machine GPU passthrough or QTS HDMI output & transcoding
Hugh capacity
2 x 10GbE
3 x PCIe slots
4 x
SAS expansion units

## Slide 18
TVS-x82
TS-x77
AMD Ryzen 1600/1700 up to 8 cores, 3.0 ~ 3.7 GHz
Optional PCIe 10GbE card
Up to 64 GB (4 x DDR4 2400) RAM
2 x M.2 SATA SSD slots + 2/4 2.5” SSD slots
Up to 3 PCIe slots
Intel® Core™ i3/i5/i7 up to 4 cores, 3.4 ~ 4.2 GHz
Optional PCIe 10GbE card
Up to 64 GB (4 x DDR4 2400) RAM
2 x M.2 SATA SSD slots + 2/4 2.5” SSD slots
Intel® HD Graphics (3 x HDMI)
Up to 3 PCIe slots
SMB 6~12-bay NAS
Multi-core for running many virtual machines
Optional PCIe graphics card for Virtual Machine GPU passthrough or QTS HDMI output & transcoding
Optional 10GbE
2 or 3 x PCIe
4 x SAS
expansion units

## Slide 19
TVS-x73e
TS-x73
TS-1635AX
AMD RX-421BD 4-core 2.1GHz, up to 3.4GHz
Optional PCIe 10GbE card
Up to 64 GB (4 x DDR4) RAM
2 x M.2 SATA SSD ports
2 x PCIe Gen.3 x4 slots
AMD Radeon™ R7 Graphics (2 x HDMI)
AMD RX-421ND 4-core 2.1GHz, up to 3.4GHz
Optional PCIe 10GbE card
2 x M.2 SATA SSD ports
Up to 64 GB (4 x DDR4 2400) RAM
2 x PCIe Gen.3 x4 slots
SMB 6~12-bay NAS
Marvell® ARMADA® 8040 ARMv8 Cortex-A72 4-core 1.6 GHz
2 x 10GbE SFP+
Up to 16 GB (1 x DDR4) RAM
2 x M.2 SATA SSD ports
2 x PCIe Gen.3 x2/x1 slots
Large capacity with 2 x 10GbE SFP+ at an affordable price
Integrated GPU with dual HDMI outputs
Optional PCIe graphics card for QTS HDMI output & transcoding
10GbE exp.
Quad cores
2 x PCIe
SAS/USB
Expansion

## Slide 20
TS-963X
TS-932X
TVS-951X
x86 performance with HDMI and integrated GPU for transcoding
AMD GX-420MC 4-core 2.0GHz
1 x 10GbE 10GBASE-T
Up to 16 GB (2 x DDR3L 1600) RAM
4 x 2.5” SSD Slots + 5 x 3.5” HDD/SDD Slots
SMB 9-bay NAS
Annapurna Labs AL-324 4-core 1.7GHz
2 x 10GbE SFP+
Up to 16 GB (1 x DDR4 2133) RAM
4 x 2.5” SSD Slots + 5 x 3.5” HDD/SDD Slots
Intel Kaby Lake Celeron 3865U 2-core 1.8GHz
1 x 10GbE 10GBASE-T
Up to 32 GB (2 x DDR4 2133) RAM
4 x 2.5” SSD Slots + 5 x 3.5” HDD/SDD Slots
1 x 4K HDMI v1.4b
4-core performance with a x86 CPU for more apps
Affordability with 2 x 10GbE SFP+ and 4-core performance
10GbE
5 x 3.5" HDD
plus
4 x 2.5" SSD
hybrid design
Ready to use
Qtier & SSD cache

## Slide 21
TS-x53Be
TBS-453A
TS-x53B
Fully loaded and highly upgradeable with a PCIe slot
SMB 2~6-bay NAS
Intel Celeron J3455 4-core 1.5GHz, up to 2.3GHz
Up to 8 GB (2 x DDR3L 1866) RAM
1 x PCIe Gen.2 x2 slot (10GbE)
1 x 4K HDMI v1.4b
OLED, USB QuickAccess, SD card slot, remote
Intel Celeron J3455 4-core 1.5GHz, up to 2.3GHz
Up to 8 GB (2 x DDR3L 1866) RAM
1 x PCIe Gen.2 x2 slot (10GbE)
1 x 4K HDMI v1.4b
Intel Celeron N3150 4-core 1.6GHz, up to 2.08GHz
Up to 8 GB (2 x DDR3L 1600) RAM
4 x M.2 SATA SSD slots
1 x GbE + 4 port GbE switch
2 x 4K HDMI v1.4b
Highly upgradeable with a PCIe slot with affordability
Compact B5-sized NASbook with a 4-port GbE LAN switch.
X86 Intel
Quad cores
Transcoding
HDMI

## Slide 22
TS-832X
TS-431X2
TS-332X
TS-431X
10GbE quad-core ARM NAS with PCIe slots
SMB 3~8-bay NAS
Annapurna Labs 64-bit AL-324 4-core 1.7GHz
2 x 10GbE SFP+
Up to 16 GB (1 x DDR4) RAM
2 x PCIe Gen.2 x2/x1 slots
Annapurna Labs 32-bit AL-314 4-core 1.7GHz
1 x 10GbE SFP+
Up to 8 GB (1 x DDR3) RAM
Annapurna Labs 32-bit AL-212 2-core 1.7GHz
1 x 10GbE SFP+
Up to 8 GB (1 x DDR3) RAM
Annapurna Labs 64-bit AL-324 4-core 1.7GHz
1 x 10GbE SFP+
Up to 16 GB (1 x DDR4) RAM
3 x 3.5"/2.5" HDD/SSD + 3 x M.2 SATA SSD slots
10GbE quad-core ARM NAS
10GbE quad-core ARM NAS with triple M.2 SATA SSD acceleration
10GbE dual-core ARM NAS
Performance
Affordability
ARM CPU
10GbE

## Slide 23
SOHO 2~4-bay NAS
Intel Celeron J1900 4-core 2.0GHz​, up to 2.42GHz
Up to 8 GB (2 x DDR3L 1600) RAM​
2 x GbE​
1x 1080p HDMI
Intel Celeron J1900 4-core 2.0GHz​, up to 2.42GHz
2GB fixed DDR3L RAM​
2 x GbE​
1x 1080p HDMI
Intel Celeron N3060 2-core 1.6GHz​, up to 2.48GHz
Up to 8 GB (2 x DDR3L 1600) RAM​
2 x GbE​
1x 4K HDMI, USB QuickAccess, SD card slot
TS-251+/451+
HS-251+
TS-251A
x86 NAS with 1080p HDMI & transcoding
Silent x86 fanless NAS with 1080p HDMI & transcoding
Dual-core x86 NAS with USB access, 4K HDMI & transcoding
X86 Intel
Transcoding
HDMI

## Slide 24
TS-231P2/431P2
TS-328
TS-131P/231P/431P
TS-128A/228A
Quad-core personal cloud for containerized apps
Home & SOHO 1~4-bay NAS
Annapurna Labs 32-bit AL-314 4-core 1.7GHz
2 x GbE
Up to 8 GB (1 x DDR3) RAM
Annapurna Labs 32-bit AL-212 2-core 1.7GHz
2 x GbE
Up to 8 GB (1 x DDR3) RAM
Realtek 64-bit RTD1296 4-core 1.4GHz
    2 x GbE
Fixed 2 GB DDR4 RAM
4K video transcoding
Realtek 64-bit RTD1295 4-core 1.4GHz
1x GbE
Fixed 1 GB DDR4 RAM
3-bay personal cloud with 4K transcoding
Up to 220MB/s performance
Up to 110MB/s performance
Power saving
Affordable

## Slide 25: Thunderbolt NAS line up
TS-453BT3
TVS-1582TU
TVS-882ST3
TVS-1282T3 & TVS-x82T series

## Slide 26: Cross-platform collaboration
Adapter for Thunderbolt 2 Ｍac/PC
Apple Thunderbolt 3 to Thunderbolt 2 adapter

## Slide 27: A flawless workflow
London
High-speed ingest/backup
1
Off-site colaboration
New York
Off-site backup
(QNAP RTRR)
Collaboration
2
3
4

## Slide 28
TVS-1282T3
TVS-882ST3
TS-453BT3
TVS-882BRT3
Thunderbolt 3 NAS
Thunderbolt 3
2 x 10GBASE-T
6 x TX expansion
Intel Core i5/i7 4 core, 3.4~4.2GHz
Max 64GB (4 x DDR4) RAM, 2 x M.2 SATA SSD
8 x 3.5" HDD + 4 x 2.5" SSD
4 x Thunderbolt 3, 2 x 10GBASE-T, 3 x 4K HDMI
Optional 5.25" LG Blu-ray drive or RDX drive
Intel Core i5/i7 4 core, 3.4~4.2GHz
Max 64GB (4 x DDR4) RAM, 2 x M.2 SATA SSD
8 x 3.5 吋 HDD + 4 x 2.5 吋 SSD
4 x Thunderbolt 3, 2 x 10GBASE-T, 3 x 4K HDMI
Intel Core i5/i7 4 core, 1.9 ~ 2.6GHz
32GB (2 x DDR4) RAM
8 x 2.5” SATA SSDs/HDDs, 2 x Thunderbolt 3
2 x 10GBASE-T, 1 x 4K HDMI
Intel Celeron J3455 4 core 1.5GHz, up to 2.3GHz,
8GB DDR3L RAM, 2 x M.2 SATA SSD 埠,
2 x Thunderbolt 3
1 x 10GBASE-T, 2 x 4K HDMI
Blu-ray disc drive or RDX drive backup
1500MB/s, for 4 Thunderbolt concurrent clients
Compact yet powerful
Affordability with Thunderbolt convenience

## Slide 29
TVS-1282T
TVS-882T
TVS-682T
Thunderbolt 2 NAS
Intel Core i3/i5/i7, 4 core 3.4~4.2GHz
Max 64GB (4 x DDR4) RAM
2 x M.2 SATA SSD
3.5" SATA HDD + 2.5" SATA SSD hybrid design
2 x Thunderbolt 2
2 x 10GBASE-T
3 x 4K HDMI
Thunderbolt 2
2 x 10GBASE-T
6 x TX expansion

## Slide 30
Blu-ray & RDX NAS
Optional
Blu-ray
writer or RDX drive
TVS-882BR
TVS-882BRT3
Intel Core i5/i7 quad-core up to 3.6 GHz
Max. 64 GB (4 x DDR4) RAM, 2 x M.2 SATA SSD
8 x 3.5" HDD + 1 x 5.25" drive slots
5.25" SATA port for optional Blu-ray or RDX support
3 x 4K HDMI
3 x PCIe Gen.3 slots
4 x Thunderbolt 3 (TVS-882BRT3)

## Slide 31
Thank you for choosing
Copyright © 2018 QNAP Systems, Inc. All rights reserved. QNAP® and other names of QNAP Products are proprietary marks or registered trademarks of QNAP Systems, Inc. Other products and company names mentioned herein are trademarks of their respective holder ​