## Slide 1
Notes: Add 10GBASE-T, 畫面要有速度感

## Slide 2: SilentNAS family w/ 0 dB & high performance
HS-453DX
HS-251+
Quad-core Intel Celeron J1900
2 GB DDR3L RAM (not expandable)
1080p HDMI output and transcoding
2 x 1GbE LAN ports
2 x SATA 3Gb/s HDD ports
Quad-core Intel Celeron J4105
4 GB/8 GB DDR4 RAM (expandable to 8 GB)
4K HDMI output and transcoding
1 x 10GbE LAN (10G/5G/2.5G/1G) +
1 x 1GbE LAN port
2 x SATA 6Gb/s HDD ports +
2 x M.2 SATA 2280 6Gb/s SSD slots
*The noise level will vary based on the drive used.

## Slide 3: QTS 4.4.0 w/ Linux kernel version 4.14
Ships with QTS 4.4.0 and the newer LTS(Long Term Support) Linux kernel 4.14
Graphics drivers
    Gemini Lake (QNAP HS-453DX)
    Coffee Lake (QNAP TVS-472XT, TVS-672XT, TVS-873XT)
Major advantages of 4.14 over 4.2
    Scalability & performance improvements for ext4

## Slide 4: Intel 4C J4105 Gemini Lake SoC
14nm
Power saving
1.5GHz
Base
2.5GHz
Burst
J4105
Gemini Lake SoC
10 watt
TDP
4 cores
4 threads
AES-NI encryption
Volume & folder support
GPU up to 750 MHz
UHD Graphics 600

## Slide 5: DDR4 2400 MHz SO-DIMM memory
HS-251+
DDR3L-1333
HS-453DX
2 x SO-DIMM
DDR4-2400
Dual-channel
2 x 4GB
HS-453DX-8G:
Available models:
HS-453DX-4G:
2 x 2GB

## Slide 6: HDMI 4K 60fps fluid motions
Notes: 支持新一代HDMI 4K @60Hz影像输出规格，动态分辨率更高，人物在高速移动之下的动态表现看起来便更加流畅、无残影，享受让你耳目一新的的高清影像。

## Slide 7: Dual HDMI ports for optimal quality
Audio
Video
Amplifier
TV

## Slide 8: NAS front view and configurations
Left tray latch
*Minimalist, non- intrusive design
Right tray latch
HDD LED
HDD LED
Status LED
IR receiver
Power button
Magnetic front cover
Notes: 需要有一個前蓋合上的圖. Show 前蓋的 LED. 可以把下面的圖去掉, 只留前蓋說明可拆

## Slide 9: Hot-swappable 3.5”/2.5” HDD/SSD
1.
2.
3.
4.
3.5-inch HDD
2.5-inch HDD / SSD
Notes: 拆前蓋
拔出 HDD tray
Show 3.5” & 2.5” 安裝方式
QIG 有線稿

## Slide 10: Reduce the heat in a hot environment
3.5”
2.5”
Keep it ventilated
No object on top
Pick 5400/5900 RPM drives
Notes: 放 3.5" HDD & 2.5" HDD 的圖各一張代表.
線稿 ok

## Slide 11: The best match 24x7 NAS HDDs
Quiet
Lower power
Lower temp

## Slide 12: How to pick the right drives
Specifications | 4TB
Model Number | WD40EFRX
Interface | SATA 6Gb/s
Formatted Capacity | 4 TB
Form Factor | 3.5”
Advanced Format (AF) | Yes
Native command queuing | Yes
RoHS compliant | Yes
Performance | 
Interface transfer rate (max) Interface speed Internal transfer rate | 6 Gb/s 150 MB/s
Cache (MB) | 64
Performance Class | 5400 PRM Class
Specifications | 4TB
Standard Model Numbers | ST4000VN008
Interface | SATA 6Gb/s
Features and Performance | 
Drive Bay Supported | 1-8 Bays
Multi-User Technology | 180TB/year
Rotational Vibration (RV) Sensor | Yes
Dual-Plane Balance | Yes
Error Recovery Control | Yes
Max. Sustained Transfer Rate OD (MB/s) | 180MB/s
Spindle Speed (RPM) | 5900
Cache (MB) | 64
Source: 2018/10/01 www.Seagate.com & www.wdc.com

## Slide 13: Easy to install M.2 SATA SSDs
1.
2.
3.
4.
Notes: 拆底部螺絲 (QIG 有線稿)
Show M.2 SSD & RAM

## Slide 14: Dual HDDs & dual M.2 SATA SSDs
2 x 3.5"/2.5" HDD/SSD ports
2 x DDR4-2400 SODIMM slot (max 2 x 4 GB)
2 x M.2 SATA 2280 6Gb/s SSD slots

## Slide 15: All solid capacitors for longevity!
Japan-quality conductive polymer aluminum solid capacitors and over-current protection for high reliability and longevity.
Notes: 日系電容
SANYO
PANASONIC
NIPPON CHEMI-CON

## Slide 16: USB Type-C & Type-A hyper connectivity
Icons: UPS, keyboard, mouse
Icons: 外接硬碟, 隨身碟, iphone 手機
Icons: USB-C 隨身 SSD/隨身碟
1 x USB 3.0 Type-C
2 x USB 2.0 Type-A
2 x USB 3.0 Type-A

## Slide 17: Live Demo
Upgrade memory
Install M.2 SATA SSD

## Slide 18: 10G/5G/2.5G/1G LAN speeds
Your existing wiring infrastructure may already support > 1Gbps!
 | CAT 5e | CAT 6 | CAT 6A & CAT 7
1G | ✔ | ✔ | ✔
2.5G | ✔ | ✔ | ✔
5G | ✔ | ✔ | ✔
10G | X |  | ✔
Save cost with NBASE-T standard
Max 55 meters

## Slide 19: Based on Aquantia’s AQC107 10GbE NIC
Aquantia
Investors
Multi-Gig IC
Better compatibility

## Slide 20: 10GbE performance
Environment:HS-453DX: 2 x 2.5" 240GB SSD + 2 x M.2 SSD, RAID 5, QTS 4.4.0, 4GB RAM, thick volume
Client PC: Windows 10 Pro, Intel Core-i7 4770 3.4GHz, 16GB RAM, LAN-10G2T-X550 MTU 9000
Read
Write
0
1 x 10GbE
encrypted volume
1 x 10GbE
Read
Write
(MB/s)
100
200
300
400
500
600
700
677
648
676
520
Notes: 1 x 10GbE
Windows download: 677 MB/s
Windows upload: 648 MB/s
- 1 x 10GbE encrypted volume
Windows download: 676 MB/s
Windows upload: 520 MB/s

## Slide 21: Install a 10GbE adapter to PC
  Linux 3.2, 3.10, 3.12, 4.2, 及 4.4
  Windows® 10, 8.1, 8, 7 (32/64 bit)
QNAP QXG-10G1T 1-port 10G network adapter
10G/5G/2.5G/1G/100M
PCIe Gen 3 x4 interface

## Slide 22: Mac users connect to 10GbE
2018 iMac Pro
1 NBASE-T port with 10GbE
Mac with Thunderbolt 3 can connect to 10GbE with the QNAP QNA-T310G1T Thunderbolt 3 to 10GBASE-T adapter
10GbE
Ethernet
Ethernet
Thunderbolt 3
(USB-C)
USB 3
SDXC card slot
3.5mm
headphone
QNA-T310G1T
NBASE-T
Specs
Controller： AQC107S-B1-C + AQX-N3F10-DRE-U3C
Interfaces：1 x Thunderbolt 3, 1 x 10GbE 10GBASE-T 埠(10G/5G/2.5G/1G)*
LAN cable：CAT 6a/ CAT 7
*Mac with macOS 10.13.3 (or newer) is required.

## Slide 23: Accessories- 10GbE Network Switch
Up to 12 x
10GbE ports
Up to 8 x
10GbE ports
QSW-1208-8C
QSW-804-4C
12-port 10GbE switch
4 x SFP+ port
8 x RJ45/ SFP+ combo ports
8-port 10GbE switch
4 x SFP+ port
4 x RJ45/ SFP+ combo ports
12 Ports
8
Ports

## Slide 24: Live Demo
10GbE performance
& Qtier

## Slide 25: HybridDesk Station for various A/V needs
Qremote App
Mouse &
Keyboard
USB
Network
Audio
HDMI

## Slide 26: Various HybridDesk Station apps
System Mgmt.
Multimedia Mgmt.
Multimedia
Surveillance
Browser & Productivity
Comm. & Social
QTS
File Station HD
Surveillance Station
QVR Pro Client
Skype
Facebook
HD Player
OceanKTV
YouTube
Clementine
Plex Home Theater
Spotify
TuneIn Radio
Photo Station HD
Video Station HD
Music Station HD
Chrome
Firefox
LibreOffice

## Slide 27: Customize actions of buttons with QButton
Play your favorite music playlist with a single button or set other buttons to play the previous or next song
View pre-selected channels on Surveillance Station for quick surveillance monitoring
Set a button to restart or power off your NAS for greater convenience
QNAP RM-IR004 IR remote control included

## Slide 28: Linux Station turns NAS into a Ubuntu PC
HDMI output from NAS to a monitor
1
Connect a USB keyboard and a mouse to the NAS to begin the Ubuntu operation
2
Ubuntu 14.04
Ubuntu 16.04
Ubuntu Kylin (Chinese)
Multi-version Ubuntu

## Slide 29: Linux Station + Kodi to play everything
Use Kodi to play contents on NAS
Install ’n use
Install Kodi plug-in Video HD
Support the same Video Station functions such as
progress, categorization, subtitle
Video HD

## Slide 30: OceanKTV for the home karaoke
Dual dynamic microphone inputs

## Slide 31: Management & playback in OceanKTV
Web
TV
Mobile
Song library
Singing & YouTube playlist
iOS/Android
remote control
3 ways to play a song

## Slide 32: Streaming & accelerated transcoding
4K H.264 decoding & encoding for real-time or offline 4K video transcoding on various client players for smooth playback and support more clients
HDMI output for 4K Ultra HD (3840 x 2160, 60FPS) content
Stream content through DLNA, AirPlay, Chromecast and Plex

## Slide 33: Use PLEX to stream media collections
Stream
Stream
Phone
Tablet
PC
Smart TV
Stream

## Slide 34: Cinema28 for the whole home streaming
Cinema28 allows for single-interface management of all your media files and can stream files to every connected device throughout your home.
HDMI
(Audio)
Bluetooth
HDMI
(HD Player)
Chromecast
USB DAC
AirPlay
DLNA
Line Out

## Slide 35: Enjoy Roon without a PC
Two M.2 SATA SSD slots for higher performance

## Slide 36: Different SSD has Different Performance
How can storage vendors help to ensure SSD has expected performance?
In QNAP Lab, engineer use FIO to test different SSD, and all SSD have showed consisted write performance degrade.
Different SSD’s controller and Garbage Collection’s Algorithm will effect the long term performance
Different SSD in QNAP NAS’s FIO consisted performance (IOpattern: RW-4K):

## Slide 37: What is SSD Over-Provisioning
D | D
D | D
D | D
6 pages of new data cannot all be stored to the SSD
N | New Data
D | Valid Data
 | Invalid Data
 | OP
 | OP
N | N
N | N
N | N
With more reserved block, the GC is not required
Unless the SSD conduct GC internally first
N | N
D | 
D | 
N | N
N | N
D | D
D | D
D | D
With limited OP, 4 additional write is needed. With more OP the movement is not required.
SSD Over-provisioning reserves space in the SSD to decrease write amplification & increase consisted performance and endurance.
Reason: to avoid Garbage Collection in any giving point of time

## Slide 38: The Advantage of Software-defined SSD Extra Over-Provisioning
Above: Samsung 850 Pro as Single Disk
Below: Micron M1100 as RAID 1
FIO configuration: runtime=1800 ioengine=libaio direct=1 rw=randwrite bs=4k numjobs=1 iodepth=32
Take Intel S4500 as an example, The continuous random write is 30,000
With QTS, users can assign more OP to the SSD RAID.
At QNAP Lab, the effect of over-provisioning can not only be observed on single consumer-level Samsung 850 Pro to gain the performance same as data center SSD, but also be seem on SSDs as a RAID.

## Slide 39: Choosing SSD is hard, choosing QNAP is simple
SSD consisted performance can only be observed after long time of usage
QNAP has provided the unique SSD Profiling Tool to help user measure the performance difference with different over-provisioning amount.
Not just IT manager, home user can also evaluate the capability of SSD.
Take Intel S4500 as an example, The continuous random write is 30,000
Using SSD Profiling Tool to identify the best OP amount.

## Slide 40: QNAP SSD Global Cache and Qtier
Qtier utilizes SSD space and let data block be reallocated based on hot or cold in the storage
Two options for users to utilize SSD on HS-453DX with M.2 SSD slots
For real-time performance boost, deploy SSD Global Cache or All flash storage
For continued data tiring between hot and cold data, deploy the Hybrid Storage Qtier™ Auto Tiering
Storage pool
Volume
Block-based LUN
HDD
SSD Global
SSD Cache lets all data enter cache and read hot data from the storage in real time
HDD
HDD
HDD
Qtier SSD Tier
Qtier HDD Tier
SSD
HDD
SSD
HDD
Volume
Block-based LUN

## Slide 41: QNAP Global SSD Cache
On HS-453DX, SSD global cache is for all volumes and LUNs:
Read-Only Copy frequently used data to SSD
Read-Write Not only copy data, new data can also be temporarily stored in SSD
Write-Only  Only new data will be written into the cache
Data from clients and storage will both be cached
How Read-write Cache work:
When SSD Space not enough
Read
Write
HDD
IO Intensive
Application
SSD
Read
Write

## Slide 42: Backup or sync data at your choice
NetBak Replicator
Qsync
macOS
Windows
Scheduled or real-time backup/sync
Protection against ransomware!
Time Machine
Qsync

## Slide 43: Enterprise-grade snapshot protection
Less space
Less risk!
Snapshot # Volume / LUN
Snapshot # per NAS
---------------------------------------------------------
1024
256
4GBRAM
≥

## Slide 44: Backup the NAS data
Hybrid Backup Sync
Cloud
Local
Remote

## Slide 45: Notification Center: stay informed at all times

## Slide 46: QVR Pro 24/7 surveillance solution
6,000+ IP cameras
8 ch free recording channels
128 ch max channels (license)
QUSBCam2 webcam recording

## Slide 47: Expand storage via VJBOD
iSCSI
Max 8 remote NAS
VJBOD
Use other NAS capacity to expand own capacity via network connection
10GbE / 1GbE mount

## Slide 48: The QNAP SilentNAS lineup
 | HS-453DX | HS-251+
Processor | Intel Celeron J4105 quad-core 1.5GHz, burst to 2.5GHz (Gemini Lake) | Intel Celeron J1900 quad-core 2.0GHz, burst to 2.42GHz (Baytrail)
Graphics | UHD Graphics 600 | HD Graphics
Encryption acceleration | Yes (AES-NI) | ---
Memory | Max 8GB DDR4-2400 (2 x 4GB SODIMM) | 2GB DDR3L-1333 (non-expandable)
HDD/SSD | 2 x 3.5"/2.5" SATA 6Gb/s | 2 x 3.5"/2.5" SATA 3Gb/s
M.2 SATA SSD | 2 x M.2 2280 SATA 6Gb/s SSD | ---
10GbE network | 1 (10G/5G/2.5G/1G/100M) | ---
HDMI | 4K (1 x HDMI 2.0 + 1 x HDMI v1.4b) | 1080P (1 x HDMI v1.4a)
Speaker | Yes | ---
USB Type-C | Yes (USB 3.0) | ---

## Slide 49: HS- 453DX
10GbE SilentNAS
Copyright© 2018 QNAP Systems, Inc. All rights reserved. QNAP® and other names of QNAP Products are proprietary marks or registered trademarks of QNAP Systems, Inc. Other products and company names mentioned herein are trademarks of their respective holders.