## Slide 2
Your Challenges, Our Solutions
The NAS and/or laptop storage are not enough; how can I upgrade once and expand all?
Notes: 50744223

## Slide 3: So many choices, but which one is the best?
While personal data is growing in both notebook and NAS, is it possible to expand capacity for both sides and allow file exchange between different platforms?
When NAS capacity is nearly full, how to expand its space without purchasing a new NAS and throwing away the old one?
Notes: 70996463, 10965498

## Slide 4: The TR-004 external RAID device
QNAP knows! The first QNAP external RAID device is here!
An external RAID device that supports both 1. Windows/macOS/Linux external storage mode 2. QNAP NAS expansion storage mode to use as an QNAP NAS expansion unit!
1+1 > 2
Storage pool
External devices
NAS
USB 3.0
USB 3.0

## Slide 5: What is External (Hardware) RAID ?
A software RAID uses CPU resources to distribute the IO on different disk to form a RAID protection. The operation of such RAID cannot go beyond the main system.
An external (Hardware) RAID is working independently from CPU, using the standalone microchip to distribute IO, offloading the CPU and allowing operation in different platform.
Client
Software RAID
System
JBOD
USB 3.0
Client
Hardware RAID as a single disk
System
TR-004
USB 3.0
External RAID
CPU
CPU

## Slide 6: QNAP Go Beyond NAS for Your Needs
The TR-004 4-bay USB 3.0 RAID expansion enclosure supports RAID 5 acceleration and protection for replacing your existing USB 3.0 & USB 2.0 single-disk external drives.
Same compatibility standard as NAS to support large capacity HDD.
Easily trasnfer huge amount of data between devices.
Source: https://www.everythingusb.com/speed.html
TR-004 supports Seagate 10 TB IronWolf drive!
0
5
USB 3.1 Gen 1
(USB 3.0)
USB 2.0
0.32 Gb/s
0.48 Gb/s
3.2 Gb/s
4.8 Gb/s
Theoretical speed
Tested speed
Notes: 42962139

## Slide 7: QNAP Go Beyond NAS for Your Needs
Traditional RAID device may only have hardware switch
Integrate with QTS Storage & Snapshot, in NAS storage mode support Storage Pool, Snapshot, Qtier, Qsirch and more!
QNAP unique RAID Manager allow software-managing Single/JBOD/RAID 0/1/5/10 modes and disk health

## Slide 8: TR-004 front view
System status LED
USB status LED
HDD 1~4 LED
Eject button
(works with QTS and QNAP Windows/macOS utility)
Copy button
(works with QTS)
4 x 3.5”/2.5”
SATA 3Gb/s HDD/SSD bays
(w/ lockable trays)
(compatible with SATA 6Gb/s HDD/SSD)
2 x tray keys

## Slide 9: Drive installation and tray locks
01
02
2.5-inch HDD / SSD
3.5-inch HDD

## Slide 10: TR-004 rear view
12CM smart fan
5-speed automatic fan control based on drive and system temperatures
Kensington security slot
USB cable clip
Self-installation with included clip
SET/Confirm button
Press ‘n hold for 3 seconds until a beep to switch between modes
Disk mode dip switch
Individual, JBOD, RAID 0/1/5/10,
Software Control (default)
USB 3.0 Type-C
For USB-C or USB-A host
Power switch
DC 12V power input

## Slide 11: Installing the USB cable clip
03
01
02

## Slide 12: USB Type-C supporting more host types
Optional USB-C to USB-C
cable for USB-C host
TS-251B
Windows PC
Macbook Pro
1-meter (3-foot)
USB-C to USB-A cable included

## Slide 13: Switching between modes (with dip switch)
● Any number of drives
● Each drive capacity separated
Individual
JBOD
RAID 0
RAID 1/10
RAID 5
Software control
(factory default)
● Minimum two drives
● Combined capacity but no fault tolerance
● Minimum two drives
● Combined capacity, best performance but no fault tolerance
● 2 or 4 drives
● RAID 1:
Losing 1-drive capacity for redundancy
RAID 10:
Losing 2-drive capacity (1 for each group) for redundancy
● Minimum 3 drives
● Losing 1-drive capacity for redundancy, enhanced performance
● Any number of drives
● Allows QTS & Windows/macOS utility to control the configuration

## Slide 14: Change disk mode from factory default
The factory default mode is Software Control
Change mode with the dip switch
Note: To change the disk mode with QTS/the utility, the switch needs to remain in the Software Control mode.
Press ‘n hold the “SET” button for 3 seconds until a beep to switch the mode*
*All data on drive(s) will be erased
Software control
(Factory default)
Individual | JBOD
RAID 1/10 | RAID 5

## Slide 15: Switching between modes (with dip switch)
In any mode other than the “Individual” mode (Factory default is Software Control)
Change the dip switch mode to the “Individual” mode
Press ‘n hold the “SET” button for 3 seconds until a beep to switch the mode to individual (reset)*
*All data on drive(s) will be erased
Change the dip switch mode to any other mode
Press ‘n hold the “SET” button for 3 seconds until a beep to switch the mode*
*All data on drive(s) will be erased
Note: To change the disk mode with QTS/the utility, the switch needs to remain in the Software Control mode.

## Slide 16: Save energy & reduce noise w/ sleep mode
TR-004 can enter the sleep mode with just 4.17 watt when these occur:
USB cable removal
The host enters sleep/hibernation*
The host is shut down
or
*depends on host support

## Slide 17: Backward compatible with USB 2.0 port
TR-004 can be supported via a USB 2.0 port on NAS or computers !

## Slide 18
Using TR-004 On Personal Computer
Notes: 分頁要改

## Slide 19: Configure your TR-004 on Windows/macOS - QNAP External RAID Manager
With TR-004, you can create a disk array by the hardware dip switch or the QNAP External RAID Manager app on your PC/Mac.
Monitor TR-004, RAID, and disk status with this utility
Supported platforms and OS version
Windows: Windows 7 (or later)
Mac: macOS 10.11 (or later)

## Slide 20: Monitor disk health
The disk color on the TR device shows disk's status. Click each of them to check the disk information
Show all disks in "Disk Information". Click status to get advanced info of disk's S.M.A.R.T information.
Quick overview
Check information

## Slide 21: Creating RAID group in two steps
Various RAID types for users to create, multiple RAID are also available in QNAP External RAID Manager
Intuitive settings: create RAID group in just two steps
In "RAID Configuration" page,
click "+RAID Group" to start
Choose RAID type, disks you want to use, and resync priority
RAID types:
JBOD, RAID 0, RAID 1, RAID5, RAID 10 Disks
Resync priority:
Service First, Default, Resync First

## Slide 22: Format RAID group
Choosing exFAT file system allows your files be exchanged between Windows, Mac & NAS without problem!
Once the RAID is set up, format the RAID to begin storing files to the disk
Direct to operating system interface for formatting
Windows: Disk Management
Mac: Disk Utility
Note: to use TR-004 in exFAT format with QNAP NAS, optional exFAT license is required.

## Slide 23: Instant notification when RAID is abnormal
When RAID degraded or failed, users will be notified by the UI, with desktop notification and with device beep.

## Slide 24: RAID protection mechanism with system events logs
Same as NAS, when RAID is degraded, insert new disk to start rebuilding while shows progress percentage
Any idle disk can be used as the spare disk without any setting while the RAID is in degrade
Logs are independent from operating system, quickly know and export events

## Slide 25: Notification for new version of firmware and application
When there is a new version, pop-up notifications will inform users
Check utility and firmware versions

## Slide 26: Use RAID Manager to create RAID group on Windows, and copy a 5GB file

## Slide 27: Using TR-004 with exFAT to transfer media file between platforms
A TR-004 external RAID can operate on different platforms
But the FAT32 format can only support single file up to 4GB.
With QNAP exFAT license, large files can be transferred between Windows/Mac/QNAP NAS
Scenario 1
Notes: https://tw.123rf.com/%E7%B4%A0%E6%9D%90%E5%9C%96%E5%BA%AB/gamer.html?imgtype=0&oriSearch=save+the+money&sti=mkdchaommjirpvme6i|&mediapopup=51967685

## Slide 28: How to choose the TR-004 partition format?
File System | QNAP QTS | Windows | macOS | Linux
exFAT | V (License needed) | V | V | V(Manually install needed)
NTFS | V | V | V (Read-only) | V
APFS | - | - | V | -
HFS+ | V | - | V | -
EXT4 | V | - | - | V
FAT32 | V (4GB file limitation) | V (4GB file limitation) | V (4GB file limitation) | V (4GB file limitation)
File system support status on different platforms:
*It is possible for an OS to install third party software to recognize unsupported file systems

## Slide 29: Advantages of QNAP External RAID Manager
Creating RAID group in two steps
Overview device, disk, and RAID info and status
Record all device events and find out the info by filter or typing the keyword
Desktop notification to inform abnormal status
Notification for new version of firmware and application
Intuitive and easy
Instant notification, quickly control
System events for troubleshooting
When RAID is degraded, insert new disk to rebuild RAID
RAID rebuild, data protection
Export to .csv file
Show the progress percentage of rebuilding

## Slide 30
Using TR-004 on QNAP NAS
Notes: 分頁要改

## Slide 31: Replacing UX-500P with TR-004
Function | QNAP TR-004 | UX-500P | Other external RAID device
Connection Type | USB 3.0 | USB 3.0 | By device
Slots | 4 | 5 | By device
Supported systems | QNAP QTS, Windows, Mac, Linux etc... | QNAP QTS | QNAP QTS, Windows, Mac, Linux etc...
Disk health monitoring | Supported | Supported | Not Supported
External RAID protection | Supported | Not Supported | Supported
Expand Storage Pool | Supported | Supported | Not Supported
RAID migration, replacing disk | Not Supported | Supported | Not Supported
Notes: 截圖看這兒 ：https://www.asus.com/tw/Motherboards/X99-E-10G-WS/

## Slide 32: Performance comparison between TR-004 and UX-500P
200
100
306
211
300
353
204
TR004
UX-500P
R
W
400
R
W
0
(MB/s)
20%
10%
23%
28%
30%
19%
24%
TR004
UX-500P
40%
0
(%)
Especially suitable to be used on the ARM-based model to release CPU resource
In QNAP lab, TR-004 & UX-500P with 4 Samsung SSD RAID 5 to compare the sequential performance.
Test standard:
TR-004 external RAID performance is same as UX-500P but NAS CPU usage is reduced for 5%.
Test standard ： fio --direct=1 --rw=write --bs=1M --runtime=180 --size=32G --name=test-write --ioengine=libaio --iodepth=1 fio --direct=0 --rw=randwrite --bs=4K --runtime=180 --size=32G --name=test-write --ioengine=libaio --numjobs=1 --iodepth=1 --refill_buffers --group_reporting
Read
Write
Read
Write

## Slide 33: Official External RAID device provide better protection
When using third party external RAID device to expand NAS, the disk health cannot be monitored.
TR-004 disk can be monitored in Storage & Snapshot for best protection.
Functions: - QTS Disk monitoring - External RAID monitoring
- Disk S.M.A.R.T.
- Customized temperature alert - Notification Center push notification and more!
Notes: 截圖看這兒 ：https://www.asus.com/tw/Motherboards/X99-E-10G-WS/

## Slide 34: Create Storage Pool with TR-004
The TR-004 is in external storage mode until a storage pool or static volume is created.
When configuring the external RAID type with QTS, the hardware dip switch at TR-004 needs to be switched to software control first to prevent data loss due to misconfiguration.
3 Steps
01
Disk/VJBOD > Select a TR-004 Disk > Configure
02
Change the external RAID type in the wizard
03
Storage/Snapshot > Create Storage Pool > Select TR-004 external RAID
Notes: 截圖看這兒 ：https://www.asus.com/tw/Motherboards/X99-E-10G-WS/

## Slide 35: Easily Manage External RAID
With the integration from QTS, a new external RAID management page is provided for below operations:
An External RAID can only be removed when its associated Storage Pool and Volume are removed.
- Monitoring external RAID
- Setup Spare Disk
- Configure Disk Resync Priority
- Change RAID Mode
- Remove External RAID
- Update External RAID Device
- Firmware Version
Notes: 截圖看這兒 ：https://www.asus.com/tw/Motherboards/X99-E-10G-WS/

## Slide 36: Transfer data from TR-004 to NAS, and change mode to expand the NAS

## Slide 37: Using TR-004 as NAS expansion or backup space
The TR-004 can be used to create storage pool and volume to store data while using Qsirch and Qfiling to move data around.
Or be used as a backup or snapshot replica destination for data protection.
Expanding the NAS with new volume
Work as backup destination for snapshot replica
Scenario 2
Notes: 截圖看這兒 ：https://www.asus.com/tw/Motherboards/X99-E-10G-WS/

## Slide 38: Transfer the snapshot exported file
While in external storage mode, the TR-004 can store exported snapshot image file.
Transfer the image file manually to clone volume or LUN without using the network.
Using TR-004 to transfer data when network is not stable or not fast enough
Scenario 3
Notes: 截圖看這兒 ：https://www.asus.com/tw/Motherboards/X99-E-10G-WS/

## Slide 39: QNAP TR-004 A new generation of NAS expansion unit
External storage/ NAS storage mode
Complete disk monitoring
Fully integration with QTS to use just like JBOD
External RAID with extra protection
QTS 4.3.5 with TR-004 support will be released soon.
A NAS that cannot be upgraded to 4.3.5 dose not support
TR-004 NAS Storage Mode, TS-128, TS-228 also does not support such mode.

## Slide 40
Copyright © 2018 QNAP Systems, Inc. All rights reserved. QNAP® and other names of QNAP Products are proprietary marks or registered trademarks of QNAP Systems, Inc. Other products and company names mentioned herein are trademarks of their respective holders.