## Slide 2
Product
Overview

## Slide 3: 10GbE NAS with Intel Xeon E CPU
TS-x83XU NAS Series
TS-2483XU-RP-E2136-16G
TS-1683XU-RP-E2124-16G
TS-1283XU-RP-E2124-8G
TS-883XU-E2124-8G
TS-883XU-RP-E2124-8G
TS-983XU-E2124-8G
TS-983XU-RP-E2124-8G
E-2124
4-core
E-2124
4-core
E-2136
6-core
E-2124
4-core
E-2124
4-core

## Slide 4: Revamped QNAP Extended Warranty
https://www.qnap.com/service/product-warranty/
Sign in
Product registration
Purchase extended warranty
3 year standard ＋2 year extended warranty = Up to 5-year warranty

## Slide 5: Enterprise Processor - Xeon
Intel® Turbo Boost Technology
Processors

## Slide 6: ECC Memory (Error Correcting Code)
Intel Xeon processors support ECC which can automatically detects and repairs single-bit error on-the-fly.
Running reliably without data corruption

## Slide 7: The majority of single-event errors in memory chips
Electrostatic discharge
Electromagnetic interference (EMI)
Lowering voltage
Background radiation

## Slide 8: How ECC Works
Data read from memory
Send to applications
Detect and repair
ECC code generated
Compare ECC code
Repair and send
Newly generated ECC Code
ECC Code
Data

## Slide 9: Complete Product Lines- 1U 9-bay
9-bay
5 x 2.5-in ports (inside)
4 x 3.5-in ports
Redundant PSU 2x300W
TS-983XU-RP-E2124-8G
Intel® Xeon® E-2124 4-core 3.3 GHz processor, max boost to 4.3 GHz
8GB DDR4 ECC RAM (2x 4GB)
TS-983XU-E2124-8G
Intel® Xeon® E-2124 4-core 3.3 GHz processor, max boost to 4.3 GHz
8GB DDR4 ECC RAM (2x 4GB)
Single PSU 250W

## Slide 10: Complete Product Lines- 2U 8-bay
8-bay
TS-883XU-RP-E2124-8G
Intel® Xeon® E-2124 4-core 3.3 GHz processor, max boost to 4.3 GHz
8GB DDR4 ECC RAM (2x 4GB)
TS-883XU-E2124-8G
Intel® Xeon® E-2124 4-core 3.3 GHz processor, max boost to 4.3 GHz
8GB DDR4 ECC RAM (2x 4GB)
Redundant PSU 2x300W
Single PSU 350W

## Slide 11: Complete Product Lines- 2U 12-bay
12-bay
TS-1283XU-RP-E2124-8G
Intel® Xeon® E-2124 4-core 3.3 GHz processor, max boost to 4.3 GHz
8GB DDR4 ECC RAM (2x 4GB)
Redundant PSU 2x300W

## Slide 12: Complete Product Lines- 3U 16-bay
16-bay
TS-1683XU-RP-E2124-16G
Intel® Xeon® E-2124 4-core 3.3 GHz processor, max boost to 4.3 GHz
16GB DDR4 ECC RAM (2x 8GB)
Redundant PSU 2x500W

## Slide 13: Complete Product Lines- 4U 24-bay
24-bay
TS-2483XU-RP-E2136-16G
Intel® Xeon® E-2136 6-core 3.3 GHz processor, max boost to 4.5 GHz
16GB DDR4 ECC RAM (2x 8GB)
Redundant PSU 2x800W

## Slide 14
Hardware
Introduction

## Slide 15: Enjoy Qtier and SSD cache in a 1U NAS
4 x 3.5”SATA 6Gb/s HDD/SSD ports
LED indicators:
System status, network, disks
5 x 2.5”
SATA 6Gb/s SSD ports

## Slide 16: TS-983XU/TS-983XU-RP Rear View
1 x low profile PCIe slot
4 x USB 3.1 Gen 1 ports
2 x USB 3.1 Gen2 (10G) ports
2 x GbE RJ45 ports
250W
2 x 300W
Redundant PSU
Single PSU
2 x 10GbE SFP+ ports
*PCIe 3.0 x16
Notes: 白手起家款

## Slide 17: TS-983XU SSD Installation
01
02
03
04
05

## Slide 18: 2U/3U TS-x83XU Front View
24/ 16/ 12/ 8 x 3.5”SATA 6Gb/s HDD/SSD ports
TS-1283XU-RP
TS-883XU / TS-883XU-RP
TS-1683XU-RP
TS-2483XU-RP
Notes: 白手起家款

## Slide 19: 2U/3U/4U TS-x83XU Front View
2U
3U
4U
Power switch
LED indicators: system status, network, external expansion enclosures, disks
Notes: 白手起家款
2U/3U

## Slide 20: 2U/3U/4U TS-x83XU Rear View
8-bay
12-bay
Single PSU
Redundant PSU
2 x 10Gb SFP+ SmartNIC ports
4 x 1Gb ports
USB 3.1 Gen2 (10G) Type-A & Type-C port
24-bay
Redundant PSU
Redundant PSU
Single PSU

## Slide 21: Industry-leading PCIe expansion options
QM2 provides 10GBASE-T port and/or M.2 SSD slots for SSD cache or Qtier tiered storage for optimized storage performance.
USB 3.1 Gen 2 expansion cards provide 10Gb/s for external USB devices．Type-A port is also backward compatible with USB 3.0/2.0 devices.
SAS expansion card is for adding support of REXP expansion units for up to 40 additional SAS/SATA drives.
40/25/10GbE and wireless network expansion cards
provide high bandwidth, low latency, or wireless AP functionality.

## Slide 22: TS-x83XU PCIe Slots
1
2
3
4
1
2
3
4
1
1U/2U: low profile
3U/4U: full height
1
2
4
5
3
Notes: 這頁需要

## Slide 23: PCIe Slot Configuration (2U/3U)
#3
#2
#1
PCIe x8
(CPU)
#4
PCIe x4
(PCH)
PCIe x4
(CPU)
PCIe x4
(CPU)

## Slide 24: 2U/3U NAS PCIe Slot Suggestion
To ensure that the SATA drives have sufficient bandwidth, slot #1 is PCIe Gen2 x4
PCIe Slot 2
PCIe Slot 3
PCIe Slot 4
HDDs
DMI
(PCIe Gen3 x4)
Gen3 x8
Gen3 x4
Gen3 x4
PCIe Slot 1
Gen2 x4
Pre-installed with a 10GbE NIC
DMI Bottlenecks
Low-speed card (such as a 1GbE NIC, USB adapter)
High-speed expansion card (such as 10/40GbE NIC, SAS expansion card & GPU card)

## Slide 25: PCIe Slot Specifications (4U)
#2
#1
PCIe x8
(CPU)
#4
#5
#3
PCIe x4
(PCH)
PCIe x4
(PCH)
PCIe x4
(CPU)
PCIe x4
(PCH)

## Slide 26: 4U NAS PCIe Slot
To ensure that the SATA drives have sufficient bandwidth, Slot #1, #3 & #5 is PCIe Gen2 x4
Low-speed card(such as a 1GbE NIC, USB adapter)
High-speed expansion card (such as 10/40GbE NIC、SAS expansion card、GPU card)
HDD 1- 4
HDD 9- 12
HDD 5- 8
HDD 21- 24
DMI
(PCIe Gen3 x4)
PCIe Slot 2
Gen3 x4
PCIe Slot 1
Gen2 x4
PCIe Slot 3
Gen2 x4
PCIe Slot 5
Gen2 x4
PCIe Slot 4
Gen3 x8
DMI Bottlenecks
Pre-installed with a 10GbE NIC

## Slide 27: GPU card slots and supported dimensions
NAS | Slot | Dimension W x H x L (mm)
TS-983XU TS-983XU-RP | Slot 1 | 19 x 68.9 x 257
TS-883XU TS-883XU-RP | Slot 2 | 37 x 68.9 x 214
 | Slot 4 | 37 x 68.9 x 214
TS-1283XU-RP | Slot 2 | 37 x 68.9 x 214
 | Slot 4 | 37 x 68.9 x 214
TS-1683XU-RP | Slot 2 | 38.5 x 111 x 214
 | Slot 4 | 38.5 x 111 x 214
TS-2483XU-RP | Slot 2 | 55 x 138 x 312
 | Slot 4 | 55 x 138 x 312
W
H
L

## Slide 28: Supports up to 64 GB Memory
Supports Dual-channel and Long-DIMM x4
Installing memory in pair to take advantage of dual-channel
One module
Tow modules
Install in A0 and B0 slots
Install in A0 slot

## Slide 29: TS-x83XU Memory Accessories
Ordering number | Specification
RAM-4GDR4ECA0-UD-2666 | DDR type: ECC DDR4(288PIN) Capacity: 4GB Manufacturer: Apacer Frequency: DDR4-2666 Manufacturer P/N: 78.B1GSB.4050B
RAM-8GDR4ECA0-UD-2666 | DDR type: ECC DDR4(288PIN) Capacity: 8GB Manufacturer: Apacer Frequency: DDR4-2666 Manufacturer P/N: 78.C1GSC.4050B
RAM-16GDR4ECA0-UD-2666 | DDR type: ECC DDR4(288PIN) Capacity: 16GB Manufacturer: Apacer Frequency: DDR4-2666 Manufacturer P/N: 78.D1GSC.4010B

## Slide 30: Tool-less Rail Kit
RAIL-B02
RAIL-A03-57
RAIL-A02-90
Supported NAS:
TS-883XU/1283XU
Max. Load: 20kg
Supported NAS:
TS-1683XU
Max. Load:57kg
Supported NAS:
TS-2483XU
Max. Load: 90kg

## Slide 31: Hardware upgrade made easy
Pull it out and lift
up the cover

## Slide 32
Versatile Applications

## Slide 33: More Efficient Backup with USB 3.1 Gen 2
USB 3.0
USB 3.1
5Gb/s
10Gb/s
2X
SPEED UP
USB 3.0
TYPE-C
TYPE-A
Notes: Type-A是紅色的

## Slide 34: Do more with graphics cards
QuAI
Support half-height GPU cards that require no external power: NVIDIA GT1030, etc.
TS-1683XU-RP
Support full-high GPU cards & GPU cards requiring external power
3U/4U NAS 500W+ power supply
2U NAS 350W/300W power supply

## Slide 35: Add-on GPU Card Applications
AI
Computing Acceleration
QTS
Transcoding Acceleration
Virtualization Station
GPU Passthrough

## Slide 36: Ride the AI wave with "QuAI"
QNAP QuAI
AI Developer Package
QuAI is intended for data scientists and developers to quickly build, train,
and optimize their AI models on QNAP NAS.
+
=
QuAI
AI
QNAP NAS
+
GPU accelerated
computing

## Slide 37
Virtualization Station
HybridDesk Station, Linux Station
QVR Pro Client (HD Station)
Video Station
Plex Media Server
Smooth Video Experience

## Slide 38: QTS & virtualization increase productivity
Supports Windows/Linux VMs and containers
QTS 4.3.5
Storage & Snapshot Manager, and new virtualization network functions
Virtualization
Station
Container
Station

## Slide 39: GPU boosts image/video processing
H/W accelerated with GPU to lower CPU usage.
w/ GPU
w/o GPU
For OpenGL & DirectX applications

## Slide 40: Super high capacity surveillance
Surveillance Station 5.1
Default: 8 free channels
Max: 80 Ch. (optional license)
QVR Pro
Default: 8 free channels
Max: 128 Ch. (optional license)
QUSBCam2
Up to 1080p USB Webcam recording

## Slide 41
Network Interface

## Slide 42: High-Speed Connectivity Supported by Mellanox
Source: Mellanox
Notes: 高速傳輸領導廠商Mellanox 技術支援
High speed Ethernet Leading company Mellanox.

## Slide 43: 10/25/40 GbE SmartNIC with offload function
Buit-in Mellanox ConnectX-4 Lx 10GbE SmartNIC
Supports 25/40GbE expansion
Supports iSER
Notes: 更新筆記: "內建" 與 Mellanox 間加一空格 (By Teresa)

## Slide 44: Offload tasks from CPU with iSER
iSER allows data to bypass general network drivers, the socket layer, and to directly enter memory buffers of the server and storage.
Increasing performance, lower CPU loading
With iSER
Without iSER

## Slide 45: iSER makes VMware Faster
When VMware Server and NAS are iSER ready:
  Random read/write performance is 60% higher than iSCSI
  Latency is 50% lower than iSCSI

## Slide 46: Built-in dual 10GbE SFP+ ports
10GbE x 2 (Throughput)
2000
1500
0
Read
Write
2358
2286
2500
Tested in QNAP Labs. Figures may vary by environments.
Test environment: NAS: TS-1283XU-RP-E2124-4G with QTS 4.3.5
Volume type: RAID 5; 16 x Intel S3500 240GB SSDs (SSDSC2BB240G4)
(MB/s)

## Slide 47: >25GbE Market Moves Faster Than Ever
The estimated market share of >25GbE will be doubled to nearly 55% (after 2018) from 22% (2017)
High speed adapters are expected to grow rapidly in Cloud, Big Data, High speed storage, Virtualization and A.I. segments.
Chart: 
| 10G | 25G | 40G | 50G | 100G | 200G
銷售 | 0.45 | 0.15 | 0.02 | 0.15 | 0.21 | 0.02
45%
15%
2%
2%
15%
21%
Chart: 
| 10G | 25G | 40G | 50G | 100G | 200G
銷售 | 0.78 | 0.07 | 0.11 | 0.02 | 0.02 | 0
78%
7%
11%
2%
2%
Of total Market
22%
25G+ Segment Growing at 38% CAGR
High Speed Adapters 2017 ($1.3B)
Notes: 25GbE以上市場大幅成長
Fast growing high speed adapter market over 25GbE
25GbE 以上高速傳輸市場佔有率預計由22%(2017)成長兩倍至55%(after 2018)
The estimated market share of over 25GbE will be doubled to nearly 55% (after 2018) from 22% (2017)
因應未來雲端應用, 大數據, 高速儲存, 虛擬運用與人工智慧
High speed

## Slide 48: Mellanox ConnectX®-4 Lx NIC
RoCE (L2) and RoCEv2 (L3) hardware offload
Ideal for low latency and high speed big data transferring
Supports RDMA Over Converged Ethernet (RoCE)
Notes: http://www.roceinitiative.org/roce-introduction/

## Slide 49: QNAP Dual-port 25GbE NIC
QXG-25G2SF-CX4
Mellanox ConnectX®-4 Lx NIC
2 x SFP28 ports
Supports 25GbE/10GbE
Supports iSER/RoCE hardware offload
Cooling system
Compatible cable
SFP28 25/10GbE DAC cable

## Slide 50: Mellanox SN2010 10/25GbE and 40/100GbE switch
Build 25GbE Ready high speed ethernet
18 x 10/25GbE SFP28 port
4 x 40/100GbE QSFP28 port

## Slide 51: Fibre Channel SAN
Use Fibre channel protocol with SCSI command to transmit block-level data
32Gbps FC is now commercial and moving to a faster speed. Its speed and lower latency are suitable for high density computing and storage
來源: https://fibrechannel.org/wp-content/uploads/2018/08/FCIA_SolutionsGuide2018_web.pdf

## Slide 52: Fibre Channel applications
​Databases
Small in size but huge in numbers data packets transfers
FC SAN provides high IOPS and lower latency
​4K & 8K media storage & editing
Huge storage space demand for TV programs and footage
FC environment for longer distance video access and real-time editing
Bank transactions
Need low-latency storage
Higher security for data segregation between FC and Ethernet

## Slide 53: Integrating Fibre Channel SAN services
QTS 4.4.1 will support FC SAN: single NAS to provide SAN, NAS and cloud storage for unified storage solution
Partnering with FC card vendor Marvell & ATTO for the most economical FC SAN storage solution
Support ATTO
Celerity 32Gb/16Gb/8Gb FC card
Support Marvell
Qlogic 32Gb/16Gb/8Gb FC card

## Slide 54
Release full potentials of SSD
SSD Over-provisioning, Snapshot Remote Restore

## Slide 55: SSD Usage In Network Attach Storage
Drive Type | Sequential Access (MB/s) | Random Access (IOPS)
HDD | 100 | 350
SSD | 300 | 60000
https://www.sandisk.com/business/datacenter/resources/white-papers/the-ssd-enabled-pc-total-cost-of-ownership
SanDisk‘s Statistic for Global SSD/HDD Price Trend
SanDisk evaluate the 256 GB SSD per GB price in 2018 is only 30% compare to 2013
SSD can provide high random IOPS for multi-clients sync and business applications that can not be achieved by HDD.
In 2018, SSD price also comes close to the sweet spot.
Besides choosing the right SSD, you should also choose right NAS!

## Slide 56: QNAP SSD Global Cache and Qtier
Storage Pool
Volume
Block-based LUN
HDD
HDD
HDD
HDD
Qtier Pool SSD Tier
HDD
HDD
SSD Cache
SSD
SSD
Qtier Pool HDD Tier
SSD Cache let all data enter cache and read hot data from the storage in real time
Qtier utilizes SSD space and let data block be reallocated based on hot or cold in the storage
Volume
Block-based LUN
IT manager can have different SSD configurations with TS-x83XU
For real-time performance boost, deploy SSD Global Cache or All flash storage
For continued data tiering between hot and cold data, deploy the Hybrid Storage Qtier™ Auto Tiering

## Slide 57: Different SSD has Different Performance!
SSD Write amplification cause performance degradation
In QNAP Lab, engineer use FIO to test different SSD, and all SSD have showed consisted write performance degrade.
Different SSD's controller and Garbage Collection Algorithm will effect the long term performance
Different SSD in QNAP NAS’s FIO consisted performance (IOpattern: RW-4K):
How can storage vendors help to ensure SSD has expected performance?
Notes: 57

## Slide 58: What is SSD Over-provisioning
D | D
D | D
D | D
6 pages of new data cannot all be stored to the SSD
N | New D
D | Valid D
 | Invalid D
 | OP
 | OP
N | N
N | N
N | N
With more reserved block, the GC is not required
Unless the SSD conduct GC internally first
N | N
D | 
D | 
N | N
N | N
D | D
D | D
D | D
With limited OP, 4 additional write is needed. With more OP the movement is not required.
SSD Over-provisioning reserves space in the SSD to decrease write amplification & increase consisted performance and endurance.
Reason: to avoid Garbage Collection in any giving point of time
Notes: 58

## Slide 59: The Advantage of Software-defined SSD Extra Over-provisioning
With QTS, user can assign more OP to the SSD RAID.
At QNAP Lab, the effect of over-provisioning can not only be observed on single consumer-level Samsung 850 Pro to gain the performance same as data center SSD, but also be seem on SSDs as a RAID.
Above: Samsung 850 Pro as Single Disk
Below: Micron M1100 as RAID 1
FIO configuration: runtime=1800 ioengine=libaio direct=1 rw=randwrite bs=4k numjobs=1 iodepth=32
2*Micron M1100 RAID 1 Random Write IOPS with Dynamic OP
Notes: 59

## Slide 60: Choose SSD is Hard, Choose QNAP is Simple
IT managers' biggest challenges in deploying SSD is to measure the SSD performance and how it can solve storage bottleneck.
With QNAP SSD Profiling Tool, users can not only set OP, but further test SSD RAID performance with different OP amount.
IT managers can decide the best practice directly on production site
Notes: 60
73652517

## Slide 61: QNAP Global SSD Cache
The QNAP SSD Cache can be applied to multiple volume / LUN
Read-Only Copy frequently used data to SSD
Read-Write Not only copy data, new data can also be temporarily stored in SSD
(New) Write-Only  Only new data will be written into the cache
Data from clients and storage will both be cached
How Read-write Cache work:
When SSD Space not enough
Read
Write
Read
Write
HDD
IO Intensive
Application
SSD
Cache Type

## Slide 62: The Write-only Cache Increase ROI of SSD Cache with high Writing Demand
Write-only cache is promoted by Microsoft for endurance control.
QNAP believe Write-only Cache can increase the ROI of purchasing SSD in below scenario:
https://docs.microsoft.com/en-us/windows-server/storage/storage-spaces/understand-the-cache
SSD
SSD
NVMe
SSD
SSD
NVMe
Writes are cached
Reads are NOT
File Server focusing on write operations
Database with more write operation (Such as IOT monitoring server)
Use high endurance SSD (Intel Optane™) with other SSD
Notes: 62

## Slide 63: Qtier (Auto-Tiering) Increase Capacity and Performance at the Same Time
Hot Data
Warm Data
Cold Data
Access Pattern Change
Before Tiering
Data place not optimized
Start Tiering
After Tiering
Performance optimized
Qtier
Engine
Beside SSD Cache,
Qtier™ can migrate
data between SSD and
HDD directly
SSD capacity can be
utilized with limited
memory requirement.
Notes: 63
93325809

## Slide 64: Qtier 2.0 IO Aware tiering for real time performance boost
Beside tiering on
schedule, Qtier now
can simulate SSD
Cache behavior
It can utilize SSD
capacity while boost
performance in real
Time thus increase SSD
ROI
SSD Tier
C、D data block be written to HDD due to SSD full
HDD Tier
A
B
C
D
Block | Hit
C | 50
D | 50
D data block be promoted as access frequency increase
HDD Tier
A
B
C
Data
Blank
D
SSD Tier
Block | Hit
C | 50
D | 200
Notes: 64
93325809

## Slide 65: TS-x83XU SSD Multiple Configurations
In addition to acting as a backup server, SSD Over-provisioning, Global Cache and Qtier let TS-x83XU be deployed as production server
Scenario | File Server | Web, Application, Virtualization Server | Collaboration, Video Editing | Surveillance, Backup, Log Server | Business-Critical Database
SSD Config | Qtier™ | Qtier™ | Read-Write Cache | Write-Only Cache | SSD RAID
SSD RAID | RAID 6 | RAID 10 | RAID 5 | RAID 10 | RAID 10
SSD OP | 10% | 20% | 20% | 30% | 30%
With 5 x 2.5”
SATA 6Gb/s SSD 1U Rackmount can use SSD too!
Notes: 65

## Slide 66: Businesses need lower RTO
Taiwan IThome survey 2017
Data Backup Time
Server Online
Disaster Happen
Recover Point Objective
Recover Time Objective
TIME
Can businesses only manually transfer data back from the remote end when disaster happen?
In the survey of 300 Enterprises and SMBs at Taiwan:
60% has used Remote Replication as Backup Plan.
50% of businesses expected the recovering time should be within 1 Hour.
But also 50% of businesses experience actual recovering exceed 1 Day!
Notes: 66
39094200

## Slide 67: Restore From Remote Snapshot Vault
The Snapshot Manager is now actively connected to Snapshot Vault
Support monitor and restore selected folders and files from the source NAS directly!
Both the source and destination NAS must be upgraded to 4.3.5 to support this function
Notes: 67

## Slide 68: Drastically Reduce Recover Time With 10GbE Network
The Remote Snapshot Vault Recovering is based on Ethernet service.
Using 1GbE network, recovering large data still takes hours.
Pair the Snapshot Replica Solution with 10GbE or even faster interfaces to increase both the backup and recovery speed !
Using QNAP 10GbE Switch to replace old 1GbE for reducing RTO dramatically
Notes: 68

## Slide 69: The Forth Way: Snapshot Export / Import
Export a snapshot from snapshot manager or snapshot vault
Using external storage device, the exported imaged can be imported to another NAS to create new volume or LUN
The same image can also be used to revert source volume or LUN
When network speed is limited, user can still import snapshots for reverting
Snapshot Reverting
Notes: 36588464

## Slide 70: With QTS 4.3.5 Power of Storage:
01
Software-defined SSD Extra OP
Measure & set unique over-provisioning amount on the NAS
02
SSD Global Cache & Qtier™
Using Cache or Auto Tiering to maximum SSD ROI
03
Remote Snapshot Restore
Using 10GbE network to reduce RTO
Notes: 36588464

## Slide 71
©2018著作權為威聯通科技股份有限公司所有。威聯通科技並保留所有權利。威聯通科技股份有限公司所使用或註冊之商標或標章。檔案中所提及之產品及公司名稱可能為其他公司所有之商標 。
Copyright© 2018 QNAP Systems, Inc. All rights reserved. QNAP® and other names of QNAP Products are proprietary marks or registered trademarks of QNAP Systems, Inc. Other products and company names mentioned herein are trademarks of their respective holders.
is your best choice!