## Slide 2
The Explosion of Data

## Slide 3
Three Ways to Expand Your QNAP NAS
A. Online RAID Capacity Upgrade
Replaces disk one by one
Takes time in RAID rebuilding
1TB
4TB
B. QNAP vJBOD
High-speed network is required
Need to purchase another NAS
10GbE Network
NAS
NAS
NAS
C. Expand with JBOD
Direct attached storage
Need to purchase JBODs
NAS
JBOD
Direct cable connection

## Slide 4
JBOD Expansion is Straightforward
JBOD: Just a Bunch of Disks.
Plug and use, ease of management
JBOD
NAS
Direct cable connection

## Slide 5
QNAP Expansion Solutions
EJ series-SAS 12Gb/s dual controller JBOD
REXP series-SAS 12Gb/s single controller JBOD
REXP-1620U-RP
REXP-1220U-RP
TX series-Thunderbolt 2 JBOD
TX-800P
TX-500P
TR-002
TR-004
UX-1200U-RP
UX-800U-RP
TR series- USB 3.1 RBOD
UX series-USB 3.0 JBOD
EJ1600 v2

## Slide 6
 | EJ seires | REXP seires | TX seires | TR seires | UX seires
Protocol | SAS | SAS | Thunderbolt 2 | USB 3.1 | USB 3.0
Host connect interface | miniSAS HD (SFF-8644) | miniSAS HD (SFF-8644) | Thunderbolt 2 (miniDP) | USB Type-C | USB Type-A
Bandwidth | 48Gbps | 48Gbps | 20Gbps | 10Gbps | 5Gbps
Supported HDD | SAS 12Gbps SATA 6Gbps | SAS 12Gbps SATA 6Gbps | SATA 6Gbps | SATA 6Gbps | SATA 6Gbps
Independent pool | Yes | Yes | Yes | Yes | Yes
Expand NAS pool | Ye | Yes | No | No | No
QNAP JBOD Comparison

## Slide 7
Advantages of SAS Protocol

## Slide 8
Source: Seagate Technology
SAS
SAS protocol has mission-critical features for the business
SAS v.s. SATA

## Slide 9
Full-Duplex and Dual-Pot
SAS HDD
SATA HDD
Full-duplex transmission
Transmits in both directions at the same time
Dual-port
Supports HA architecture
Half-duplex
Transmits in one direction at a time
Channel 1
Channel 2
SAS host 1
SAS host 2
SATA host 1
Channel 1

## Slide 10: SAS Wide Port and Bandwidth
SFF-8644 mini-SAS HD is wide port which includes 4 PHY
Each PHY provides 12Gb/s bandwidth
A wide port can provide up to 48 Gb/s bandwidth
NAS
JBOD
SFF-8644 Connector
SFF-8644 connector

## Slide 11: SAS Connector
SFF-8644 (mini-SAS HD)
48Gb/s data rate (12Gb/s x 4 lane)
SFF-8088 (mini-SAS)
24Gb/s data rate (6Gb/s x 4 lane)

## Slide 12
QNAP SAS JBOD Solutions

## Slide 13
EJ1600 v2 Dual-controller JBOD
2x COM port
3 x mini-SAS HD wide port
Power Button
LED indicator
LED indicator
3U 16-bay Dual-controller. Supports hot-plug.
Broadcom expander
450W redundant power supply

## Slide 14
REXP-1620U-RP
2x COM port
3 x mini-SAS HD wide port
Power button
Power button
LED indicators
JBOD ID
3U 16-bay single-controller
Broadcom expander
450W redundant power supply

## Slide 15
REXP-1220U-RP
2x COM port
3 x mini-SAS HD wide port
Power button
Power button
LED indicators
JBOD ID
2U 12-bay single-controller
Broadcom expander
450W redundant power supply

## Slide 16
QNAP SAS Adapter and Cables
SAS-12G2E
8 port SAS 12Gb/s card
CAB-SAS05M-8644
CAB-SAS10M-8644
CAB-SAS20M-8644
CAB-SAS30M-8644
Mini-SAS HD cable (12Gb/s)
Mini-SAS to Mini-SAS HD cable
CAB-SAS05M-8644-8088
CAB-SAS10M-8644-8088
CAB-SAS20M-8644-8088
CAB-SAS30M-8644-8088

## Slide 17
ES NAS High Availability Cabling Instruction
Dual-controller
ES NAS
Dual-controller
EJ series JBOD
Daisy-chain up to 7 EJ1600 v2
Avoids single point of failure
  Multipath function allows to access data even when one controller has failed
System can operate when a cable or a controller has failed.

## Slide 18
Turbo NAS Cabling Instruction
Tier 1
Tier 2
Tier 3
Tier 4
Turbo NAS
REXP JBOD
Daisy chained up to 8 REXP or 4 tier
High availability is not supported

## Slide 19
JBOD Applications

## Slide 20
Three Key Applications
Capacity Expansion
Local Data Backup
Data Migration

## Slide 21
Capacity Expansion
NAS
JBOD
NAS
JBOD
Original pool in NAS
Expanded pool capacity
Pool A in NAS
Pool B in JBOD
Expand existing pool in NAS
Independent pool in JBOD
Video folder
User A folder
User B folder
User C folder

## Slide 22
Import data to NAS B
1
Copy data to a JBOD
2
B
A
Data Migration
QJBOD Express for transfering huge amount of data
48 Gb/s high-speed to reduce time
SAS cable (48 Gb/s)
JBOD
JBOD
SAS cable (48 Gb/s)

## Slide 23
Back up Data at Local Site
Snapshot Replica supports incremental and versioning backup
  Against Ransomware infection
  Data recovery when multiple disks have failed in a RAID group
  SAS 48 Gb/s high speed data transferring to shorten RTO (Recovery Time Objective)
JBOD
NAS
SAS cable (48 Gb/s)
Versioning backup
Snapshot Replica
Restore Data

## Slide 24
©2018著作權為威聯通科技股份有限公司所有。威聯通科技並保留所有權利。威聯通科技股份有限公司所使用或註冊之商標或標章。檔案中所提及之產品及公司名稱可能為其他公司所有之商標 。
Copyright© 2019 QNAP Systems, Inc. All rights reserved. QNAP® and other names of QNAP Products are proprietary marks or registered trademarks of QNAP Systems, Inc. Other products and company names mentioned herein are trademarks of their respective holders.​​​​
Best Expansion Solution with QNAP JBOD