## Slide 3: Let PC & NAS perform better and excel on reliability.
Overview on QDA product series
Use Windows utility QNAP External RAID Manager to check the RAID and disk status
Add dual disk drives to a NAS drive slot

## Slide 4: QDA series

## Slide 5: PC with a single drive only
Out of storage
space
Running slow

## Slide 6: Drive has failed and had no data backup?
SSD/HDD
failed

## Slide 7: 3.5”SATA to dual 2.5” SATA adapter
2 x 2.5” SATA 6Gb/s
Jmicron JMS562
SATA port multiplier
(RAID 0/1, JBOD, individual)
3.5” SATA 6Gb/s
138.2mm
101.6 mm
25.9mm
SATA 6Gb/s
SATA 6Gb/s
SATA 6Gb/s
JMS562
Supporting
7mm & 9.5mm
2.5” HDD/SSD
Supporting
7mm & 9.5mm 2.5”HDD/SSD
Disk mode switch
QDA-A2AR

## Slide 8: 2.5” SATA to dual M.2 SATA adapter
2 x M.2 2280 SATA 6Gb/s
SATA 6Gb/s
100.5mm
69.9mm
Jmicron JMS562
SATA port multiplier
(RAID 0/1, JBOD, individual)
9.5mm
JMS562
SATA 6Gb/s
SATA 6Gb/s
SATA 6Gb/s
M.2 2280 SATA 6Gb/s SSD
M.2 2280 SATA 6Gb/s SSD
SSD 2
SSD 1
SSD 2
SSD 1
Disk mode switch
QDA-A2MAR

## Slide 9: Hardware RAID controller, reducing host CPU resources
Individual
(Port multiplier)
JBOD
RAID 0
RAID 1
(Default)
Any number of drives. Each drive capacity separated​*.
2 drives​ with combined capacity but no ​fault tolerance​.
2 drives with combined capacity, best performance but no fault tolerance​.
2 drives​ but losing 1-drive capacity ​for redundancy​.
* Make sure your system supports port-multiplier in order to detect both drives in the Individual mode.
QDA-A2AR/A2MAR

## Slide 10: QDA hardware RAID disk mode switch
QDA-A2AR
QDA-A2MAR
Creating or deleting RAID is only supported by the hardware-based disk mode switch.
Disk mode switch tool included.

## Slide 11: QDA-A2AR 2.5” SATA HDD/SSD installation
Use Phillips #2 screw driver

## Slide 12: QDA-A2MAR M.2 SATA SSD installation
Use
Phillips #1
screw driver
Use supplied thermal pads

## Slide 13: Switch the disk mode on a PC
1
Switch to Individual mode first (Port Multiplier mode)
Connect QDA to the SATA data and power ports
After 10 seconds, remove the QDA
Switch to another disk mode
Connect QDA to the SATA data and power ports
2
3
4
5

## Slide 14: Switch the disk mode on a NAS

## Slide 15: Standard 3.5” and 2.5“ sizes for the best compatibility
QDA-A2AR/A2MAR
Compatible with 3.5” & 2.5” USB enclosure
Compatible with 3.5” & 2.5” drive space in a computer
Compatible with QNAP NAS drive trays

## Slide 16: U.2 NVMe Adapters
QDA-UMP: U.2 to M.2 NVMe
QDA-U2MP: U.2 to 2 x M.2 NVMe

## Slide 17: U.2 NVMe SSDs are fast and cool, why are they not popular yet?
U.2 was named SSF-8639, and supports up to 32Gbps (PCIe NVMe Gen3 x4) speed
U.2 SSDs come in 2.5” drive form factor, thus better heat dissipation compared to M.2 SSDs
Fewer brands
U.2 SSDs cost more than M.2 SSDs
Source: 2019/03/21 Amazon.com

## Slide 18: U.2 NVMe to M.2 NVMe adapter
M.2 2280
PCIe NVMe
Gen3 x4
U.2 PCIe NVMe
Gen3 x4
100.4mm
69.85mm
15mm
U.2 PCIe NVMe
Gen3 x4
M.2 2280
PCIe NVMe
QDA-UMP
Notes: Linux utility for QDA

## Slide 19: U.2 NVMe to dual M.2 PCIe NVMe adapter
2 x M.2 2280 PCIe
NVMe Gen3 x4
Asmedia 2812
Gen3 PCIe switch
100.4mm
15mm
U.2 PCIe NVMe Gen3 x4
69.85mm
M.2 2280
PCIe NVMe Gen3 x4
M.2 2280
PCIe NVMe Gen3 x4
U.2 PCIe NVMe
Gen3 x4
ASMedia
2812
SSD 2
SSD 1
SSD 2
SSD 1
QDA-U2MP

## Slide 20: Let hosts with U.2 interface use affordable and high capacity M.2 SSD
PowerEdge R6415 server
Up to 10 x 2.5”U.2 NVMe SSDs
Source: 2019/3/21
https://www.dell.com/en-us/work/shop/povw/poweredge-r6415
Amazon.com
Asus ROG RAMPAGE VI EXTREME OMEGA
Up to 1 x 2.5”U.2 NVMe SSD

## Slide 21: Free up NAS PCIe slots and add M.2 NVMe SSDs
4 x 2.5”U.2 NVMe Gen3 x4 SSD slots
  - Use QDA-UMP or QDA-U2MP to add up to 8 x M.2 2280 NVMe SSDs
16 x 2.5” SATA 6Gb/s SSD slots
8 x 3.5”/2.5” SATA 6Gb/s HDD slots
QNAP TS-2888X

## Slide 22: High quality metal construction for better heat dissipation
QDA-A2MAR
The included M.2 SSD thermal pads and aluminum-alloy metal frame provides excellent heat induction and keeps the SSDs cooler.
QDA-A2AR
SGCC bottom frame
Aluminum-alloy top frame
Aluminum-alloy bottom frame
SGCC
(Steel Galvanized ColdRolled Coil)
QDA-UMP & QDA-U2MP
M.2 SSD thermal pads included

## Slide 23: Using QDA on PC / Servers

## Slide 24: Low cost and easy to use! Rapidly enhance performance or data protection
Easily configure RAID 0 to get faster transferring speed, or create RAID 1 to enhance data protection.
Using on PC/Servers: Enjoy higher performance or data protection
2TB
2TB
4TB
QDA-A2AR/A2MAR
RAID 0 Performance
2TB
2TB
2TB
RAID 1 Protection

## Slide 25
Use QNAP External RAID Manager
to check QDA series information
Install QNAP External RAID Manager, you can:
    Check QDA series device, RAID, disk information and status
    Update firmware
  Supported platforms and OS version
Windows: Windows 7 (or later), Windows Server 2012 R2 (or later)
* Creating or Deleting RAID by software is not supported, it is only supported by the hardware-based disk mode switch.
Please consult your system provider and Install the latest driver for your SATA controller
  Support QDA-A2AR/A2MAR, but can not mix TR and QDA series devices together. Including:
    Install QDA-A2AR in TR series devices
    Install QDA-A2MAR in QDA-A2AR

## Slide 26: Monitor Disk Health
The disk color on the device shows disk's status. Click on any of them to check the disk information
Show all disks in "Disk Information". Click status to get the details of disk's S.M.A.R.T information.
Check information
Quick overview

## Slide 27: Individual Mode
Use the dip switch on QDA-A2AR/A2MAR to set it on Individual Mode. The utility will show two independent disks, after formatting the disk, you can start to use it.
Note: Check whether your PC supports SATA Port Multiplier when you switch to Individual Mode. If so, system can detect both drives in Windows Disk Management.

## Slide 28: Format the external RAID group in advance to be able to use it.
After setting the RAID type through Hardware dip switch, QNAP External RAID Manager will guide users to operating system interface for formatting.
Direct to Windows Disk Management
for formatting

## Slide 29: Instant notification when external RAID is abnormal
When the RAID is degraded or has failed, users will be notified by the UI as well as desktop notification

## Slide 30: External RAID protection mechanism with system event logs
Same as the NAS, when RAID is degraded, change a new disk to start rebuilding and rebuild progress is shown
Logs are independent from operating system, quickly know and export events

## Slide 31: Firmware Information and Updates
Can check the current and latest firmware version in Firmware Information page
When there is a new version, pop-up desktop notification will inform users

## Slide 32: Use affordable and high-capacity M.2 NVMe SSD in U.2 NVMe host computers
Samsung 960 Pro M.2 NVMe SSD on QDA-UMP can still maintain high performance
QDA-UMP/U2MP

## Slide 33: Use SSD vendor tool to know NVMe SSD status
Download Samsung Magician from https://www.samsung.com/semiconductor/minisite/ssd/download/tools/
QDA-UMP/U2MP

## Slide 34: Use 3rd party tool to monitor NVMe SSD status
CrystalDiskInfo
https://crystalmark.info/en/software/crystaldiskinfo/
O.S.：Windows 10/8.x/7/Vista/XP (32 & 64 bit)
QDA-UMP/U2MP

## Slide 35: PC usage & performance demo

## Slide 36: QDA On QNAP NAS

## Slide 37: The QDA can also be used on the NAS
The QDA can also be utilized on all QNAP NASs.
Same as TR series device, QDA series stand up with its combabilities with the NAS to support disk monitoring for data protection.
Functions: - QTS Disk monitoring - External RAID monitoring
- Disk S.M.A.R.T.
- Customized temperature alert - Notification Center

## Slide 38: How does QDA combine hardware & software RAID
The QDA-A device have hardware RAID 0/1 for the 2.5 or M.2 disk inserted.
The hardware RAID will be recognized as a single virtual disk on the QNAP NAS to create storage space independently or combine with other disks.
QDA-A2MAR
RAID 0
QDA-A2MAR
RAID 0
2.5 Inch SSD
Software RAID 5
Virtual Disk
Virtual Disk
*QDA-A does not support use management interface to control RAID. The QDA-A device cannot be set as Individual at the NAS.

## Slide 39: Use multiple QDA devices for storage expansion
All the QDA Devices, with SSD, support both SSD Cache and Qtier.
For General Server and QNAP NAS, multiple QDA Devices can be used to create larger storage space with limited slots.
VS
2*256 GB RAID 1
= 256 GB Cache
2*256 GB RAID 0*2
= 2*512G RAID 1
= 512 GB Cache
Scenario
Note: TR-002/004 do not support QDA-A2AR & QDA-A2MAR; QDA-A2AR does not support QDA-A2MAR.

## Slide 40: Manage the QDA devices in the NAS
Change multiple QDA-A device with Hardware RAID 0 and use software RAID to gain the maximum device potential on the NAS.
To change the QDA-A Device RAID type, use the dip switch on the device.
It is possible to upgrade multiple QDA device firmware's at once.
QDA-A2AR
QDA-A2MAR

## Slide 41: NAS Demo

## Slide 42: QDA series adapters In & out for quick setup and conversion
Copyright © 2019 QNAP Systems, Inc. All rights reserved. QNAP® and other names of QNAP Productsareproprietary marks or registered trademarks of QNAP Systems, Inc. Other products and company names mentioned herein are trademarks of their respective holders.