## Slide 2
Easy to build a network for your device
QWA-AC2600
Introduction
Wireless network card advantages
Wireless base station setup
Application introduction
Notes: 4章節
1.使用 2. 3.QNAP NAS and Uabuntu PC 4.一些

## Slide 3: Wireless Network Card Advantages

## Slide 4
Direct access to wireless terminal data, effectively reducing the physical wireless routers loading.
QWA-AC2600 provides 5Ghz and 2.4Ghz dual-band, allows working together at some time.
Flexible configuration and expansion, one single PC/NAS can be configured with 2 or more NICs for expansion.
Create private network applications.
What are the advantages of
wireless network card?
Notes: 在QNAP NAS 或 Ubuntu PC上
1.分流NAS/PC 資料 2.雙IC 3.實體網卡擴充 4.建立安全私有網路

## Slide 5
Wireless edge computing
Data collection
Show results
Notes: 網路繁忙時 先將運算資料存放於PC/NAS 等到網路正常時再進行傳輸 以分擔雲端運算工作量 增進效能

## Slide 6: Enjoy network optimization with traffic shunting
Router over loading
Separate NAS traffic to avoid busy routers slowing down the network
Notes: 在傳統應用上 AP Router 連接所有網路設備 大量傳輸造成 Router 處理負載過高 影響網路速度
透過QWA-AC2600 與 PC/NAS 進行直接資料傳輸 可減緩Router的負載 達到最佳化的網路環境

## Slide 7
Set up a flexible wireless environment
2.4 G as AP
2.4 G as Client
5 G as AP
Through QWA-AC2600 dual IC design, It allows dual-band working at some time, 1 band as a client and 1 band as an AP.
Notes: 即可更彈性的架設網路環境

## Slide 8
Expand more physical bandwidth for more users
PC / NAS PCIe slot
Add multiple expansion wireless
NICs IN A PC/NAS
Notes: 使用虛擬存取點分享實體網卡，連線品質仍然受到單一網卡頻寬限制，
現在我們可以在Ubuntu PC 或 QNAP NAS上透過擴充實體網卡增加獨立且不會互相干擾實體頻寬

## Slide 9: Turn QNAP NAS into wireless AP
WirelessAP Station
QWA-AC2600
TS-251B

## Slide 10
ARM-based processor
x86-based processor
TS-x53B/x53Be, TS-x53BU
TVS-x63, TS-x63U
TVS-x73/x73e, TS-x73U
TS-x77
TVS-x82/x82T, TVS-1582TU
*QTS 4.3.5 or newer required
TS-x31XU
TS-832X
TS-1635, TS-1635AX
*TS-531P, TS-531X, TS-831X
Supports NAS models with PCIe slot(s)
Notes: 可以支援所有PCIe 插槽NAS機種 1.搭配 QTS 4.3.5 或更新版的ARM 架構處理器機種 2. x86架構處理器機種
如 TS-531X ,TS-832,TS-253Be? 非常合適 bundle 這個產品

## Slide 11
You can also assign individual NICs to the Container or use different QNAP services as required through integration with QNAP Network & Virtual Switch, and enjoy a separate wireless connection interface.
For example: If you need to set up a private IOT environment, you can set it up to not pass through any other devices, so that your IoT network becomes a highly secure and reliable independent network.
Freely set up an independent and secure wireless connection interface
Notes: 當我們需要使用 較高安全性的環境時 例如IOT設備或者監控設備 可以透過虛擬交換器的設定
建置私密的網路環境 提高網路安全性

## Slide 12
Introduction

## Slide 13: QWA-AC2600 PCIe wireless NIC
For extending to Quad-antenna magnetic base
3 size bracket for all QNAP NAS (include X70 model)
Low profile PCIe
Up to 500 MB/s PCIe bandwidth
With a PCIe 2.0 x1 interface
Adjust the 3-level fan speed by real time chip temperature
Active cooling module to ensure the transmission quality
4 X Detachable RP-SMA connectors
Notes: 1.QWA-AC2600 搭配了四支(可拆式 RP-SMA接口)天線，可以選擇自備的擴充天線，或是使用包裝內附的四支天線
2.PCIe 擴充卡採半高式設計，支援多數QNAP NAS 機種，並貼心附有三種檔板 1.半高式(預設) 2.全高式(機架) 3.特製半高式檔板(部分QNAP)
3.採用高規格散熱風扇，能自主偵測即時監控 IC溫度以調整風扇高中低轉速確保良好傳輸品質
4.採用PCIe Gen 2 x 1 接口 支援高達 500 MB/s 頻寬

## Slide 14: 5 GHz and 2.4 GHz dual band
Up to 2600 Mbps total bandwidth
802.11ac (5GHz): up to 1733 Mbps
802.11n (2.4GHz): up to 800 Mbps
Dual Qualcomm QCA9984 support Dual Band Dual Concurrent
Notes: 搭配高通雙晶片提供同步雙頻無線功能 同時使用 5G 2G
QWA-AC2600 = 5G 1733 + 2.4G 600
5G: 1733 Mbps (4*433Mbps)
2.4G: 600 Mbps (4*150Mbps)

## Slide 15: High mobility Quad-antenna base
Upgrade or replace the antenna by demand
For optimized antenna placement
0.8 m RF high frequency coaxial cable
4 detachable omni-directional high gain antennas
Notes: 80公分高擴展性延伸式底座 +4支雙頻全向式的天線 可針對傳輸環境靈活調整天線訊號

## Slide 16: Flexible deployments with the antenna base
Attached on the wall or ceiling
Wall-mount
Attached to metal surfaces
Magnetic
Notes: 1.天線採底座採方框設計並於底部設有壁掛孔 可靈活掛於壁掛上
2.底部彩磁吸式設計 可固定於金屬表面
3.底部附有止滑墊設計 可有效止滑並防止刮傷接觸材質

## Slide 17: 2 Qualcomm QCA9984 wireless NIC
Simultaneously communicate with multiple devices
Compliant with IEEE 802.11ac wave 2
Compatible with IEEE 802.11ac, IEEE 802.11n and IEEE 802.11a/b/g
4 x 4 MU-MIMO
Notes: 採QUALCOMM 高通 QCA9984 高規格晶片 支援 4 x 4 MU-MIMO
可讓 多用戶同時進行資料傳輸並讓無線傳輸速度不打折
支援到IEEE 802.11 ac wave 2 以及 IEEE 802.11ac IEEE 802.11n IEEE 802.11a/b/g

## Slide 18: All QNAP NAS PCIe card bracket
Low profile PCIe expansion card design
Low profile bracket
Special half height bracket
(For some QNAP NAS)
Standard full height bracket

## Slide 19: Wireless Base Station Setup
■ Build NAS WirelessAP - AP mode
■ Private network environment -
Router mode

## Slide 20: Setting of QWA-AC2600
Advanced applications on
a private network
environment (Router)
General application
QNAP NAS wireless AP
Notes: 基本應用
設定NAS無線網路
進階應用
建置安全監控環境

## Slide 21
General Application

## Slide 22: Installation of QWA-AC2600
NOTE 1：Some models may require its speaker to be temporary removed to install QWA-AC2600
Remove the cover of TS-253Be
Remove the PCIe cover
Install QWA-AC2600
NOTE 2：Bracket exchange of QWA-AC2600 is required to be installed on some models
STEP 1
STEP 2
STEP 3
Notes: 首先移除外殼螺絲 => 移除外殼 => 移除 PCIe 插槽檔板 => 安裝 QWA-AC2600 => 裝回外殼

## Slide 23: 3 Steps to convert a QNAP NAS into an AP
Download and install WirelessAP Station form QTS App Center
Click “Add Access Point”
Select QWA-AC2600
Configure the Access Point
QWA-AC2600
STEP 1
STEP 2
STEP 3
Notes: 接下來我們透過簡單的三個步驟 1.點 「新增存取點」2.選擇 QWA-AC2600 網卡 3輸入 AP 存取點的設定

## Slide 24: Turn The NAS into a Wireless AP Station
  Now you can freely set up independent and secure wireless connection interface
Notes: 建立 NAS 與裝置間的無線專屬網路，形成小型的私人網路，當我們需要建制隱密性較高的私人物聯網環境時，就可以不用透過其他分享器，直接完成NAS與物連網裝置直接溝通的私有網路。

## Slide 25
Advanced Applications

## Slide 26: Use QWA-AC2600 to share VPN wirelessly
2.4G
5G

## Slide 27: 6 steps to set up wireless connection interface
STEP 1
STEP 2
STEP 3
STEP 4
STEP 5
STEP 6
Click「Add」
Select Advanced Mode
Select the devices for the Virtual Switch
Set up the Virtual Switch IP address
Set up the Virtual Switch service
Confirm Virtual Switch settings
Open Network & Virtual Switch form QTS
Notes: 這邊使用網路與虛擬交換器這個選項 設定六個步驟 即可完成安全監控環境的設定

## Slide 28: Advanced Applications on Private Surveillance
Connect wireless cameras to the network provided by WirelessAP Station and build a secure and professional surveillance system with QVR Pro
Notes: 當我們在使用監控設備或是較具隱私的IOT設備時 我們必須建置較安全的私有無線網路

## Slide 29: Enable DHCP & NAT services to a secure surveillance environment
Adapter 1
WirelessAP 1
Set SSID as QVR Pro
Wireless encryption as WPA2
Virtual Switch 1
10.0.0.1
QVR Pro Client
10.0.0.2
10.0.0.3
Wireless camera
1 Gbe
Create a Virtual Switch to a private network by QTS "Network and Virtual Switch" function
Notes: 使用QTS 網路與虛擬交換器 透過 DHCP 以及 NAT 功能 建置安全監控及IOT環境

## Slide 30: IPC/PC Setting Demo

## Slide 31: Turn PC or IPC into wireless AP
Build PC or IPC as a wireless access point with QWA-AC2600
Install Ubuntu 17.10
Install QWA-AC2600
Install and setup
AP suite：Hostapd
Client: wpa_supplicant

## Slide 32
TANK-870 without AC2600
somewhere

## Slide 33
TANK-870 with AC2600
here

## Slide 34: Install AP Suite
●AP Suite：Hostapd
○Command: sudo apt-get install hostapd
●Ubuntu default setting will lock the network management function, need to unlock by instruction
○sudo nmcli radio wifi off
○sudo rfkill unblock all
●If require changing the network interface card name (or using default name) sudo ip link set wlp4s0 name wifiap0 sudo ip link set wlp5s0 name wifiap1
Notes: 這邊使用網路與虛擬交換器這個選項 設定六個步驟 即可完成安全監控環境的設定

## Slide 35: Set up Hostapd #1
1.Create /etc/hostapd/hostapd_5G.conf profile
2.Set up Interface
# AP netdevice name (without 'ap' postfix, i.e., wlan0 uses wlan0ap for # management frames); ath0 for madwifi interface=wifiap0
Notes: 這邊使用網路與虛擬交換器這個選項 設定六個步驟 即可完成安全監控環境的設定

## Slide 36: Set up Hostapd #2
3.Set up Driver
# Driver interface type (hostap/wired/madwifi/test/none/nl80211/bsd); # default: hostap). nl80211 is used with all Linux mac80211 drivers. # Use driver=none if building hostapd as a standalone RADIUS server that does # not control any wireless/wired driver. driver=nl80211
Notes: 這邊使用網路與虛擬交換器這個選項 設定六個步驟 即可完成安全監控環境的設定

## Slide 37: Set up Hostapd #3
4. Set up SSID for Wireless network：
# SSID to be used in IEEE 802.11 management frames ssid=QNAP-AP
5. Set up Wirelss network operation mode
# Operation mode (a = IEEE 802.11a (5G), b = IEEE 802.11b, g = IEEE 802.11g(2.4G), # Default: IEEE 802.11b hw_mode=a
Notes: 這邊使用網路與虛擬交換器這個選項 設定六個步驟 即可完成安全監控環境的設定

## Slide 38: Set up Hostapd #4
6. WPA setting：
# Enable WPA. Setting this variable configures the AP to require WPA # bit0 = WPA # bit1 = IEEE 802.11i/RSN (WPA2) (dot11RSNAEnabled) wpa=2
Notes: 這邊使用網路與虛擬交換器這個選項 設定六個步驟 即可完成安全監控環境的設定

## Slide 39: Set upHostapd #5
7. Input Password for Wireless network：
# WPA pre-shared keys for WPA-PSK.
wpa_passphrase=QNAP12345
8. #Start up hostapd sudo /usr/sbin/hostapd -B /etc/hostapd/hostapd_5G.conf sudo /usr/sbin/hostapd -B /etc/hostapd/hostapd_2.4G.conf
Notes: 這邊使用網路與虛擬交換器這個選項 設定六個步驟 即可完成安全監控環境的設定

## Slide 40: Hostapd detail setting information
interface=wifiap0 driver=nl80211 ssid=QNAP-AP-5G hw_mode=a channel=0 preamble=1 auth_algs=3 wpa=2 wpa_key_mgmt=WPA-PSK rsn_pairwise=CCMP wpa_passphrase=QNAP12345 wmm_enabled=1 uapsd_advertisement_enabled=1 disassoc_low_ack=1 country_code=TW
ieee80211d=1 ieee80211n=1 ht_capab=[HT40+][SHORT-GI-20][SHORT-GI-40][LDPC][TX-STBC][RX-STBC1][DSSS_CCK-40][MAX-AMSDU-7935] ieee80211ac=1 vht_capab=[MAX-MPDU-11454][RXLDPC][VHT160-80PLUS80][SHORT-GI-80][SHORT-GI-160][TX-STBC-2BY1][RX-STBC-1][SU-BEAMFORMER ][SU-BEAMFORMEE][MU-BEAMFORMER][BF-ANTENNA-2][BF-ANTENNA-3][SOUNDING-DIMENSION-2][SOUNDING-DIMENSION-3][MAX-A-MPDU-LE N-EXP7][RX-ANTENNA-PATTERN][TX-ANTENNA-PATTERN] vht_oper_chwidth=1 vht_oper_centr_freq_seg0_idx=0 vht_oper_centr_freq_seg1_idx=0
Notes: 這邊使用網路與虛擬交換器這個選項 設定六個步驟 即可完成安全監控環境的設定

## Slide 41: Made for IPC and QNAP NAS
DBDC PCIe Wireless Adapter
Copyright © 2019 QNAP Systems, Inc. All rights reserved. QNAP® and other names of QNAP Products are proprietary marks or registered trademarks of QNAP Systems, Inc. Other products and company names mentioned herein are trademarks of their respective holder
Notes: 以上是我們本次的介紹 謝謝各位的觀看