## Slide 2
M.2 SSD＋10GbE revealed
NAS/PC supported, experience super speed NVMe SSD
QTS 4.4.1 fully utilize SSD’s performance

## Slide 3: M.2 SSD＋10GbE cache card Revealed

## Slide 4: Select the QM2 card you need
QM2-2S-220A
QM2-4S-240
QM2-2P-344
QM2-2P-384
QM2-2P-244A
QM2-4P-284
QM2-4P-342
QM2-4P-384
Support 10GBASE-T port
Expand four M.2 ports
QM2-2S10G1TA
QM2-2P10G1TA
M.2 SATA
M.2 PCIe Gen 2
M.2 PCIe Gen 3
Notes: 3/21, QM2卡直播 P.23

## Slide 5: Clear naming rule – featured 10GbE
QNAP M.2 PCIe cache/10GbE card
Number of supported M.2 SSD
M.2 SSD + 10GbE
Supported M.2 SSD connector type
P: PCIe NVMe SSD
S: SATA SSD
10GbE port
Single port BASE-T RJ45 throughput
revision

## Slide 6: Clear naming rule - M.2 cache only
QNAP M.2 PCIe cache card
Number of supported M.2 SSD
2: 2 x SSD
4: 4 x SSD
Supported M.2 SSD connector type
P: PCIe NVMe SSD
S: SATA SSD
PCIe interface
34= Gen3 x4
28= Gen2 x8
NVMe SSD slot bandwidth
4= Gen3 x4
2= Gen3 x2

## Slide 7: SSD cache and 10GbE in one card
QM2-2P10G1TA
Supports maximum 2 x PCIe NVMe SSD (M-key), provides Gen2 x2 on each slot
QM2-2S10G1TA
Supports maximum 2 x SATA M.2 SSD, provides 6Gb/s on each slot
Notes: QNA 直播 P.8

## Slide 8: Expand cache capacity or 10GbE redundant
TS-1283XU
TVS-672XT
Expand cache capacity by installing QM2 in idle PCIe slots
Provide redundant 10GbE for fail-over
Built-in 10GbE

## Slide 9: 3rd party operating system support
QNAP NAS don’t need to install Driver, Windows/Linux platforms please visit QNAP website to download the driver
Note: M.2 SSD compatibility and function supported depends on the hardware design and platform. Please check with your motherboard manufacturer for details.
Low-profile PCIe add-on cards, bundled with full-height bracket.
Self-monitored with thermal sensors to control the speed of smart fan modules.
Active cooling module
Compliant with PCIe standards
AQC-107S
Linux & Windows
Dual platform supported
Notes: QM2 直播P.22

## Slide 10: Multi-Gigabit supported
Support Multi-Gigabit NBASE-T standard.
QSW-804-4C
QSW-1208-8C
Provides 12 ports of 10Gbps transfer
Provides 8 ports of 10Gbps transfer
 | CAT 5e | CAT 6 | CAT 6A & CAT 7
100 M | ✓ | ✓ | ✓
1G | ✓ | ✓ | ✓
2.5G | ✓ | ✓ | ✓
5G | ✓ | ✓ | ✓
10G | ✘ | ✓(55M) | ✓
Notes: QNA 直播 P.9
QM2卡要在NAS裡

## Slide 11: Efficient cooling dissipation
10GbE 10GBASE-T port
M.2 slots
M.2 thermal pad is bundled, provides more efficient heat transfer
Active cooling fan
Fin array heatsink

## Slide 12: QM2-2P10G1TA performance up
QM2-2P10G1TA
QM2-2P10G1T
Random read enhanced nearly 25%
Iometer on PC, tested in QNAP Lab,
PC Environment 1. CPU: Intel (R) Core(TM) i7-6700 CPU@ 3.40GHz. 2. OS: Windows 10. 3. Memory: 64 GB. 4. SSD: Samsung SSD 860 EVO 1TB M.2 SATA *2, Software-RAID 1.
(IOPS)
RR-4K
RW-4K
272808
205057
200760
203626
QM2-2P10G1TA
QM2-2P10G1T

## Slide 13: NAS/PC supported, experience super speed NVMe SSD

## Slide 14: Ideal choice to boost performance: M.2 PCIe NVMe SSDs
You don’t need to change motherboards or HW configurations, just simply install the QM2-2P10G1TA on your PC’s Gen2 x4 slot then you can enjoy the high speed of NVMe SSD
20Gb/s
32Gb/s
M.2 PCIe Gen 2 x4
M.2 PCIe Gen 3 x4
16G/s
M.2 PCIe Gen 3 x2
Interfaces
Theoretical Speed
★ Mainstream
M.2 SATA III
6Gb/s
M.2 PCIe NVMe SSDs have more than 2Xa performance enhancement
Notes: https://www.carmagazine.co.uk/features/car-culture/how-we-ended-up-racing-an-old-sports-car-at-le-mans/

## Slide 15: Leave the 3.5” slots for huge capacity HDDs
Huge capacity storage
Install NVMe for cache
Freely upgrade a normal pool to a Qtier pool
without starting over
QM2 SSD RAID
Without changing existing configurations
PC
NAS

## Slide 16: High performance NVMe in PC
Upgrade your PC to NVMe!
PC Environment 1. CPU: Intel (R) Core(TM) i7-6700 CPU@ 3.40GHz. 2. OS: Windows 10. 3. Memory: 64 GB.
4. PC SSD: ADATA Prod_SP550 120GB 5. QM2 SSD: Samsung SSD 970 EVO 256GB M.2 NVMe *2, RAID1;
Samsung SSD 860 EVO 1TB M.2 SATA *2, Software-RAID 1.
(IOPS)
RR-4K
RW-4K
272808
55972
200760
13893
QM2-2P10G1TA
SSD
(IOPS)
RR-4K
RW-4K
156973
55972
70823
13893
QM2-2S10G1TA
SSD
QM2-2P10G1TA
QM2-2S10G1TA

## Slide 17: QM2 series on Windows PC
Catch the NVMe SSD information from device manager
Disk partition
Set RAID1 protection

## Slide 18: QTS Supports M.2 SSD Cache Acceleration
Accelerates IOPS performance
Applies SSD cache to all volumes and LUNs with a single setup process, or specified volumes only
Reduce I/O latency
Global read-write cache
Read
Write
HDD storage
SSD storage
Application layer
Read caching
Read/Write caching
Notes: QM2 直播 P.4

## Slide 19: Expand high-speed M.2 SSD tier with Qtier
HDD storage
SSD storage
Application layer
Qtier 2.0
Total capacity = hard drives + SSD
Total capacity = hard drives
Read/Write caching
Sequential
Random
Hot data & reserved block
Cold and archived data
Keep flexibility to accelerate performance of key data and increase cost/performance ratio
Storage space and SSD caching
I/O aware
Tiering on Demand
Notes: QM2 直播 P.5

## Slide 20: Live Demo Install QM2 on PC to enhance performance

## Slide 21: QTS 4.4.1 Fully utilize SSD’s performance

## Slide 22: SSD Evolution Trend
QNAP QM2 in QNAP NAS is ideal on sharing data, applications and virtualized server applications for multi users. Install the QM2 on the NAS which has no other HDD slots available then combine with the 10GbE port and QTS 4.4.1’s remove and re-create Qtier solution, keep improving the random access speed (IOPS) to experience dramatic performance improvements.
Disk Type | SW (MB/s) | RW (IOPS)
HDD | 100 | 350
SSD | 300 | 60000

## Slide 23: One Global Cache with Three Modes
QNAP SSD Cache can be applied to all volumes and LUNs once set with 3 modes:
Read-Only  Copy frequently used data to SSD
Read-Write  Not only copy data, new data can also be temporarily stored in SSD
Write-Only  Only new data will be written into the cache
Data from clients and storage will be cached at the block-level in real time
How Read-write Cache work:
HDD
IO Intensive
Application
When SSD Space not enough
SSD
Write
Write
Read
Read

## Slide 24: The Write-only Cache Increase ROI of SSD Cache with high Writing Demand
Reference: https://docs.microsoft.com/en-us/windows-server/storage/storage-spaces/understand-the-cache
SSD
SSD
NVMe
SSD
SSD
NVMe
Writes are cached
Reads are NOT
Write-only cache is promoted by Microsoft for endurance control.
QNAP believes that Write-only Cache can increase the ROI of SSD in below scenario:
1. File Server focusing on write operations
2. Database with more write operation (Such as IoT monitoring server) 3. Use high endurance SSD (Intel Optane™)
Notes: 24

## Slide 25: The Advantage of Software-defined Over-provisioning
SSD vendor will reserve 7% or more SSD space for internal operation usage.
QNAP allow user to test and increase the over-provisioning ratio from the software to increase that consist performance and endurance of SSD.
Reference: http://www.atpinc.com/technology/ssd-over-provisioning-benefits-configure
FIO used with parameters: --direct=0 --bs= 4k(random)1M(sequential), --io depth=1(random) 32(sequential), --file size= 90G
Notes: 25

## Slide 26: Alternative for Cache: Qtier Tiering Storage
On QTS, PCIe NVMe SSD can only work as SSD Cache currently.
Hot Data
Warm Data
Cold Data
QNAP allows the combination of SSD and HDD RAID into the same pool and migrate data automatically based on accessing pattern.
Before Tiering
1
4
2
Data Access Pattern Changed
3
After Tiering
Start Tiering
Qtier
Engine
Support SATA, SAS, M.2, QM2 and U.2 SSD with QNAP Over-provisioning.
Provide higher capacity as SSD can be used to store data

## Slide 27: Challenge: Changing SSD Tier Interface
SSD RAID
SSD RAID 5
HDD RAID 6
HDD RAID 6
While SSD Tier is already created with SATA Disk, how can I replace it with QM2 to expand the NAS while improving the SSD Tier performance?
Challenge
SSD RAID
Notes: 32258279

## Slide 28: QTS 4.4.1 Support Remove Qtier SSD Tier
SSD RAID Usage
SAS HDD RAID Usage
SSD RAID Usage
Pool Metadata
SATA HDD RAID Usage
SSD RAID Usage
Pool Metadata
QNAP QTS 4.4.1 supports remove Qtier SSD Tier, the users can remove then re-create SSD tier as required.
When removing the SSD tier, all the storage pool data will be retained as data on SSD only to be moved to HDD.
Storage pool

## Slide 29: Test of recreating Qtier SSD Tier
In QNAP Lab, 4 250 GB SSD need to be replaced with 500 GB SSD. The operation is conducted with both Replacing Disk & Remove SSD Tier.
The time for removing and re-creating the SSD tier is almost 2 times faster than replacing disk. The replacing disk method also does not support changing SSD on different interface.
* Using TVS-1282T with 4 enterprise HDD for testing.
Remove and Upgrade SSD Tier
Replacing Disk
0
(Mins)
Consumed Time (Mins)
10
15
20
25
30
35
40
45
50
5
23
44
Notes: 35157436

## Slide 30: Choose Between SSD Cache & Qtier
The best SSD configuration may only be measurable once it is configured. The SSD Cache and Qtier have different advantages.
Real Time Performance Boost
1. For accessing with burst IO such as file syncing and video editing.
2. Can be changed to Read or Write only with bypass block size.
SSD Cache
Qtier 2.0
Fully use SSD Capacity
1. For boosting IO with fixed pattern such as mail or database server.
2. With IO Aware Qtier can also support database operations.
SSD Cache
Qtier
0
1050
900
750
600
450
300
150
Sequential R/W (MB/s)
SSD Cache
Qtier
20000
160000
140000
120000
100000
80000
60000
40000
Random R/W (IOPS)
0
Write
Read
817
831
830
820
82823
133402
130388
88022
TVS-872XT-i5-16G with QM2-2P10G1TA and Samsung SSD 960 pro 1TB M.2 NVMe *2, RAID 1 , compare SSD cache and Qtier, running Network and SSD transfer at the same time
Notes: Qtier

## Slide 31: QM2 Highlight points with QTS
Improve random access performance when the NAS has no idle HDD slots and 10GbE ports
Improve NAS performance by using read only, read-write and write-only 3 type of caches for the whole NAS storage space via QM2
Software-defined Over-provisioning increase Performance and endurance of SSD
QTS Qtier improves both performance and capacity, in QTS 4.4.1，users can easily change the SSD to QM2 in the SSD Tier.
4.4.1 Beta will be released at End of May!
QTS 4.4.1 fully utilize SSD’s performance