## Slide 2: Explore Software Router
What is software router?
MikroTik RouterOS Intro
  License purchase and validation
NAS x RouterOS
  NAS Hardware support
  NAS Software support
  Virtual Router topology
Demo
  Basic setup
  Advanced user story

## Slide 3: What is software router？
Running software-based routers in a virtual environment or an appliance.
Forwards data between computer and network.
Software Router
Router

## Slide 4: Why You Need It
Provides full-function routing functions
Allocating computing resources on demand
Leveraging virtualization technology to build a network environment rapidly

## Slide 5: MikroTik RouterOS
Proprietary
Linux-based operating system
Installation
  ISO image – PC/ x86
  CHR (Cloud Hosted Router) – virtual machines
Licensing
  PC/ x86 – by the scalability of usage, e.g. num. of tunnels
  CHR – by the speed of data transfer

## Slide 6: Installation
ISO image for：
  RouterBOARD
  PC
  x86
CHR (Cloud Hosted Router) for ：
  Virtual Machine
  Amazon AWS marketplace

## Slide 7: Purchase / Activate License
Purchase
Register a MikroTik account
Log-in and purchase
Activate (for prepaid keys)
Log-in MikroTik
Enter Software ID

## Slide 8: NAS x RouterOS (1/2)
QWA-AC2600
40 GbE Mellanox
10 GbE Aquantia
10 GbE Intel X550
  NAS Hardware Support:
X86 NAS from SOHO to Enterprise
QWA-AC2600 WiFi expansion card
1GbE - 40GbE Network expansion cards

## Slide 9: NAS x RouterOS (2/2)
  NAS Software Support
Flexible resource allocation, e.g. CPU, memory and interfaces.
Dynamically adjust network topology via Virtual Switches
Wireless AP Station supports Wi-Fi Access Point (AP)
Provides a VM console to manage router configuration

## Slide 10: NAS Software – VM resources
2 - 40 CPU cores
512 MB - 1TB Memory
2 - 8 virtual NICs
VM
Virtualization Station
VM
VM

## Slide 11: NAS Software – Virtual Switch
Virtual Switch connects “physical” and “virtual” NICs and be used to build up a network environment.
Virtual NICs
Virtual Switch
Physical NICs
Bridged mode：connects different network segments (w/ IP assigned)
External-only mode：dedicate bandwidth to virtual switch (w/o IP assigned)
VM (LAN)
RouterOS (LAN)
RouterOS (WAN)
40 GbE Mellanox ConnectX-3
10 GbE Aquantia
10 GbE Intel X550
QWA AC-2600

## Slide 12: NAS Software – Wi-Fi AP
Composed of QNAP QWA-AC2600 and Wireless AP Station.
5G
2.4G

## Slide 13: Virtual Router Topology
vNIC 1:
WAN interface, all the traffic throughout virtual router first.
vNIC 2:
LAN interface, applying network settings of virtual router via physical NIC and QWA-AC2600.
vNIC 3:
LAN interface, applying network settings of virtual router via Virtual Switch
Internet
Physical NIC
Physical NIC
Physical Switch
PC
Sever
Virtual Switch (external-only)
Virtual Switch (Bridged)
Virtual_NIC_1 (WAN)
Virtual_NIC_3 (LAN)
Virtual_NIC_2 (LAN)
VM
VM
VM

## Slide 14: Demo – Basic configuration setup (1/3)
Download MikroTik RouterOS CHR
Import virtual appliance
Add virtual NICs for WAN/LAN
Set up a LAN interface IP address

## Slide 15: Demo – Virtual Switch Setup (2/3)
Create a Virtual Switch for WAN and setup as External-Only mode.
Create a Virtual Switch for LAN and setup as Bridged mode.
Connect vNICs of VMs and RouterOS to Virtual Switches respectively.

## Slide 16: Demo – Wi-Fi AP Setup (3/3)
Download Wireless AP Station from App Center.
Plug in
QWA-AC2600
Add access point with 5G/2.4G and configure a password.

## Slide 17: Demo Environment Topology
Internet
Physical NIC
Virtual Switch
Virtual Switch
Virtual_NIC_1 (WAN)
Virtual_NIC_2 (LAN)
VM
VM

## Slide 18: Demo

## Slide 19: Demo – Advanced User Story
Site-to-Site EoIP Tunnel with IPsec and bonding different ISPs.
Production
Backup
Router
Fiber-optic 60M
Server Farm
QNAP Router-NAS
RouterOS
Router
Backup
Core-Switch
Server Farm
QNAP Router-NAS
RouterOS
Bonding
Bonding
Site to Site VPN
EoIP Tunnel +IPsec
Fiber-optic 100M
Fiber-optic 100M
Production
Core-Switch

## Slide 20: Demo

## Slide 21
QNAP is your best choice!
QNAP NAS X MikroTik RouterOS
Copyright © 2019 QNAP Systems, Inc. All rights reserved. QNAP® and other names of QNAP Products are proprietary marks or registered trademarks of QNAP Systems, Inc. Other products and company names mentioned herein are trademarks of their respective holders.