## Slide 2: 常見的客戶需求有哪些？
有甚麼方式能讓我快速且安全地存取資料？
如何輕鬆地擴建區塊層級的網路儲存空間？
有甚麼方式可以備份 SAN 的資料，並實現複本資料管理 (CDM) 應用？

## Slide 3: QNAP NAS x ATTO 光纖通道擴充卡
QNAP NAS 高效能儲存空間
跨界支援 Fibre Channel SAN 給用戶高可靠、可擴充、且價格更實惠的 FC-SAN 儲存方案
QNAP 支援 ATTO CelerityTM FC 32Gb & 16Gb 擴充卡

## Slide 4: 企業為什麼要建置 FC-SAN
連接性佳： 在光纖通道儲存網路 (FC-SAN) 架構下，任一伺服器可與任一儲存裝置直接相連，任一儲存裝置也可彼此直接相連。
擴充性佳： 企業可以在不增加伺服器與區域網路負擔的情況下進行擴充。
資料分享能力佳： 因儲存裝置不再與特定的某一伺服器相連，所以多部伺服器可共享資源，且大量檔案傳輸時亦不影響主網路效能。

## Slide 5: iSCSI 與 FC 架構比較
SCSI Layer
Operating System/Application
光纖通道不需透過乙太網路，且在系統中的物理層比 iSCSI 較少 ，在擴建區塊層級的儲存網路時，用光纖通道可免去網路負擔。
iSCSI 需透過乙太網路 ，擴建區塊層級的儲存網路。
iSCSI
光纖通道
SCSI Layer
TCP
IP
Ethernet
FC
FCP

## Slide 6: 光纖通道可減輕 CPU 負擔
F/W: 4.4.1
CPU: Intel(R) Xeon(R) E-2124 CPU @ 3.30GHz
Tested SSD: Samsung SSD 850 PRO 512GB SATA*12, RAID 0
RAM: 8 GB (4GB x 2)
Block-based LUN; AIO enable
FC 32G: ATTO Fibre Channel Adapter
25GbE: QXG-25G2SF-CX4, MTU 9000
IOmeter Global Configuration: Maximum Disk Size: RAM*4/ Ramp Up Time: 30 seconds Seq / Run Time: 3 Minutes / 2-workers/ 64-outstanding Random / Run Time: 3 Minutes / 4-workers/ 32-outstanding
Server Environment:
CPU: Intel(R) Xeon(R) CPU E5-2630 v3 @ 2.40GHz
OS: Windows Server 2016 Database Evaluation.
Version: 10.0.14393 Build 14393
Memory: 128 GB.
FC 32G: ATTO Fibre Channel Adapter
25GbE: QXG-25G2SF-CX4, MTU 9000
Speed/CPU |  | iSCSI |  | FC | 
 |  | 25GbEx1 | CPU% | 32G | CPU%
Throughput (MB/s) | SW-1M | 2709 | 56% | 2946 | 39%
 | SR-1M | 2755 | 32% | 2770 | 30%
 | SW-512K | 2707 | 61% | 2950 | 37%
 | SR-512K | 2825 | 43% | 2870 | 35%
IOPS | RW-4K | 154793 | 81% | 155197 | 77%
 | RR-4K | 108263 | 69% | 113162 | 67%
測試環境：TS-1283XU-RP
備註：此測試環境為 RAID 0

## Slide 7: 光纖通道效能佳
IOmeter Global Configuration: Maximum Disk Size: RAM*4/ Ramp Up Time: 30 seconds Seq / Run Time: 3 Minutes / 2-workers/ 64-outstanding Random / Run Time: 3 Minutes / 4-workers/ 32-outstanding
Speed/CPU |  | FC | 
 |  | FC32Gx1(PC) | CPU%
Throughput (MB/s) | SW-1M | 3132 | 30%
 | SR-1M | 4798 | 25%
 | SW-512K | 3154 | 29%
 | SR-512K | 2772 | 28%
IOPS | RW-4K | 92632 | 40%
 | RR-4K | 195360 | 36%
備註：此測試環境為 RAID 5
F/W: 4.4.1.0955 build 20190603
CPU: Intel(R) Xeon(R) E-2136 CPU @ 3.30GHz
SSD: Samsung SSD 850 PRO 512GB SATA*24,RAID 5
RAM: 16GB, 8GB*2
Thick volume; Block-based LUN; AIO enable; MPIO
FC32G: ATTO Fibre Channel Adapter
測試環境：TS-2483XU-RP
PC Environment
CPU1: Intel(R) Xeon(R) CPU E5-2630 v3 @ 2.40GHz, 2401 Mhz, 8 Core(s), 16 Logical Processor(s)
OS: Windows Server 2016 Datacenter Evaluation Build 14393
Memory: 128 GB.
FC32G: ATTO Fibre Channel Adapter

## Slide 8: QNAP FC-SAN 解決方案
Windows / Linux / VMware 主機
HP DL360 G7 server
Windows / Linux / VMware 主機 (啟動器模式) + NAS (目標模式)：
TVS-872XU
TVS-872XU
ATTO Celerity 16Gb
Fibre Channel adapter
Other FC-SAN Storage
Fibre Channel Switch
光纖通道
儲存區域網路
(SAN)
ATTO Celerity 16Gb
Fibre Channel adapter
ATTO Celerity 16Gb
Fibre Channel adapter

## Slide 9: 企業 FC-SAN 與 QNAP NAS 達成 CDM 應用
QNAP NAS
QNAP NAS
伺服器
SAN 儲存空間
正式工作環境
備份伺服器
SAN Fabric
LUN
LUN
LUN
LUN
LUN
用於本地快照保護
(LUN 可透過 iSCSI 或 FC 存取)
Qtier
SSD 快取
用於異地備份的快照副本
伺服器可以透過iSCSI 存取資料
FC
LAN

## Slide 10: 支援市場 ATTO CelerityTM Fibre Channel 介面卡
與業界領先的 FC 介面卡供應商合作，提供最經濟的 FC-SAN 存儲解決方案。
支援 ATTO CelerityTM
32Gb & 16Gb FC 擴充卡
相容性列表: qnap.com/compatibility/

## Slide 11: 相容多款 FC 介面卡，支援 4G/8G/16G/32G
相容性列表: qnap.com/compatibility/
ATTO FC 卡 | 介面 | 支援速度 | 技術世代 | PCIe | 高度規格
CTFC-322E | 2 X 32GFC | 32G/16G/8G | Gen 6 | 3.0 x8 | Low profile
CTFC-321E | 1 X 32GFC | 32G/16G/8G | Gen 6 | 3.0 x8 | Low profile
CTFC-162P | 2 X 16GFC | 16G/8G/4G | Gen 6 | 3.0 x8 | Low profile
CTFC-161P | 1 X 16GFC | 16G/8G/4G | Gen 6 | 3.0 x8 | Low profile

## Slide 12
Notes: 封面

## Slide 13: Corporate Overview
Established in 1988 – Upstate NY Headquarters
Experienced engineering leadership
Scalable manufacturing capacity
Products – host bus adapters, NICs, storage controllers, bridging appliances and software
Interconnect expertise – Fibre Channel, SAS, Ethernet, SATA, iSCSI, Thunderbolt, NVMe
Customers – Original Equipment Manufacturers through End Users (supported with a robust channel)
Worldwide distribution
2

## Slide 14: Customers and Partnerships
6
OEM Customers
Technical Alliances
End Customers

## Slide 15: Technology Meets Products
Bridges
Thunderbolt™ Adapters
Storage Controllers
RAID Adapters
Network Interface Cards
Host Bus Adapters
SAS/SATA
Thunderbolt
Ethernet
Fibre Channel
NVMe
Latency Management
Bandwidth Optimization
Core Technology

## Slide 16: Data Intensive Environments
ATTO develops high-performance products that manage latency in the most demanding, real-time environments, resulting in accelerated application performance and enhanced transaction processing
IOPS Random Non-Sequential
Database ERP Web servers Email Servers Back-office ops
Mixed Environment Randomized Sequential
Business analytics Financial/OLTP Content distribution Asset management Cloud-based applications
MB/s Streaming Sequential/Real-Time
CAD/CAE Video post-production Broadcast video Medical imaging Seismic/oil & gas
ATTO
ATTO
Competitors
Competitors

## Slide 17: Product Line
Host Bus Adapters
  Fibre Channel
  SAS/SATA
Network Interface Cards
  10/25/40/50/100Gb Ethernet
Thunderbolt™ Adapters
  Fibre Channel
  Ethernet
  SAS/SATA
Storage Controllers
  Fibre Channel-to-SAS/SATA
  Ethernet-to-SAS/SATA
Software
  ATTO ConfigTool™
  Latency Scout™

## Slide 18: Technical Differentiators
ATTO Advanced Data Streaming (ADS™)Technology
  Provides controlled acceleration of data to ensure smooth streaming and most consistent performance
ATTO MultiPath Director™
  Enables macOS®, Windows® and Linux® workstations and servers to connect directly to enterprise-class storage with redundant controllers, providing failover and load balancing capabilities across multiple paths to the storage
ATTO DriveAssure™ Technology
  Compensates for misbehaving drives to prevent premature drive failures and slow downs to maximize system uptime and ensures 100% throughput during data rebuilds
ATTO intelligent Bridging Architecture™
  Combines powerful hardware with an efficient software data engine to deliver the flexibility of “anything-to-anything” connectivity
ATTO vConfigTool™
  A software plug-in to integrate centralized management and monitoring within a VMware vCenter® environment to accelerate adapter deployment; optimize configurations and reduce VMware host infrastructure costs
ATTO Latency Scout™
  A storage I/O diagnostic utility that boosts data center performance by identifying bottlenecks, allowing for the optimization of system performance and infrastructure uptime

## Slide 19: Fibre Channel Competitive Review
Company | Strength | Weakness | Market Perception | Competitive Strategy
ATTO | High Performance products and solutions, Support & Service | Brand awareness in IT | Performance and support leader | Niche Markets, Responsiveness, Customer Support
Marvell Cavium QLogic | Market share leader focused on driving incremental revenue from the target solutions | Limited mindshare to T2/3; so many acquisitions … are they really focused on their channel customers? |  | I/O solution provider focused on storage connectivity
Broadcom Emulex | Focus is on IT markets, Strong T1/T2 OEM relationships for both Silicon and HBA | Lacking mindshare to T3; so many acquisitions … are they really focused on their channel customers? | Strong feature set, IT market leader | IT and T1/T2 OEM focus

## Slide 20: Target Mode Support
SDK Option
Write specific code to connect to desired devices.
ATTO SCSITMD Source Code
(Linux and Windows)
Celerity Fibre Channel Target Mode Driver
SCST Option
Select the desired SCST module to connect to desired devices.
SCST Core
ATTO SCST Driver Interface
(Linux)
Celerity 32Gb/s and 16Gb/s Fibre Channel HBAs
Target Mode Support
  Design solutions from ground up for the greatest flexibility with ATTOs Software Developers Kit (SDK)
    Provides the ability to offer value added features/software
    Available for Linux, Windows and FreeBSD platforms
  Design solutions from pre-set modules for quicker time to market with ATTOs SCST
    Available for Linux platforms

## Slide 21: MultiPath Director
High-Availability Storage - Automatic path failover and failback provides uninterrupted access to storage.
Superior Performance - Load balancing increases overall system performance by using more than one Fibre Channel path to transfer data.
Improved Productivity - Workstations can share storage, enabling collaborative workflows and real-time access to content to meet project deadlines.
Flexible Connectivity - Ability to mix Windows, Linux and Mac workstations in a heterogeneous environment.
Simplified Management - ATTO Configuration Tool simplifies administration, troubleshooting and management of multiple paths to storage.
* ATTO is the ONLY Fibre Channel HBA manufacturer with its own multipathing driver – MultiPath Director.
* In addition to Server environments, ATTO’s MultiPath Director allows workstations to connect directly to Enterprise-class storage enclosures with dual controllers. (All competitors are forced to use multipathing functions available only in Server Operating Systems.)
Notes: “We already have multipathing, why to we need ATTO’s MultiPath Director?”
The ATTO FC HBA standard drivers provide standard support to operate in each operating system. It also allows the user to have multiple paths using built-in multipathing tools such as MPIO in Windows and DM-Multipath in Linux. This is often enough for server based installations (Windows Server 2008 and up and any Linux distribution that we support), but it leaves a hole in the workstation market. Workstation operating systems such as Windows 7, 8 and 10 do not include MPIO, and MacOS only supports certain vendors with their implementation of multipathing. But many professional users run on these operating systems. Additionally, they need to connect to high-end storage and they want to take full advantage of the performance features of the storage. ATTO grabbed this opportunity and we developed our own multipath driver for Windows, Linux and Mac.
ATTO Multipath Director (MPD) is based on the ALUA standard (Asymmetric Logical Unit Access).
ATTO has designed MPD to be easy to use. The ALUA standard helps make the solution almost "Plug-n-play" when configuring your SAN. Only storage configuration (LUN creation and mapping) is needed.
ATTO MPD also provides path statistics down to the LUN level that are easy to read and monitor.
For the expert user, MPD allows you to manage your paths down to the LUN level (whereas the operating system versions only allow you to manage to the target level).
ATTO MPD provides 3 load balancing policies (Round Robin, Queue depth and Pressure (default)).
ATTO MPD provides consistent performance across all 3 platforms supported (Windows, Linux and Mac).
IT managers do not have to become multipath experts. They do not need to learn DM-multipath (Linux), MPIO (Windows) and/or ALUA (MacOS) to implement a SAN in a heterogeneous environment. MPD provides a uniform application experience across all 3 platforms.
While MPD was designed for workstation operating systems, it will also work in the server environments. ATTO has found that many IT managers prefer ATTO MPD over the operating system options because ATTO MPD often performs better and it is easier to user and monitor your SAN.

## Slide 22: Where to Purchase
7
Solkenix has been ATTO’s Distributor in Taiwan since 2001
  Experts in first-line support for ATTO product & solutions. Fibre Channel, iSCSI/Ethernet, SAS, and Thunderbolt products
  https://www.solkenix.com/
Rest of the World
  https://www.atto.com/howtobuy/

## Slide 23: QNAP x ATTO Summary
7
Together QNAP and ATTO offer the highest-performing and lowest cost solutions
Take advantage of the Try-before-you-buy offer before it expires
&

## Slide 24: QTS iSCSI 與光纖通道管理員
功能特色
設定彈性
1. LUN 對應：輕鬆對應到 iSCSI
或光纖通道。
2. LUN 遮罩：設定伺服器存取
LUN。
3. 光纖通道連接埠繫結：
綁定連接埠與伺服器。
易於辨識
光纖通道的 WWPN 可以編輯別名。

## Slide 25: 設定 LUN 遮罩
LUN 遮罩：
指定哪個伺服器可以存取哪個LUN 。

## Slide 26: 設定光纖通道連接埠繫結 (Binding)
光纖通道連接埠繫結：
編輯哪個伺服器可以綁定哪個連結埠。

## Slide 27: 透過別名清單來辨識伺服器與光纖通道連接埠
編輯別名：
指定光纖通道的 WWPN 別名清單。使用者易於辨識儲存區域網路中的伺服器及光纖通道連接埠。

## Slide 28: FC-SAN 搭配快照保護及 Qtier / SSD 快取 兼顧資料安全及操作效能
iSCSI & Fibre Channel management
簡單又快速打造 FC-SAN 環境
快照功能
快照備份任務
快照保險庫
Qtier, SSD 快取
加速傳輸效能

## Slide 29: 快照與快照備份任務
QNAP NAS 內建支援快照保護，可在儲存與快照或檔案總管輕易擷取、閱覽、還原快照。
本地快照支援
建立完整磁碟區或 LUN，若欲啟用快照應以少量分配逐步擴充為原則。
快照空間管理
建立快照差異備份任務，並且透過遠端快照還原直接由網路還原回本機。
快照備份任務

## Slide 30: Qtier
熱資料
暖資料
冷資料
分層前
頻繁存取資料效能未優化
1
4
2
資料存取行為改變
3
分層後
頻繁存取資料效能已優化
開始分層
Qtier
引擎
除了全 SSD 儲存，QNAP Qtier 自動分層可將 SSD 和 HDD RAID 整合為一組儲存池，並智能判斷冷熱資料，自動在分層間移動。
一般 SATA/SAS SSD 外，也支援 M.2 與 QM2 PCIe 外接卡。
儲存不僅受惠於 SSD 的強大效能，更保有最大的儲存大容量。

## Slide 31: Live Demo

## Slide 32: Fibre Channel 支援的機架型 NAS 型號
Intel & AMD NAS 支援 32Gb/s & 16Gb/s ATTO FC 介面卡
TES-3085U (QTS), TES-1885U (QTS), TDS-16489U
TS-2483XU, TS-1683XU-RP, TS-1283XU-RP, TS-983XU-RP, TS-983XU, TS-883XU-RP, TS-883XU
TVS-EC2480U/1680U/1580MU/1280U, TS-EC880U
TS-2477XU-RP, TS-1677XU-RP, TS-1277XU-RP, TS-977XU-RP, TS-977XU, TS-877XU-RP, TS-877XU
TVS-2472XU-RP, TVS-1672XU-RP, TVS-1272XU-RP, TVS-972XU-RP, TVS-972XU, TVS-872XU-RP, TVS-872XU

## Slide 33: Fibre Channel 支援的直立 / 桌上 NAS 型號
Intel & AMD NAS 支援 32Gb/s & 16Gb/s ATTO FC 介面卡
TS-2888X
TS-1685
TVS-1282, TVS-882, TVS-682
TS-1677X, TS-1277, TS-877, TS-677
TVS-872XT, TVS-672XT, TVS-472XT
TVS-863, TVS-663, TVS-463

## Slide 34: Fibre Channel 的建議機種
24 bay (24 x 3.5”)
Intel® Xeon® E-2136 6-core 3.3 GHz
Max 64GB RAM
16 bay (16 x 3.5”)
Intel® Xeon® E5-2630 v4 10-core 2.2 GHz
Max 256GB RAM
12 bay (8 x 3.5” + 4. 2.5”)
AMD Ryzen 7 8-core 3.0GHz
Max 64GB RAM
FC 16Gb
TS-1277
FC 32Gb
TS-2483XU
FC 32Gb
TDS-16489U R2

## Slide 35: 價格親民 操作簡單 設定彈性
QNAP NAS
X
ATTO CelerityTM
FC 擴充卡
光纖通道儲存網路
最佳解決方案

## Slide 36
©2019著作權為威聯通科技股份有限公司所有。威聯通科技並保留所有權利。威聯通科技股份有限公司所使用或註冊之商標或標章。檔案中所提及之產品及公司名稱可能為其他公司所有之商標 。