## Slide 1
USB 技術與普及性
TL USB JBOD 硬體介紹
在 Windows 與 macOS 利用 QNAP JBOD Manager 軟體管理 JBOD 擴充設備
擴充 NAS 首選

## Slide 2
What if you run out of storage space
TL-D800C & TL-R1200C-RP USB JBOD overview
Use QNAP JBOD Manager utility on Windows/macOS/Ubuntu to manage JBOD enclosures
Expand NAS capacity
筆記型電腦
個人電腦
伺服器
QNAP TS-251D

## Slide 3: How to easily and economically expand storage capacity of the host?
Mac
PC
Server
QNAP TS-251D

## Slide 4: Pick your own interface based on performance & budget
Theoretical throughput
Interface
Popularity
96 Gb/s
40 Gb/s
5 Gb/s
3 Gb/s
USB 3.0/3.1 Gen1
USB 3.1/3.2 Gen2
USB 3.2 Gen2 x2
Thunderbolt 3
SAS 12Gb/s
eSATA
6 Gb/s
10 Gb/s
20 Gb/s

## Slide 5: A TL USB JBOD enclosure can simplify many things
Consolidate multiple external storage devices into one unit.
Just need a USB port to connect.
Does not take multiple power outlets

## Slide 6: All-new USB 3.1 Gen2 TL JBOD enclosures
UX-500P
UX-800P
UX-800U-RP
UX-1200U-RP
USB 3.0 UX enclosures
High speed 10Gbps
USB 3.1 Gen2 TL series JBOD enclosures
TL-D800C
TL-R1200C-RP
Twice the speed
Supported by NAS QTS 4.4.2 or later
Type-C design to support either a Type-A or Type-C host
For NAS QTS, Windows, macOS and Ubuntu

## Slide 7: TL-D800C front view
Two keys supplied
Status indicators
Drive status indicators
Lockable drive trays
System
USB link
Fan error

## Slide 8: TL-D800C HDD/SSD installation
2.5-inch HDD / SSD
3.5-inch HDD
Use screws during transportation
Tool-less 3.5” HDD installation

## Slide 9: TL-D800C rear view
USB 3.1 Gen2
10Gbps
Type-C port
Fan speed
(Auto, high, med, low)
Audio alert
(On, off)
USB cable clip mounting hole
AC100-240V power input
Power switch
1M USB 3.1 Gen2 Type-C to Type-A cable supplied

## Slide 10: TL-D1200C-RP front view
System status
USB link
Fan error
Status LED indicator
Drive status LED indicator
Optional RAIL-B02 rail kit

## Slide 11: TL-R1200C-RP HDD/SSD installation
21
2
1
2
1
2.5-inch HDD / SSD
3.5-inch HDD

## Slide 12: TL-R1200C-RP rear view
待換實體
Redundant power supply
2 x 250W
USB cable clip mounting hole
Audio alert
(On, Off)
USB 3.1 Gen2
10Gbps Type-C port
Power switch
Fan speed
(Auto, high, med, low)
1M USB 3.1 Gen2 Type-C to Type-A cable supplied

## Slide 13: How to install the USB cable clip
21

## Slide 14: TL-D800C USB JBOD architecture
NAS, Windows, Mac, or Ubuntu that support USB 3.1 Gen2 or Gen1
(USB 2.0 is not supported)
Type-C
10Gbps
USB 3.1 Gen2 10Gbps Hub
10Gbps
10Gbps
USB 3.1 Gen2 10Gbps Hub
USB 3.1 Gen2 10Gbps Hub
6Gbps
6Gbps
6Gbps
6Gbps
HDD/SSD 1
USB 3.1 Gen2 10Gbps to SATA 6Gb/s
HDD/SSD 3
HDD/SSD 4
6Gbps
6Gbps
6Gbps
6Gbps
HDD/SSD 5
HDD/SSD 6
HDD/SSD 7
HDD/SSD 8
HDD/SSD 2
USB 3.1 Gen2 10Gbps to SATA 6Gb/s
USB 3.1 Gen2 10Gbps to SATA 6Gb/s
USB 3.1 Gen2 10Gbps to SATA 6Gb/s
USB 3.1 Gen2 10Gbps to SATA 6Gb/s
USB 3.1 Gen2 10Gbps to SATA 6Gb/s
USB 3.1 Gen2 10Gbps to SATA 6Gb/s
USB 3.1 Gen2 10Gbps to SATA 6Gb/s
10Gbps
10Gbps
10Gbps
10Gbps
10Gbps
10Gbps
10Gbps
10Gbps

## Slide 15: TL-R1200C-RP USB JBOD architecture
Type-C
10Gbps
USB 3.1 Gen2 10Gbps Hub
10Gbps
10Gbps
USB 3.1 Gen2 10Gbps Hub
USB 3.1 Gen2 10Gbps Hub
6Gbps
6Gbps
6Gbps
6Gbps
HDD/SSD 1
USB 3.1 Gen2 10Gbps to SATA 6Gb/s
HDD/SSD 3
HDD/SSD 4
6Gbps
6Gbps
6Gbps
6Gbps
HDD/SSD 5
HDD/SSD 6
HDD/SSD 7
HDD/SSD 8
HDD/SSD 2
USB 3.1 Gen2 10Gbps to SATA 6Gb/s
USB 3.1 Gen2 10Gbps to SATA 6Gb/s
USB 3.1 Gen2 10Gbps to SATA 6Gb/s
USB 3.1 Gen2 10Gbps to SATA 6Gb/s
USB 3.1 Gen2 10Gbps to SATA 6Gb/s
USB 3.1 Gen2 10Gbps to SATA 6Gb/s
USB 3.1 Gen2 10Gbps to SATA 6Gb/s
10Gbps
10Gbps
10Gbps
10Gbps
10Gbps
10Gbps
10Gbps
10Gbps
10Gbps
USB 3.1 Gen2 10Gbps Hub
6Gbps
6Gbps
6Gbps
6Gbps
HDD/SSD 9
HDD/SSD 10
HDD/SSD 11
HDD/SSD 12
USB 3.1 Gen2 10Gbps to SATA 6Gb/s
USB 3.1 Gen2 10Gbps to SATA 6Gb/s
USB 3.1 Gen2 10Gbps to SATA 6Gb/s
USB 3.1 Gen2 10Gbps to SATA 6Gb/s
10Gbps
10Gbps
10Gbps
10Gbps
NAS, Windows, Mac, or Ubuntu that support USB 3.1 Gen2 or Gen1
(USB 2.0 is not supported)

## Slide 16: Support more OS platforms than UX-500P/ UX-800P/UX-800U-RP/UX-1200U-RP enclosures
Mainstream operating systems
  Windows / macOS / Ubuntu users can use QNAP JBOD Manager to manage JBOD units
  Expand NAS capacity with QTS & QTS hero OS
Follow these steps to connect or disconnect the JBOD enclosure.

## Slide 17: Build a software RAID 0/1/5 volume with native Windows utility
https://support.microsoft.com/zh-tw/help/12438/windows-10-storage-spaces
Create a new pool and storage space in Windows
Resiliency type including [Simple]、[Two-way mirror]、[Three-way mirror] and [Parity]

## Slide 18: Build a software RAID 0/1 volume with native macOS Disk utility
In「Disk Utility」App , choose「File」>「RAID Assistant...」
https://support.apple.com/zh-tw/guide/disk-utility/dskua23150fd/mac

## Slide 19: Build a RAID 0/1/5 volume with a third-party application - SoftRAID
https://www.softraid.com/
https://www.softraid.com/

## Slide 20: Create a RAID 0/1/5 pool with Linux
https://www.digitalocean.com/community/tutorials/how-to-create-raid-arrays-with-mdadm-on-ubuntu-18-04
Install mdadm via terminal
sudo apt-get install –y mdadm
Build RAID 5 with mdadm
sudo mdadm --create --verbose /dev/md0 --level=5 --raid-devices=3 /dev/sda /dev/sdb /dev/sdc
Create & mount RAID pool
sudo mkfs.ext4 -F /dev/md0
sudo mkdir -p /mnt/md0
sudo mount /dev/md0 /mnt/md0
Please DO NOT unplug the USB cable while RAID space is connected & mounted, which may cause unexpected data loss or trigger RAID degrade.

## Slide 21: When your device could not recognize all drives or insufficient resources occurred
Windows/Mac/Linux
QNAP NAS
Follow the QNAP Expansion compatibility to check the maximum number of supported JBOD units.
USB endpoints
A host computer’s USB 3.0/3.1/3.2 (xHCI) controller usually has the maximum number of supported USB endpoints (normally 64~128 USB endpoints). When a USB device is connected to a host, depending on the device, a number of USB endpoints may be consumed. Therefore, when a host has multiple USB devices connected, the issue of insufficient USB endpoint resource may occur, which in turn resulted in missing some devices.
Source: https://www.cambrionix.com/articles_support/endpoint-limitation-usb-hubs/
https://www.qnap.com/go/compatibility-expansion/

## Slide 22: Add dual USB 3.1 Gen2 ports to PC or NAS
QNAP USB 3.1 Gen2 expansion cards (P/N：USB-U31A2P01 & QXP-10G2U3A) are equipped with two USB type-A ports running USB 3.1 Gen2 speed for faster file transfer speed and more device compatibility.
PCIe Gen2 x2
2 x USB 3.1 Gen2 Type-A
Different brackets included for various computer and NAS models
BETTER PERFORMANCE
USB-U31A2P01
QXP-10G2U3A
PCIe Gen3 x2
Coming soon

## Slide 23: UASP protocol support for high performance
907
MB/s
Windows 10 Pro
Mac
Ubuntu
SW RAID 0
Read
Write
SW RAID 5
Read
Write
NAS
SW RAID 0
Read
Write
SW RAID 5
Read
Write
SW RAID 0
Read
Write
SW RAID 5
Read
Write
SW RAID 0
Read
Write
SW RAID 5
Read
Write
868
MB/s
992
MB/s
242
MB/s
626
MB/s
988
MB/s
1019
MB/s
912
MB/s
1017
MB/s
664
MB/s
1028
MB/s
949
MB/s
1028
MB/s
738
MB/s
Not natively supported by macOS
TL-D800C performance tests

## Slide 24
透過 QTS 儲存與快照總管
• TL 系列與 軟體 RAID 架構的優勢 • 內部與外接儲存模式 • 應用情境與比較表
DEMO
Performance & Device
TL-D800C
TL-R1200C-RP
Performance
Device
Test environment:
TL-R1200C-RP + 12 x 2.5” SSDs
Windows 10 with a TL-R1200C-RP and RAID 0

## Slide 25
USE THE USB JBOD
ON YOUR PC OR LAPTOP

## Slide 26: QNAP JBOD Manager
QNAP JBOD Manager could let you know the information and status of JBOD device and each disk.
Supported platforms and operating system:
Windows: Windows 8 (or newer), Server 2012 R2 (or newer)
Mac: macOS 10.13 & 10.14, (10.15 will coming soon)
Linux: Ubuntu 18.04

## Slide 27: Monitor the disk health
Quickly Explore
The color of the disk allows you to easily identify the disk status. Click it can get more detail like type, manufacturer, capacity...etc.
The tab of "Disk Information" will provide you the detail SMART info of each disk.
Detail Info

## Slide 28: Device Information and Health View
Detail information of each enclosure
Enclosure health
Bus type
PSU status (only for RP model)
System temperature
Fan speed

## Slide 29: Device Temperature Threshold
You can set up the temperature threshold from 55 to 69 degree C, when the temperature exceeds the threshold, the enclosure will alarm and the health status will change to red. (Warning)
You can also see that the fan speeds up automatically when encountering high temperatures. (FAN set Auto)

## Slide 30: Log history and Notification
Utility UI + desktop notification
Independent log, it record all events that occur in the TL JBOD, and allows to export events for analysis

## Slide 31
QNAP NAS TL USB 3.1 Gen2 JBOD
With QTS Storage & Snapshot manager

## Slide 32: Based on Software RAID, manage JBOD with QTS
Enclosure & QTS Disk related features:
Temperature warning
S.M.A.R.T test
Seagate Ironwolf IHM
Disk Scan
Disk Erase
Disk performance test
TL-D800C、TL-R1200C-RP JBOD can be monitored and managed in the storage and snapshot manager like the old USB JBOD. Without external RAID chip, compared with TR series, it supports more QTS local disk management features.

## Slide 33: QTS integrate customized enclosure management for TL
Monitor the FAN speed of TL-JBOD via NAS UI, and configure the threshold of temperature warning.
When SSD becomes more popular, the temperature management of the enclosure is more important than before.
Notes: Why? the lifetime of SSD will be affected by the operating temperature.

## Slide 34: One machine for two uses: internal expansion or external disk mode
開啟儲存與快照總管 > 進入儲存 / 快照
選擇建立 >
新儲存池或新磁碟區
選擇 TL 系列 JBOD 並指定
RAID 類型即完成建立
The storage is individual for each disk, it will show 8 independent external disks on UI.
RAID & Storage Pool
External Disk mode
All disks of TL-JBOD would be identified by Storage & Snapshot manager, then configure as a RAID of storage pool.

## Slide 35: Easily create storage space in QTS / QTS hero
Different than the TR series, TL-JBOD based on QNAP software RAID will support all local RAID operations, also supports RAID migration and RAID expansion. TL-R1200C can even be configured as RAID 50/60.
Storage & Snapshot manager > Storage / Snapshot
Create >
New Storage Pool
Select TL JBOD and
set up the RAID type
TL -JBOD cannot be configured as a RAID group with those internal disks from NAS.
In three steps, it will be changed the TL-JBOD from an external storage device to the expansion storage.

## Slide 36: Flexible Storage Expansion or as a backup space
TL USB JBOD can expand QNAP NAS storage capacity. It supports either the configurations of the storage pool, or the snapshots storage from volume and LUN.
Based on the structure of software RAID, TL JBOD units are more suitable for expansion devices than TR series.
應用情境
TL-D800C
TS-877
Be the Storage Expansion
Be the Snapshot Vault

## Slide 37: Use QNAP USB 3.1 Gen2 card connecting more JBOD
If you don't have the enough USB slot? (Virtualization station / HD station)
Add QNAP USB 3.1 Gen2 card, then supports two TL USB JBOD.
TL-D800C
TS-877
USB-U31A2P01
TL-R1200C-RP
TL USB JBOD need to establish a separate storage pool, and cannot be used to expand the original pool on NAS.

## Slide 38: TL USB JBOD feature comparison
功能 | QNAP TL USB JBOD | QNAP TR-002/004
連線類型 | USB 3.1 Gen2 | USB 3.1 Gen2/3.0
槽位數 | 8, 12 | 2, 4
分割區可使用系統 | QNAP QTS, Windows, Mac, Linux 等 | QNAP QTS, Windows, Mac, Linux 等
QTS 磁碟監控、建立儲存池 | 支援 | 支援
QTS 磁碟操作如壞軌掃描 | 支援 | 不支援
外接 RAID 保護 | 不支援 | 支援
RAID 遷移、替換磁碟 | 支援 | 不支援
適用情境 | 單一平台大量 儲存空間擴充 | 跨平台擴充與資料傳輸
 | QNAP TL USB JBOD | QNAP TR-002/004/004U
Connectivity | USB 3.1 Gen2 | TR-002: USB 3.1 Gen2 TR-004: USB 3.1 Gen1 TR-004U: USB 3.1 Gen1
Number of bays | TL-D800C: 8 TL-R1200C-RP: 12 | TR-002: 2 TR-004/TR-004U: 4
Supported O.S | QNAP QTS, Windows, Mac, Linux | QNAP QTS, Windows, Mac, Linux
Cerate QTS storage pool | Supported | Supported
QTS operation like disk scan | Supported | X
H/W RAID Protection | X | Supported
RAID level migration | Supported | X
Scenario | High capacity for expansion | Cross paltform / plug & play

## Slide 39: Extend the warranty for up to 5 years
For 2-year standard warranty
TL-D800C
Order P/N:
LIC-NAS-EXTW-GREEN-3Y
Available 2-Year or 3-Year Extended Warranty
For 3-year standard warranty
TL-R1200C-RP
Order P/N:
LIC-NAS-EXTW-ORANGE-2Y
Standard Warranty
Warranty service that comes in effect at the time of purchase.
Free repair and part replacement for products under normal use during warranty period. (Spare parts and consumables are excluded)
Extended Warranty (extra cost)
Extending your warranty, available within 270 days of the initial unit purchase.
Offers identical service to standard warranty.

## Slide 40: TL USB 3.1 Gen 2 JBOD series
QNAP NAS expansion
Flexible 2 usage modes (internal and external modes) with comprehensive QTS/QTS hero features
Free utility to monitor JBOD and disk status on Windows 、Mac、Ubuntu
QNAP JBOD Manager
8-bay TL-D800C
12-bay TL-R1200C-RP
USB 3.1 Gen2 TL JBOD
enclosures for NAS、 Windows、Mac、Ubuntu
Notes: 多一組QTS 儲存池的容量擴充 / 外接硬碟模式 左邊放平台icon